## Slide 1: Discussion on AI/ML for Mobility
3GPP TSG RAN Meeting #102 December 11-15, 2023
Agenda Item: 9.1.2.4
RP-233510
Sourced by: CEWiT, IIT-K, Tejas Networks

## Slide 2: AI/ML for Mobility - Summary
Type of mobility
L3-based mobility and L1/L2-triggered mobility (LTM) are both considered
HO optimization in Network side [/UE side], including
Candidate/target cell prediction in L3-based mobility, or, candidate/target beam(s) and cell(s) prediction in LTM
RRM measurement and event prediction, including
  Beam-level measurement prediction
  Cell-level measurement prediction, e.g., using intra-frequency measurement results to forecast the RRM measurement of inter-frequency/inter-RAT cells
  HO failure/RLF prediction
  Measurement events prediction
LCM framework and others
  The conclusions in Rel-18 AI/ML study should be used as baseline
  Other impacts are further studied

## Slide 3: Proposals
Study both L3 and LTM based mobility
LTM is crucial for fast handover
LTM already suffers with some ping-pong effect which can be optimized using AI/ML
Reuse the outcomes of Beam management Rel18 SI wherever possible
Model identification and switching
LCM
Signalling aspects and procedures