## Slide 1: NR coverage enhancements for Rel-19
China Telecom, China Unicom, Nokia, Nokia Shanghai Bell, ZTE, Ericsson, CATT, vivo, Spreadtrum, Apple, Panasonic, TCL
Dec. 2023
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
Agenda:9.1.1.9
RP-233560

## Slide 2: Background
  Based on the outcome of RAN #101, the following can be observed
  Many companies are supportive of Rel-19 coverage enhancements, including 7 operators from different regions.
  The potential scope is stable including the following 2 objectives:
    Multiple PRACH TX over different beams including beam selection for Msg3
    PUSCH repetition scheduled by DCI 0_0 with C-RNTI

## Slide 3: Multiple PRACH transmissions with different beams
  Justifications
  For a UE with beam correspondence, the UE knows the preferred UL Tx beam based on the DL Rx beam, then it can enjoy the repetition gain for quick access. However, for the UE without beam correspondence, the UE does not know the preferred UL Tx beam thus it may need to perform beam sweeping. Thus, multiple PRACH transmissions with different Tx beams could allow such UE to quickly do UL beam sweeping and access into the network.
  During the discussion in Rel-18, it can be observed that multiple PRACH transmissions with different Tx beams can enhance the coverage in some cases. Additional ~1~3dB gain can be achieved compared to multiple PRACH transmissions with the same beam.
  When multiple PRACH transmissions with different beams is enabled, beam indication for subsequent UL transmissions can be realized, e.g., beam indication for Msg.3 transmission, which will benefit the coverage of subsequent UL transmissions.
  PRACH transmissions with different beams
  For instance, if gNB identifies that this beam is the best UL beam for corresponding UE, it can indicate it to the UE to improve the performance of subsequent UL transmissions.

## Slide 4: Msg5 PUSCH repetition
  Justifications
  Msg5 PUSCH, which is scheduled by DCI format 0_0 with CRC scrambled by C-RNTI does NOT support repetition transmission yet.
  Based on the filed test, Msg5 PUSCH is the coverage bottleneck during the initial access. The main reason lies in Msg5 has a very large payload size, e.g., >100 Bytes which is larger than the typical Msg3 payload size. The situation would get worse when Msg3 repetition is implemented cause more UEs would access to the network while congested during Msg5 transmission.
    It is observed that the performance gap between Msg5 PUSCH transmission and Msg3 PUSCH transmission is large.
  Except for Msg5, similar coverage issue could be observed for PUSCH carrying UE capability reporting.
Simulation cases | Target SNR (dB) w/o power normalization | Target SNR (dB) w/ power normalization to one PRB
Msg3 without repetition | -7.31 | -4.3
Msg3 with 2 repetitions | -11.27 | -8.26
Msg3 with 4 repetitions | -13.67 | -10.66
Msg3 with 8 repetitions | -15.91 | -12.9
Msg5 with max 2 (re-)transmissions | -9.21 | 5.84
Msg5 with max 4 (re-)transmissions | -10.25 | 4.8
Msg5 with max 8 (re-)transmissions | -11.18 | 3.87
Tab. Performance for Msg3 and Msg5 at BLER = 0.1

## Slide 5: Proposals
  Proposal 2: The detailed objectives of Rel-19 coverage enhancements are as follows:
  Specify following PRACH coverage enhancements (RAN1, RAN2)
    Multiple PRACH transmissions with different Tx beams for 4-step RACH procedure.
    UL beam indication based on multiple PRACH transmissions with different Tx beam for Msg3.
    Note 1: The enhancements of PRACH are targeting for FR2, and can also apply to FR1 when applicable.
    Note 2: The enhancements of PRACH are targeting short PRACH formats, and can also apply to other formats when applicable.
    Note 3: The multiple PRACH are transmitted over ROs associated with the same SSB.
  Specify enhancements to support PUSCH repetition scheduled by DCI 0_0 with C-RNTI (RAN1, RAN2)
  Proposal 1: Include coverage enhancement as one of the RAN1-led projects in Rel-19.

## Slide 6: Thanks!