## Slide 1: Views on Rel-19 Ambient IoT
China Telecom
Dec, 2023
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
Agenda Item: 9.1.1.4
Document for: discussion
RP-233571

## Slide 2: Potential objectives
Option 1: Only 18-month SI in Rel-19. Option 2: 12-month SI + 6-month WI in Rel-19.
Several standards organizations (IEEE) are experimenting with potential passive IoT solutions, which will pose a threat
Existing communication methods such as Bluetooth and LoRa are expanding in the market
Current business needs are clear, especially in factories, logistics, etc
Therefore, a WI in Rel-19 will be better to accelerate the business progress
Proposal 1：Support to have a WI stage in Rel-19

## Slide 3: Potential objectives
transmit
receive
RFID design can be used as reference for device A/B, but hard to confirm a reference for device C target
Licensed FDD have better coverage performance and no need to consider slot conversion issue
In-band with simple deployment, guard-band with low NR interference and standalone whose spectrum is hard to find
Topology 1, simple and intuitive
Topology 2, complex with the additional relay
Topology 4, lower transmission power
Topology 3-1, complex structures
Topology 3-2, complex structures
A clear target for device A/B
The target for device C is unknown
In-band, guard-band or standard
U
U
U
U
U
U
D
D
D
S
U
D
Licensed FDD, no slot conversion issue
Proposal 2：Prioritize licensed FDD spectrum deployment
Proposal 3：Prioritize studying on device A and B first
Proposal 4：Further discussion is needed for spectrum
Topology 1 is the simplest scenario and closest to the target scenario deployment, which can be as a basis of research
Adding relay node requires a study of the relay system, which is slightly complex and can be considered as an enhancement
Coverage distance is not far enough due to lower power for Topology 4, which has little advantage compared with RFID
Adding an assisting node will increase network complexity, which should be low priority
Proposal 5：Prioritize topology 1 as the baseline

## Slide 4: Physical channel
Confirm the potential DL and UL waveform
LP-WUS design can be referred to as DL waveform
All “ON”continuous carrier can be considered as UL waveform
Confirm the channel design
PDCCH
PDSCH
SSB
PUSCH
PUCCH
……
IoT data channel
Only define a new data channel instead of legacy NR design
Proposal 6：LP-WUS design can be referred to as DL waveform design mechanism
Proposal 7：A new IoT data channel should be defined instead of utilizing legacy NR design
Define the new “Frame”
An unified IoT format
Information contained
Define the unified channel coding
Mainly consider CRC for DL
Consider channel coding for UL
Proposal 8：A new “Frame” structure should be defined
Proposal 9：Consider CRC coding for DL, and consider potential channel coding for UL

## Slide 5: Physical and higher layer
Confirm the synchronization and access method
Higher power and complexity for SSB measurement
Higher complexity for legacy NR random access
Design combined with frame structure
Design corresponding procedure combined with frame structure
Proposal 10：A new DL synchronization procedure should be considered
Proposal 11：A new UL random access procedure should be considered
Scheduler and “H-ARQ”
Define the specific scheduling content
Proposal 12：Consider corresponding higher layer design
Proposal 13：Consider corresponding “H-ARQ” like procedure for A-IoT
Corresponding signal bandwidth and subcarriers
Corresponding higher layer data package structure
Similar “H-ARQ” procedure like RFID can be considered

## Slide 6: Potential Scope and Objectives in Rel-19
Consider SI+WI procedure in Rel-19 A-IoT
Focus on specific deployment scenarios in Rel-19
  Prioritize FDD in the licensed spectrum
  Prioritize Topology 1 as a baseline
  Prioritize device A/B first in the Rel-19 stage
  Spectrum co-existence with legacy NR signal needs to be further discussed
Consider physical layer design on A-IoT
  Waveform, physical layer channel, channel coding and frame structure
  DL synchronization, UL random access, “H-ARQ” like procedure
Consider higher layer design on A-IoT
  Control plane functionalities, including scheduling content and corresponding mechanism
  User plane functionalities, including the content about the data channel and the data packet structure
Consider evaluation methods for A-IoT
  Evaluation methodology and assumptions
  Design target such as coverage range and power consumption

## Slide 7: Thank You!