## Slide 1: Views on Network Energy Saving for Rel-19
China Telecom
Dec, 2023
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, Dec 11 - 15, 2023
Agenda: 8.1.1.5
Document for: discussion
RP-233573

## Slide 2: Background
  Work in Rel-18 NES
    In Rel-18 NES SI, ~20 NES techniques in time/spatial/power/frequency domain are studied and evaluated with results drafted in TR 38.864
  In Rel-18 NES WI, only part of the studied techniques were included, and there are also leftovers for the techniques
  Based on the outcome of RAN#101 and summary from RAN chair, the following techniques can be considered as objectives for Rel-19 NES
    On-demand SSB/SIB1 transmission
    SIB1-less operation in multi-carrier scenario
    Adaptation of common signal/channel transmissions
    Further enhancement on Cell DTX/DRX

## Slide 3: Potential scopes for NES in Rel-19
  On-demand SSB
  On-demand SSB can both considered for for UEs in idle/inactive mode and UE in connected mode for Scell in CA scenario.
    The adaptation of SSB patterns can be considered to flexibly reduce the transmission of SSB for Scell in CA scenarios.
    The trigger signals/mechanism for on-demand SSB/SIB1 transmission for UEs in idle/inactive mode and in connected mode in Scell of CA should be considered.
  Proposal 1:
  Specify procedures and signaling method(s) to support on-demand SSB SCell operation for UEs in connected mode configured with inter-band/intra-band CA. [RAN1/2/3/4]
    Specify the adaptation of SSB patterns in time domain.
  Proposal 2:
  Specify procedures and signaling method(s) to support on-demand SSB SCell operation for UEs in idle/inactive mode. [RAN1/2/3/4]
    Specify the trigger signals/mechanism for on-demand SSB/SIB1 transmission.
  On-demand SIB1 transmission
  For UE in idle/inactive mode, similar to on-demand SSB, on-demand SIB1 can also be considered, where the signaling and mechanism should be specified.
  Proposal 3:
  Specify procedures and signaling method(s) to support on-demand SIB1 for UEs in idle/inactive mode [RAN1/2/3]
    Specify the trigger signals/mechanism with WUS using existing signal/channel.

## Slide 4: Potential schemes for NES in Rel-19
  SIB1-less operation in multi-carrier scenario
  For multi-carrier scenario, the SIB1 of non-anchor carrier can be carried on the anchor carrier, so that the transmission SIB1 on non-anchor can omitted and more energy can be saved.
  Proposal 4:
  Specify SIB1-less operation for non-anchor NES carrier for UEs in idle/inactive mode [RAN2/1/3]
    Specify the mechanism for UE to access the non-anchor carrier with the SIB1 carried on the anchor carrier
  Further enhancement of Cell DTX/DRX
  The Cell DTX/DRX has been introduced in Rel-18 but still have potential to be further specified due to the limited time. Cell DTX/DRX can be more practical and save more energy if the mechanism can be adopted in more scenarios and more signals/channels can be stopped transmitting/receiving during the non-active period.
  Proposal 5:
  Further specify the enhancement of Cell DTX/DRX
    Specify support of Cell DTX/DRX for UEs in idle/inactive modes.[RAN2/1/3]
    Specify turning off the transmissions of more channels/signals such as TRS.[RAN1/2/3]
    Specify the trigger of Cell DTX/DRX based on UE indication.[RAN1/2/3]

## Slide 5: Thanks!