## Slide 1
Views on Rel-18 Further NR mobility enhancements
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
Agenda item: 9.3.2.1
TDoc number: RP-233630

## Slide 2: Summary of Rel-18 Further NR mobility enhancements
Overall progress of Rel-18 WI on Further NR mobility enhancements (RP-231475)
  Objective 1~Objective 6 are considered as completed from RAN1/2/3/4 perspective.
  Objective 7 is considered as not completed at least from RAN2 perspective because RAN4 hasn’t completed the work.
Solutions discussed in RAN4 for objective 7: (using RAN2 terminologies)
  Enhanced measurements: existing measurements (e.g. R16 EMR) + verification (i.e. within the last [X] sec before msg1 transmission for RRC resume/setup request)
  Additional measurements: R16 EMR (FFS if cell re-selection measurements is also covered or not) + additional measurements during RRC resume/setup procedure. The measurement results obtained during RRC resume/setup procedure are always considered as valid, extra verification is not needed.
Objective 7: To study and specify how to reuse the IDLE/INACTIVE mode measurement results which are to be reported during and/or after RRC connection setup/resume in order to improve SCell/SCG setup delay [RAN4, RAN2], including: Availability and validation of the IDLE/INACTIVE mode measurement results to be reported [RAN4]; and Definition of corresponding RRM requirements [RAN4]; and If necessary based on RAN4 outcome, definition of corresponding signalling support [RAN2]. Note 6: RAN4 will coordinate in due course with RAN2 to start the work. Note 7: R4-2220415 serves as baseline for future work in RAN4 Note 8: With exception of the above scenarios, enhancements on IDLE/INACTIVE mode measurements and on UE behavior in IDLE/INACTIVE mode are not in scope.

## Slide 3: Consideration on Rel-18 Further NR mobility enhancements
Situation in RAN4 and RAN2 for objective 7:
  RAN4 has defined RRM delay and accuracy requirements for Enhanced measurements, however, no delay requirements has been defined so far for Additional measurements.
  RAN2 discussion mainly focused on Enhanced measurements because the RAN2 impact caused by Additional measurements is unclear.
  Our consideration on objective 7 and the completion of the WI:
  Additional measurements should be dropped from the Rel-18 WI considering the lack of UE requirements and complexity in UE implementation.
  Additional measurements are also not considered as part of the discussion on Rel-19 mobility enhancements.
  To continue RAN2/RAN4 work to finalize Enhanced measurements in Rel-18, the WI is extended to Q1 2024.
  Proposal : Extend Rel-18 Further NR mobility enhancement WI to Q1 2024, revise the WID to only support Enhanced measurements in Objective 7. Additional measurements (e.g. measurement performed during RRC resume/setup procedure) are not considered in either Rel-18 or Rel-19.

## Slide 4: Thank You！