## Slide 1: Discussion on Rel-19 Mobility enhancements (Phase 4)
3GPP TSG RAN #102 RP-233652
Edinburgh, UK, 11th – 15th December 2023
Agenda Item: 9.1.2.1
Source: Intel Corporation
Document for: Discussion

## Slide 2: R19 Mobility enhancements: Inter-CU LTM
Inter-CU LTM
  R18 LTM is restricted to intra-CU
  LTM cannot be used for UEs at the CU border
Scenarios for Inter-CU LTM
  MN only scenario (no DC) is simplest and should be highest priority
  Inter-CU LTM for UEs with DC configuration should be considered
    Releasing DC during inter-CU LTM will impact UE performance
  Inter-CU for SN should also be considered
    For UEs configured with DC, inter-gNB HO for SN is likely more frequent than inter-gNB HO for MN
    For gNBs without CU-DU split, inter-CU-LTM will be a frequent occurrence
Proposed objective:
Specify support for inter-CU Layer 2 Mobility (LTM) [RAN2]:
  Prioritize the case when CU is acting as MN when DC is not configured
    Additionally support:
      when DC is configured
      CU is acting SN

## Slide 3: R19 Mobility enhancements: Measurement enhancements
Event triggered measurement reporting
  Event triggered measurement reporting has been supported in L3 HO over many generations
    Provides significant reduction in measurement reporting signalling
  This optimisation for measurement reporting is not supported in LTM
  Interaction with RAN1 MIMO:
    While there may be some possible interaction, given that RAN1 MIMO details are also to be worked out, RAN2 can start this work after initial progress of RAN1 work
CSI-RS measurements for LTM
  Currently LTM is only supported for SSB based measurements
  CSI-RS measurement for candidate cells and CSI-RS based LTM can enable more accurate L1 operation based on refined CSI-RS beam rather than wider SSB beams; should also provide latency advantages from reduced beam refinement
Proposed objectives:
Measurements related enhancements for purpose of supporting LTM:
  Specify event triggered L1 measurement reporting for triggering LTM [RAN2]
    RAN2 to wait until June ‘24 to review RAN1 progress to avoid potential overlap work
  Specify support for CSI-RS measurements for LTM procedures and enable CSI-RS based beam management and/or other physical layer operations on candidate cells before LTM [RAN1]

## Slide 4: Rel-19 mobility enhancements: LTM and L3 HO optimisations
Other objectives
  LTM for Rel-18 does not support CHO like operation
    CHO is considered a useful feature for L3 mobility for HO performance improvement
  LTM/SCPAC supports multiple cell configurations between which UE can perform sequential cell switch without requiring new RRC reconfiguration message
    L3 HO does not allow this optimised sequential HO
  L3 HO does not support early TA for RACHless HO
    Early TA is supported by LTM can allow faster HO, reduce interruption and HO failure
Proposed objectives:
Support of LTM conditional mobility (including set of candidate cells, UE evaluated mobility conditions) [RAN2]
Support L3 HO multiple sequential HOs without need for RRC reconfiguration along with short mobility interruption time using RACHless/Early TA [RAN2]

## Slide 5: Summary of proposed objectives
Specify support for inter-CU Layer 2 Mobility (LTM) [RAN2]:
  Prioritize the case when CU is acting as MN when DC is not configured
    Additionally support:
      when DC is configured
      CU is acting SN
Measurements related enhancements for purpose of supporting LTM:
  Specify event triggered L1 measurement reporting for triggering LTM [RAN2]
    RAN2 to wait until June ‘24 to review RAN1 progress to avoid potential overlap work
  Specify support for CSI-RS measurements for LTM procedures and enable CSI-RS based beam management and/or other physical layer operations on candidate cells before LTM [RAN1]
Support of LTM conditional mobility (including set of candidate cells, UE evaluated mobility conditions) [RAN2]
Support L3 HO multiple sequential HOs without need for RRC reconfiguration along with short mobility interruption time using RACHless/Early TA [RAN2]

## Slide 7: For Info: Slide from RP-232745

## Slide 8: Mobility Enhancements WI
References: RWS-230488, RP-231540, RP-232618
Potential objectives:
  Specify support for inter-CU Layer 2 Mobility (LTM)
    Prioritize the case when CU is acting as MN when DC is not configured
    Whether to additionally support e.g. when CU is acting SN? (focus on practical deployments)
      In this case, whether it is supported for EN-DC and/or NR-DC only?
  Measurements related enhancements for purpose of supporting LTM:
    Specify event triggered L1 measurement reporting for triggering LTM  depending on the detailed discussion in RAN#102, resolve how to avoid overlapping with similar objective in MIMO WI
    Specify support for CSI-RS measurements for LTM procedures and enable CSI-RS based beam management and/or other physical layer operations on candidate cells before LTM
  Support of conditional mobility (including set of candidate cells, UE evaluated mobility conditions, ability for UE to perform subsequent mobility procedures without need for RRC configuration) along with short mobility interruption time (similar to that achievable with LTM).
    Next Step question to consider the most appropriate approach to achieve this aim. For example, by specifying conditional triggering of LTM, or specifying support of Early TA or RACHless (as defined for LTM) to be used as part of layer 3 CHO, or possibly other approaches. If this questions cannot be concluded during the Rel-19 scoping discussion then it may be possible to start with a RAN2 study phase.
  Anything else (e.g., RAN4 related)?