## Slide 1: Discussion on Rel-19 XR enhancements
3GPP TSG RAN #102 RP-233653
Edinburgh, UK, December 11 – 15, 2023
Agenda Item: 9.1.2.2
Source: Intel Corporation
Document for: Discussion

## Slide 2: XR Traffic with Multi-modal Data
Motivation:
SA2 introduced in R18 the concept of Multi-modal data referring to data from XR App. that generates multiple types of traffic flows (e.g., video/audio stream, as well as sensor data for more immersive experience)
Proposed WI Objective:
Enable RAN/UE enhancements targeting XR traffic with Multi-modal data (i.e., different/multiple data streams of one XR application) including the study of:
  Synchronized or coordinated transmissions
  Multiple C-DRX configurations active simultaneously
  UE assistance/feedback information
Note 1: Coordination with SA2/SA4 required
Note 2: Focus on intra-UE scenario

## Slide 3: Measurement Gap for XR
Motivation:
To minimize impact of measurements to XR traffic while also reducing the scheduling restrictions (e.g., to reduce delay and discard of packets).
  This enhancement is not XR specific. RAN4 Rel-19 material (RP-233687) also includes measurement gap related enhancement for time-sensitive or reliability-sensitive types of services (URLLC) which could apply to XR.
Proposed WI Objective:
Measurement gap enhancements to mitigate the impact on the XR traffic
    Note-3: This objective can also be addressed in the RAN4 led WI on measurement gap enhancements

## Slide 4: SN Gap for XR
Motivation:
Rel-18 discard enhancements may create gaps on PDCP SN that will delay delivery of the packets to the upper layers due to the reordering, which is not ideal for XR services.
Proposed WI Objective:
Define a mechanism for transmitter to inform the receiver of SN gap (or missing SNs) in PDCP

## Slide 5: Delay Aware Scheduling
Potential R19 objective proposed:
Delay aware / Delay adaptive (remaining time) scheduling
Considerations to include:
UL direction should be the focus
Study phase is preferable considering
  The possibility of having multiple high priority traffic/DRBs simultaneously that can starve XR traffic
  Existing solutions, such as, AS reflective QoS mechanism may be able to address this requirement as it can temporarily and dynamically change the LCP handling for a QoS flow by directing that flow to a different DRB
  New solutions can be studied – e.g., to enhance LCP mechanism to consider delay, e.g., remaining time
    Potential complexity of changes to LCP mechanism
Updated WI Objective, if adopted:
Study and, if agreed, specify delay aware / delay adaptive (remaining time) scheduling enhancements in UL considering the following:
  For the scenario where multiple high priority traffic/DRBs simultaneously that can starve XR traffic
  Potential complexity of changes to LCP mechanism should be considered
  Solution should be evaluated against existing solutions, such as, AS reflective QoS mechanism

## Slide 6: RLC Optimisation
Motivation:
RLC AM can introduce additional delay when a packet is subject to re-transmission
  This can result in additional delay for all subsequent packets due to re-ordering
  Makes RLC-AM unsuitable for delay sensitive traffic
  One has to rely on RLC-UM that does not offer sufficient reliability
Study enhancements to RLC-AM to allow its use for delay sensitive traffic
Proposed WI Objective:
Study and, if agreed, specify means to enhance NR RLC operation to improve the performance of data transfer within small packet delay budgets

## Slide 7: Summary of the Proposed WI Objectives on Rel-19 XR
Enable RAN/UE enhancements targeting XR traffic with Multi-modal data (i.e., different/multiple data streams of one XR application) including the study of:
  Synchronized or coordinated transmissions
  Multiple C-DRX configurations active simultaneously
  UE assistance/feedback information
  Note 1: Coordination with SA2/SA4 required
  Note 2: Focus on intra-UE scenario
Measurement gap enhancements to mitigate the impact on the XR traffic
    Note 3: This objective can also be addressed in the RAN4 led WI on measurement gap enhancements
Define a mechanism for transmitter to inform the receiver of SN gap (or missing SNs) in PDCP
Study and, if agreed, specify delay aware / delay adaptive (remaining time) scheduling enhancements in UL considering the following:
  For the scenario where multiple high priority traffic/DRBs simultaneously that can starve XR traffic
  Potential complexity of changes to LCP mechanism should be considered
  Solution should be evaluated against existing solutions, such as, AS reflective QoS mechanism
Study and, if agreed, specify means to enhance NR RLC operation to improve the performance of data transfer within small packet delay budgets