## Slide 1: Discussion on Rel-19 AIML Mobility
3GPP TSG RAN #102 RP-233654
Edinburgh, UK, December 11 – 15, 2023
Agenda Item: 9.1.2.4
Source: Intel Corporation
Document for: Discussion

## Slide 2: Guideline from RAN Chair
RAN Chair has provided some guidance for further discussion on the scoping of the objective of the study [RP-232745].
Following are suggested baseline for further discussions
  HO optimization in NW-side, including candidate/target cell prediction in L3-based mobility, or, candidate/target beam(s) and cell(s) prediction in LTM
  RRM measurement and event prediction, including
    HO failure/RLF prediction
    Measurement events prediction
  Possible down-scoping for other aspects in RP-232622.

## Slide 3: Summary of Rel-18 AI/ML air interface SI (RAN2)
3GPP has studied the support of AI/ML framework in Rel-18 including
  Data Collection for model training, inference and management
  Functionality mapping between network entity and AI/ML functions
Requirements of data collection framework for NW-side model and UE-side model are identified. Furthermore, for NW-side model, RRM measurement and MDT framework are identified to be further enhanced to support data collection for AI/ML air interface use cases.
RAN specification impacts are identified for model transfer/delivery methods
The study outcome of LCM, data collection and model transfer/delivery methods can be used to support new use cases.

## Slide 4: Motivation
Existing L3 HO mechanism has been proven in wireless system over generations. Furthermore, Rel-16 introduces CHO, which can help to provide HO command in advance when the channel link is still good.
With the emergence of AI/ML techniques, study whether and how much performance gain it will bring on mobility especially considering challenges in HO, e.g.
  Power consumption/signaling overhead due to high quantity of measurements and reporting of neighboring cells
  Increased handover failure/ping-pong ratio/service interruption in very dense/high-frequency deployments
  Early handover command provided to UE in a more stable radio link condition than legacy HO
Fig. AI/ML based Mobility

## Slide 5: Potential Scope & Objectives
General framework
  The conclusions in Rel-18 AI/ML study for LCM, data collection, model transfer/delivery (if needed) are used as baseline for AI/ML mobility
    Avoid overlapping discussion with AI/ML air interface SI/WI on LCM, data collection, model transfer/delivery.
Performance evaluation between AI/ML-based HO and existing HO mechanism
  Optimization target and performance evaluation metrics may include:
    HO failure
    Ping-pong
    Measurement and report reduction
    Duration of stay in the candidate/target cell
Type of mobility
  L3-based mobility and L1/L2-triggered mobility (LTM)
RRM optimization at UE-side, including
  Event prediction (e.g. Measurement events prediction, HO failure/RLF prediction, etc)
HO optimization in Network side:
  Candidate/target cell prediction in L3-based mobility
  Candidate/target beam(s) and cell(s) prediction in LTM