## Slide 1: Proposal for RAN4 package (BS and UE RF)
3GPP TSG RAN Meeting #102 RP-233747
Edinburgh, Scotland, December 11-15, 2023
Agenda Item: 9.1.4.2
Source: Ericsson
Document for: Discussion

## Slide 2: Overall priorities
UE RF
  Improve FR1 MIMO performance (return on AAS investment)
  Improve UL coverage for FR2
  Enhance CA both in terms of power and reliability
BS RF
  Incorporate EIRP mask methodology into the RAN4 specifications (for now and future needs)
  Enable 1-O OTA testing with reasonable complexity in all bands
  Simplify cumbersome BS specifications needing lots of CRs

## Slide 3: UE RF: improvement of MIMO performance for FR1 and coverage for FR2
Improve MIMO FR1 performance: SRS measurements in the field show large variability due to uncertain SRS power and different interpretation of the specifications
Improved DL CSI estimation: SRS output power reporting for DL CSI estimation:
  Report the output power per SRS resource in a new MAC-CE based on type 3 PH and maximum output power or similar, for 2/4/8 Rx
UL (spherical) coverage for FR2 PC3 improved for all MCS in all FR2 bands for improved performance
Improved coverage for FR2: a new HPUE power class PC3bis for handheld UEs
  New power class with min-peak EIRP of ≈ 24dBm (28 GHz), and improved spherical coverage by ≈ 5 dB assuming 2 panels
Ensure UL-MIMO performance in FR1 for coherent transmissions for FWA/CPE applications in FR1
Minimum requirements for 4Tx/8Tx with coherent transmissions for FWA/CPE
  existing RAN requirements based on two-port/connector transmissions (Rel-15)

## Slide 4: UE RF: enhancement of CA performance
HPUE for CA
Intra-band UL CA
  intra-band UL CA requirements with power capability per-CC lower than the per-band (and per-BC) capability
  without adding further ambiguities to power-class reporting
Improved CA performance in the field for FR1 and FR2
UL CA/DC performance: configurable UE-specific relative power limits for consistent UE behavior
  Avoidance of Scell dropping in FR1/FR2: make RAN5 test mode (supported for FR2 from Rel-16) available also to the NW
  Can also be also be used for HPUE intra-band UL CA with per-CC power capability < per-band power class, see annex.
  Modification of limits without RRC reconfiguration for faster adaptation, e.g. MAC-CE

## Slide 5: BS RF proposals
EIRP mask
  Core requirement on EIRP mask
  Develop conformance methodology and specification. This is useful both for band under question and future masks in other bands
FR1 OTA improvements
  Simplification of some resource consuming measurements such as TX IM and out-of-band blocking
  [Examine candidates for OTA co-location method suitable for the upper part of the FR1 range]
  Improve description of TRP test methods
BS specification simplification
  E.g. simplify the specification of co-existence and co-location requirements to avoid large tables and the need for large numbers of CRs

## Slide 7: Annex UE RF proposals: UE-specific limits
For ‘standard’ UL CA requirements the per-band power class is supported per CC (for UL-MIMO scaled between PUSCH ports), UE-specific limits prevent the UE become power limited as implemented for the RAN5 test mode
  the test mode supported by UL CA capable FR2 UEs from Rel-16 (UPLF)
Can also be used for HPUE and intra-band CA when the per-CC power cabability (e.g. 23 or 26 dBm PA) is less than the per-band PC (e.g. 29 dBm), limits configured according to UE capability for the BC
  no need for new power-class UE capabilities