## Slide 1: Topology Enhancements in Rel-19
RP-233786
3GPP TSG RAN #102 Edinburgh, UK, 11-15 December 2023
Source: Ericsson, Deutsche Telekom, China Unicom Agenda Item: 9.1.3.3 Document for: Discussion, Decision

## Slide 2: Summary
Status of discussions after RAN #101 (RP-232625)
Proposal from RAN Chair (RP-232745)
Considerations on mIAB
Considerations on femtos
Conclusions, proposals

## Slide 3: Status of Discussions After RAN #101 (RP-232625) (1)
“List of objectives for further discussion, refinement, and downscoping” (from summary of offline discussion RP-232625):
  WAB/mIAB
    Study enhancements for the support of WAB including (RAN3-led, RAN2):
      Study impact of gNB mobility within a stationary RAN and in proximity to other mobile gNBs:
        Identify the issues of dynamic inter-gNB neighbor relations resulting from gNB mobility, e.g., ANR, inter-gNB HO/DC and SON.
        Identify RAN-related issues when collocating a UPF with the gNB for MEC, local services and/or local inter-UE communications.
        Identify necessary inter-gNB- and gNB-to-CN signaling to address these issues.
      Study the signaling enhancements for the authorization of WAB nodes.
      Study signaling enhancements to extend the IAB resource multiplexing framework to WAB, as necessary.
      Study enhancements to QoS support on WAB backhaul, as necessary.
    Study enhancements for the support of single-donor IAB topology, including (RAN2-led, RAN3):
      Study enhancements to the robustness of multi-hop routing within the IAB topology in presence of local IAB-node mobility.
    Note: Access link for WAB backhaul can be TN or NTN.

## Slide 4: Status of Discussions After RAN #101 (RP-232625) (2)
“List of objectives for further discussion, refinement, and downscoping” (from summary of offline discussion RP-232625):
  5G Femto
    Study the overall RAN architecture and required functional and procedural impacts for supporting 5G Femto deployments.
    Study how to define the 5G access control mechanism by (re-)using the existing CAG functionality and identify needed enhancements (if any).
    Study how to enable access to local services from the 5G Femto via collocated local UPF.
    Note: The study involves a gap analysis of existing 5G functionality with HomeNB functionality.
  Enhanced VMR
    Moderator: Based on the proponent comments, local service breakout and local switch is already considered in WAB/mIAB. Support of multiple access technologies may not be as acceptable to companies. It was noted that the list is too generic and that there was no time for further discussion on this topic. Proponents are encouraged to provide additional details in December.

## Slide 5: Proposal from RAN Chair (RP-232745)
6-month SI followed by 12-month WI
  ~2 TUs for for SI
  ~1.5 TU for WI

## Slide 6: Considerations on mIAB
Variety of potential justifications for WAB/mIAB (RP-232625):
  UEs onboard aircrafts/cruise ships/helicopters, vehicles in remote areas, public safety, disaster recovery, deep urban coverage, MEC, local services, inter-UE communications, aerial coverage, …
Current IAB “toolbox” is very powerful
  We have been building IAB for 3 releases, even adding mobility
  (Side effect: Network Controlled Repeaters)
Any functionality really missing from IAB? I.e., any missing functionality foreseen from real deployments?
  Opportunity to let ecosystem catch up; any missing features could be handled as TEI
Proposal 1: No further work on mIAB until missing features, if any, preventing the support of credible use-cases (e.g. emergency/disaster) are clearly identified
  Rationale: current objectives assume gaps have already been identified and agreed – Chair’s proposal to allocate TUs now for SI+WI seems to reflect this – but that may not be the case

## Slide 7: Considerations on femtos (1)
Rel-8 3G/4G | Rel-18 5G
“Macro network is monolithic; RAN architecture is not flexible” | Split NG-RAN (CU-DU; CP-UP)
“CN cannot cope with femto traffic; concentration/aggregation stage is needed” | - CN, RAN are virtualized - No hard limit on n. of CP connections / cells - CU-DU split may be leveraged for CP concentration if needed
Indoor coverage problematic with early UMTS bands | Many different bands
No tools to extend/tailor coverage | - IAB - NCR - MIMO - …
No support for closed user groups | CAG, NPN

## Slide 8: Considerations on femtos (2)
Introduced in Rel-9, fully specified in Rel-12
  Specific architecture; dedicated GW, security GW, management system
  Closed/open/hybrid access and mobility added over several releases
    Membership verification in CN
  Dedicated air interface additions
  Limited functionality
    e.g. no S1-flex, X2 mobility limitations, …
  Specific local breakout (LIPA) added later
Given the apparent differences in deployment, feature set and architecture, migration of this architecture from 4G to 5G appears problematic
Source | Target | Notes
eNB or any HeNB | open access HeNB | 
eNB, or any HeNB | hybrid access HeNB | 
hybrid access HeNB or closed access HeNB | closed access HeNB | Only applies for same CSG ID and PLMN, and if the UE is a member of the CSG cell.
Any HeNB | eNB | 
X2 handover support (Rel-12)
3GPP TS 36.300

## Slide 9: Considerations on femtos (3)
Femtos in NG-RAN are supported
  Local Area BS class applicable to femtos (R4-2220263, agreed 11/2022)
    Operators may deploy femtos accordingly
  Need to identify missing parts (if any) first, in current NG-RAN:
    Gap analysis as currently mentioned in the draft SI objectives, should help to avoid duplicating existing functionality
Proposal 2: Pragmatic approach for femtos: start from operator requirements and consider available NG-RAN toolbox rather than pre-5G solutions

## Slide 10: Considerations on Local Breakout
4 “flavors” of local breakout were available in E-UTRAN:
  LIPA (only works for HeNBs)
  SIPTO@LN with co-located GW (also ported to UTRAN)
  SIPTO with stand-alone GW
  SIPTO above RAN (CN functionality)
Current NG-RAN, 5GC functionality allow to relocate UPF anywhere on the fly (supported by in-band signaling)
Proposal 3: For local breakout, identify gaps (if any) in available functionality; if further specification work is needed, work on a common solution to avoid multiple “flavors”

## Slide 11: Conclusions, Proposals
Consider the current stage in NG-RAN architecture lifecycle (i.e., fairly late)
Proposal 1: No further work on IAB until missing features, if any, preventing the support of credible use-cases (e.g. emergency/disaster) are clearly identified
  Rationale: current objectives assume gaps have already been identified and agreed – Chair’s proposal to allocate TUs now for SI+WI seems to reflect this – but that may not be the case
Proposal 2: Pragmatic approach for femtos: start from operator requirements and consider available NG-RAN toolbox rather than pre-5G solutions
Proposal 3: For local breakout, identify gaps (if any) in available functionality; if further specification work is needed, work on a common solution to avoid multiple “flavors”

## Slide 12
https://www.ericsson.com/en/5g