## Slide 1
RP-233799
RAN1 AI/ML for Air Interface in Rel-19
—
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023

## Slide 2: Contents
        Rel-18 AI/ML Overview
        Views on Rel-19 RAN1-led AI/ML for Air Interface
        Conclusion
RP-233799

## Slide 3: Rel-18 AI/ML Overview
    Initial common AI/ML framework
      Development of the two Life Cycle Management (LCM) procedures:
        Functionality-based LCM, based on UE capability
        Model-ID-based LCM
      Definition of different collaboration levels between NW and UE
      Focus on offline training, as well as offline model identification and testing
      Aspects such as model transfer/delivery, and online training are being deprioritized
    Use cases studied on AI/ML for NR Air Interface SI
      CSI compression (two-sided)
        Trade-off between performance and complexity.
      CSI prediction (UE-side)
      Spatial and temporal domain beam prediction (NW-side, UE-side)
      Direct AI/ML and AI/ML assisted positioning (NW-side, UE-side)
RP-233799

## Slide 4: Views on Rel-19 RAN1-led AI/ML for Air Interface
    Potential Objectives for Rel-19 WI for AI/ML Air Interface are as follows:
        Enable the development of data collection frameworks for training, performance monitoring, and inference at the NW and the UE side.
        Specify signalling aspects for model management, including activation/deactivation/switching/fallback.
        Specify the use of assistance information from NW to UE and UE to NW.
        Specify a reliable performance monitoring framework that supports model selection.
        Consider a unified AI/ML framework that accommodates use case-specific signalling and reporting (including CSI prediction, beam management, positioning and mobility)
        Define applicability/additional conditions signalling.
        Focus on UE capability signalling reduction.
        Focus on beam management and positioning use cases.
RP-233799

## Slide 5: Views on Rel-19 RAN1-led AI/ML for Air Interface
RP-233799
    Additional considerations
    Aspects not fully addressed in the study; these considerations are essential for constructing a resilient LCM framework
      Training data availability, transfer and ownership:
        UE perform measurements, and NW-side owns the data and trains a model.
        The NW-side provide resources (e.g., beams, activate TRPs, LMF/PRU) and UE-vendor owns the data and trains a model.
      Performance monitoring responsibility and monitoring data/logs ownership:
        NW cannot ensure QoS, because a UE activates an under-performing model and there is no active monitoring on UE-side.
        The NW-side provides resources for monitoring (e.g., beam sweep, LMF/PRU), but does not benefit from the monitoring data/logs.
      Model testing for robustness and generalizability:
        How can the model undergo testing and verification to ensure for generalizability over different settings and environments?
        How can area-specific models be tested and under which considerations?

## Slide 6: Views on Rel-19 RAN1-led AI/ML for Air Interface
    Additional Objectives for Rel-19 WI for AI/ML Air Interface :
      Within the unified AI/ML framework consider the following aspects:
        Specify accessibility, transfer procedures of training and performance monitoring data with a specific focus on data ownership considerations.
        Specify model testing for both generalizable and cell/area-specific models.
        Specify adequate, dynamic tests for model generalizability and robustness.
RP-233799

## Slide 7: Conclusion
        The initial framework for AI/ML integration has been defined during the Rel-18 study item
        Different use cases have been studied showing a performance improvement over legacy approaches and should be handled in the normative phase in Rel-19
                CSI compression and prediction
                Beam management
                Direct AI/ML positioning and AI/ML-assisted positioning
RP-233799