## Slide 1
RP-233805
Considerations for SBFD in Release 19
—
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023

## Slide 2: Contents
        Considerations for SBFD in Rel. 19
        Conclusion
RP-233805

## Slide 3: Considerations for SBFD in Release 19
    Based on the evaluation framework for Duplex Evolution developed during Rel.18 the WI in Rel. 19 can build a fundamental step forward to enable:
        Flexible slot formats allowing simultaneous transmission and reception at the gNB in a given band
        Demand driven provision of additional UL resources using “traditional” DL slots
        Interference management framework for inter-gNB cross link interference, CLI
          Inband interference, adjacent band interference
        More flexible TDD operation in real deployment scenarios
        Radio environment sensing using mono-static and bi-static sensing use cases (listen while talking)
    SBFD is considered a forward compatible feature enabler introduced on the network side in order to reduce impact and complexity at the UE side
RP-233805

## Slide 4: Considerations for SBFD in Release 19
    Although flexible TDD has been specified, the current 3GPP enabled features have not allowed meaningful flexibility on TDD operation for MNOs in their own networks and in co-existence with other MNOs
RP-233805
Source: https://cdn.codeground.org/nsr/downloads/researchareas/white_paper_XDD.pdf
        Current status to avoid inter-gNB CLI inband and across bands:
          Neighbouring gNBs of same MNO are operated at same TDD slot structure
          Adjacent bands of same MNOs are operated at same TDD slot structure
          Bands of different MNOs in same TDD band are operated at same TDD slot structure

## Slide 5: Considerations for SBFD in Release 19
    Gradual features enhancements on top of current SOTA slot structure as base line should ensure high degree of coexistence
RP-233805
Source: https://cdn.codeground.org/nsr/downloads/researchareas/white_paper_XDD.pdf
      Enablers to be specified during Rel.19 WI:
        Interference management framework between gNBs (all types of gNBs macro to femto)
          Intra gNB intra-band: by means of self interference cancellation
          Inter gNB intra-band: by means of spatial mitigation and suppression
          Inter gNB inter-band: by means of spatial mitigation and suppression & spectral shaping/filtering

## Slide 6: Conclusion
        Rel-18 study item provides a clear scope where SBFD should be specified
        Rel- 19 WI has to provide frame work and technical means to enable Duplex Evolution towards SBFD by
          Specifications of means for interference measurement and management for CLI between gNB
          Specifications of means for interference mitigation for gNB-2-gNB CLI and UE-2-UE CLI
          Specifications of means for interference suppression between gNB-2-gNB CLI
          Specifications of means for enhanced inter UE CLI measurements between neighboring cells of same and different MNOs
        Rel- 19 WI should include all types of gNBs
RP-233805