## Slide 1
RAN WG3 Chair: Yin Gao
RAN WG3 Vice-Chairs: Angelo Centonza, Gen Cao
RAN3 Secretary: Seonggu Shim
Status Report for RAN WG3
3GPP TSG RAN #103, Maastricht, NL
Mar 18th – 21st, 2024
RP-240008

## Slide 2: Executive Summary
Total 729 Tdocs at submission deadline (excluding LSin received from other groups) in Q1
  15% LSs and related documents
  18% Maintenance: Rel-17 & earlier
  3% Rapporteur Corrections: Rel-18
  63% Documents to Rel-18 WIs
Updated endorsed guidelines for f2f meeting with 1-way remote access: R3-240003
TR30.531 Work Plan and Working Procedures - RAN WG3 was updated and approved in R3-240004
R18 positioning WI is completed in RAN3.
For XR in DC, RAN3 does not support DC in Rel-18 due to time limitation. Whether to continue the discussion in R19 XR WI or TEI19 needs to be decided in RAN#103.
RAN3 #123 | Feb 26th – Mar 1st, 2024 Athens, GRE
RAN #103 | Mar 18th – 21st, 2024 Maastricht, NL

## Slide 3: Tdoc submitted to RAN3
The total number of contributions around 700 for each RAN3 meeting is affordable
Notes: w

## Slide 4: Tdocs for each Topic

## Slide 5: RAN3 CRs to RAN
List of RAN3 CRs to RAN in RP-240009, which includes:
  202 CRs were agreed in Q1 for R18 WIs maintenance and TEI corrections.
    3 Rel-15: 3 Cat.F CRs
    10 Rel-16: 8 Cat.F CRs, 2 Cat.A CRs
    26 Rel-17: 18 Cat.F CRs, 8 Cat.A CRs
      6 Non-Backwards-Compatible (NBC) CRs
        Rel-16: R3-240527(Cat.F)
        Rel-17: R3-240528(Cat.A), R3-240825(Cat.F)
        Rel-18: R3-240529(Cat.A), R3-240826(Cat.A), R3-240839(Cat.F)
        (Here is how 3GPP works with NBC changes)
    111 CRs for Rel-18 WIs: 105 Cat.F CRs, 1 Cat.A CR, 5 Cat.B for positioning WI
    89(+1) Rel-18 TEI: 1 Cat.B CRs (+1 Cat.B CR for RAN2 spec.), 18 Cat.D CRs, 37 Cat.F CRs, 33 Cat.A CRs
    2 Cat.B TEI18 CRs with TEI identifier
      [2Rx_XR_Device] R3-241070, R3-241069 (draft CR for stage 2 TS38.300), impact on RAN2 (two set of CRs) and RAN4 (R4-2403890 was endorsed)
  29 endorsed draftCRs to RAN2 specs.
  R3-241205 triggered by LS from CT4 (R3-240006) with WI code: NR_newRAT-Core, TEI18 and Cat.F

## Slide 6: Experience for GTW Usage in f2f meeting
RAN3 had three meeting rooms for main session (1) and offline discussion (2) which support 1-way remote access.
In general, the number of remote participants for main session is limited, less than 10. The audio device test for remote access needs to be performed before daily session starts.
MCC and IT support during the meeting is sufficient.

## Slide 7: R18 Positioning WI
Progress in the last quarter
  For LPHAP:
    In POSITIONING INFORMATION REQUEST, combine the new added parameters in Requested SRS Transmission Characteristics IE to a new IE, e.g. Validity Area specific SRS Information.
    Add new IE in Positioning Information Request in NRPPa/F1AP to provide pre-configured SRS information (requested SRS transmission characteristics, including the VA), a new IE listed 16 SRS characteristics.
    Add a list of preconfigured SRS configuration, each of them is associated to a VA in Positioning Information Response in NRPPa and F1AP.
    Introduce SRS Reservation Notification in NRPPa and F1AP. Use the Requested SRS Transmission Characteristics IE instead of the SRS Config in SRS INFORMATION RESERVATION NOTIFICATION.
    For area-specific SRS allocation, the cell list of positioning validity area is signaled to gNB-DU in POSITIONING INFORMATION REQUEST. The cell list of positioning validity area is also provided to gNB-DU in F1AP SRS INFORMATION RESERVATION NOTIFICATION for the purpose of SRS reservation.
  For BW Aggregation:
    Support new Reporting Granularity Factor {-3, -4, -5, -6} in addition to {-1, -2}.
  For Redcap positioning:
    Introduce a new Tx Hopping Configuration IE in the Positioning SRS Resource IE that is aligned with RRC.
    Introduce a new SRS Periodicity IE which can be reused within the Requested SRS Transmission Characteristics IE, Positioning SRS Resource IE, and Tx Hopping Configuration IE.
    Add new IE in TRP Measurement Result to indicate either a single-hop or multi-hops measurement
Other important info
The R18 Positioning for NG-RAN WI is completed in RAN3.

## Slide 8: R18 SON/MDT Correction
Progress in the last quarter
For NPN:
  Update description for PNI-NPN area scope in stage2 TS37.320.
  Add "M" Presence condition for PLMN ID IE in the choice of PNI-NPN Based MDT in Area Scope of MDT IE in tabular to align with ASN.1
  For SPR & SHR
    Update description of SPR available indication, SN mobility information,“addition” for the terminology and section headers in TS37.340 and TS38.300.
    Change references for SN mobility information to TS37.340.
  For RACH
    To replace PSCellIdListNR with CellIdListNR in Semantics description part of PSCell List Container IE contained in ACCESS AND MOBILITY INDICATION message in XnAP.
    Added text that only NR report is forwarded in TS37.340.
    Correct the UE behavior after receiving SPR configuration from network and Update the wording for collection of SN RA Reports in TS37.340.
  For NR-U
    Update description on MRO for NR-U in stage2 TS 38.300.
    Add procedural description on DL LBT failure handling in XnAP.
    Introduce the stage 2 and stage 3 description on DL LBT failure handliing for CU-DU split scenario in TS 38.401 and F1AP.
  For MRO
    Update description on CPAC Execution to wrong PSCell in stage2 TS37.340.
    Add semantics description on UE RLF Report Container in “Inter-system Mobility Failure for Voice Fallback”.

## Slide 9: R18 SON/MDT Correction
Progress in the last quarter
  For ASN.1 checking:
    Update the ASN.1 for PNI-NPN Based MDT is modified so that it is encoded as an extensible SEQUENCE like the other choice options in NGAP and XnAP.
    Add transaction ID in the RACH INDICATION message in F1AP.
Other important info
N/A

## Slide 10: R18 QoE Correction
Progress in the last quarter
Update stage-2 description on 38.300 and semantic descriptions to clarify the scenarios for using the Further RAN visible reporting path related IEs. Stage-3 corrections need to be further checked.
Add ‘Available RAN Visible QoE Metrics’ in the QMC Coordination Request message.
Change the code point of release indication into ENUMERATED (rvqoe, qoe and rvqoe, ...).
Introduce release indication from MN to SN.
Remove the SN-related QMC Information at MN IE from the XnAP Handover Request message.
Correct the SRB id over F1, for SRB4 and SRB5 which are introduced for QoE.
Correct some ASN.1 issues over XnAP.
Corrections on the following specifications are endorsed agreed:
TS37.340, TS38.300, TS38.413, TS38.420, TS38.423, TS38.470, TS38.473
Other important info
N/A

## Slide 11: R18 AI RAN Correction
Progress in the last quarter
  Reply LS to SA5 on Lifecyle Management of AI/ML model. No requirement was identified related to lifecycle management of AI/ML model from RAN3 perspective in R18.
  Reply LS to SA5 on Energy cost Index. RAN3 gives clear understanding on the usage and requirement of energy cost index, and answer the questions from SA5 on the details of mapping rule between energy cost and energy consumption.
  No consensus on the introduction of new cause values due to time issue and new code points apart from “Start” and “Stop” to the Registration Request for data collection IE.
  Miscellaneous stage2 and stage3 corrections for support of AI/ML for NG-RAN.
Impacts and dependencies on other WGs
  SA5 shall take the understanding from RAN3 into account in their work on AI/ML.
Other important info
N/A

## Slide 12: R18 mobile IAB Correction
Progress in the last quarter
In 38.401, revise mIAB RLF recovery procedure to include the scenario where the F1-terminating donor is different from the RRC-terminating donors.
38.401 to capture the behavior of the MT’s target IAB-donor when the mIAB authorization status = “non-authorized” is received during MT migration and RLF recovery.
Agree that CU can request from mIAB-DU to change cell barring via gNB-CU Configuration Update Request.
Add clarification to 38.423 that for mobile IAB, the “non-F1-terminating IAB-donor” in the TMM procedures and IAB Resource Coordination procedures refers to the “RRC-terminating IAB-donor”. Clarify that the term “boundary node” used in the context of these procedures does not apply for mobile IAB.
Add new cause values to be used in TMManagement Reject for “no radio resources available for BH” and “mIAB-node not authorized”.
The implementation should ensure that the IAB TRANSPORT MIGRATION MANAGEMENT procedure is initiated once the F1 setup of the mobile IAB-DU or the mobile IAB-MT migration has completed, so that the RRC-terminating IAB-donor can send the updated authorization status via the IAB TRANSPORT MIGRATION MODIFICATION REQUEST message.
Miscellaneous corrections on the following specifications are agreed: TS38.413, TS38.420, TS38.423, TS38.473, TS38.401, TS38.455.
Impacts and dependencies on other WGs
Regarding PDU session indication in NG Handover Required, wait for ongoing discussion in SA2 to concluded.
Regarding PDU session indication in NG Handover Request ACK, capture AMF’s behavior when receiving the PDU session Resource Admitted List IE in case the mIAB MT has no PDU Session. The AMF behaviour to be specified is pending SA2´s agreements
Other important info
N/A

## Slide 13
Progress in the last quarter
RAN3 agreed to include the ltm-EarlyUL-SyncConfigSUL, the ltm-nzp-CSI-RS-Resource List, and the PathlossReferenceRS in F1.
Change the source gNB-DU ID to a list of candidate gNB DU ID including the source in UE context setup request/UE context modification request in LTM preparation.
Add a list of Preamble Index linked with the RACH Configuration and candidated gNB-DU ID(including the source gNB-DU) to both UE CONTEXT SETUP RESPONSE and UE CONTEXT MODIFICATION RESPONSE message.
Add a list of Preamble Index linked with the RACH Configuration to the Early Sync Information List within UE CONTEXT MODIFICATION REQUEST message.
Send a list of early RACH configuration prepared by different candidate gNB-DUs to the new serving DU for example, after cell switch command, or step 7 and 8, or after access success.
The target DU receives the TA values for subsequent LTM in Cell Switch Notification.
The gNB-CU provides the TA =0 to the source gNB-DU and other candidate gNB-DUs.
The gNB-CU signals to source DU to indicate UE base TA information.
Introduce UL TCI state ID in the cell switch notification.
Other miscellaneous corrections for LTM.
Some corrections on CHO with CPAC.
Some corrections on S-CPAC.
Impacts and dependencies on other WGs
The encoding for ltm-nzp-CSI-RS-Resource List, and the PathlossReferenceRS is pending to RAN2.
R18 Mobility Enh. Correction

## Slide 14: R18 MBS Correction
Progress in the last quarter
LS handling on MBS Assistance Information on NGAP during mobility.
Send LS to CT4 and CC SA2 to ask for support of handling NG-U Path Failure for MBS traffic.
Rel-17 correction on multiple F1-U tunnels for broadcast MRB.
Rel-18 corrections on redundant info, simplication on ASN.1 (e.g., remove the IEs already exists in per interface message from the per session message ), DU includes DL TNL Address in-DU initiated F1-U establishmen procedure and other ASN.1 corrections.
Introduce the overall procedure for Broadcast MBS Session Setup for network sharing scenarios in 38.401.
Impacts and dependencies on other WGs
N/A.
Other important info
N/A.

## Slide 15: R18 Sidelink Relay Correction
Progress in the last quarter
Introduce the U2U RLC Channel QoS IE (with criticality “reject”) referring to a PC5 QoS Parameter IE in the UE CONTEXT SETUP REQUEST message and UE CONTEXT MODIFICATION REQUEST message from gNB-CU to gNB-DU. Capture the corrections for U2U relay in TS 38.473 and TS 38.470.
Keep both IEs (i.e., Target Relay UE ID IE and Remote UE Local ID IE) in Path Addition Information IE.
Miscellaneous corrections to stage 2 and stage 3 specs for SL relay.
Other important info
N/A

## Slide 16: R18 NR NTN and IoT NTN Correction
Progress in the last quarter
For NR NTN:
  Update procedural description for Downlink RAN Early Status Transfer procedure in NGAP.
  Change the Criticality of Conditional Handover Time based Information IE from “ignore” to “reject” in XnAP.
  Update description on time-based CHO in TS 38.300.
  For IoT NTN
  Update procedural description for MME Early Status Transfer procedure in S1AP.
  Change the Criticality of Conditional Handover Time based Information IE from “ignore” to “reject” in X2AP.
  Correct the IE type and reference of Handover Window Start IE in S1AP and X2AP.
  Update description on time-based CHO in TS 36.300.
  For ASN.1
    Update the ASN.1 to refer to the Bearers-SubjectToDLDiscardingList.
    Change the presence of DL Discarding from “optional” to “mandatory” in ASN.1.
    Delete the new added coding of COUNT-PDCP-SN12 and COUNT-PDCP-SN18, and reuse the existing of IE .i.e. COUNTValueForPDCP-SN12 and COUNTValueForPDCP-SN18 in ASN.1.
Other important info
N/A

## Slide 17: R18 NR XR Correction
Progress in the last quarter
For Non-integer DRX cycle:
- For CU -> DU direction, no need to add a new IE.
- For DU -> CU direction: no enhancement is needed.
Not support DC in Rel-18.
For UL: Introduce a per DRB new indication in F1AP from CU to DU.
Introduce the new PSI based discard indication with two codepoints {start, stop} in the UE context setup/modification procedure.
When configuration and reconfiguration of the PSI based discard indication, codepoint ‘start’ is used. When release of the PSI based discard indication, codepoint ‘stop’ is used.
Add the DL PSI based Discard timer in the PDCP configuration IE in E1AP from gNB-CU-CP to gNB-CU-UP.
Other miscellaneous corrections.
Other important info
N/A

## Slide 18: R18 NR MT-SDT Correction
Progress in the last quarter
Some stage 2 and Stage 3 clarification, without ASN.1 impact.
Other important info
N/A

## Slide 19: R18 NR Redcap Enh. Correction
Progress in the last quarter
Agreements achieved based on incoming LS R3-240043 (SA2)
  Add the cause value “eRedCap UE Not Supported” for the Rel-18 target node (which does not support eRedCap) to inform the failure reason during NG based handover.
  Add the “eRedCap Indication” IE similar to the “RedCap Indication” IE in INITIAL UE MESSAGE, PATH SWITCH REQUEST and HANDOVER REQUEST ACKNOWLEDGE messages.
Agreements achieved based on incoming LS R3-240026 (SA2)
  RAN3 needs to modify the Paging Policy Differentiation IE in the RAN PAGING REQUEST message by adding a list of PDU Sessions with list of QoS flows, with the parameters QFI, PDU session ID, PPI, ARP, 5QI, and the DL data size.
  The encoding of the new DL data size follows other specifications, i.e. up to 96000 bytes.
Other important info
N/A

## Slide 20: R18 NR URLLC Correction
Progress in the last quarter
To reword ‘event c’ as “event a) occurred and b) has not yet been reached for a RAN TSS attribute an implementation-dependent time interval has passed, or a previously reported value can no longer be met.” Corresponding CR to TS 38.401 is agreed.
It is agreed to introduce Transaction ID in F1AP TSS messages to follow the general specification principle.
SA2 agreed to support multiple TSS reporting sessions and to introduce a routing ID to identify the requesting TSCTF. Corresponding CR to TS 38.413 is agreed.
Some text clarification in 38.300 is endorsed.
Other important info
N/A

## Slide 21: R18 RAN Slicing Correction
Progress in the last quarter
  Adding resource handling for Alternative S-NSSAIs in TS38.300.
  Correction of cell unavailable list in XnAP.
  ASN.1 corrections for Partially Allowed NSSAI in NGAP.
Other important info
N/A

## Slide 22: R18 Network ES Correction
Progress in the last quarter
An F1AP CR is agreed, to correct some errors in taular and ASN.1.
A CR to TS38.470 is agreed, to add the description for the CU to provided to DU about the allowed cells to for beam deactivation.
Common understanding is that the existing procedure texts (see below) already cover the SSB already activated case.
“If Cells to be Activated List Item IE is contained in the GNB-CU CONFIGURATION UPDATE message and the indicated cells are already activated, the gNB-DU shall update the cell information received in Cells to be Activated List Item IE”
Other important info
N/A

## Slide 23: Other R18 WIs
Progress in the last quarter
  R18 UAV
  - Correct NGAP procedure name for UAV related procedure in TS 38.300.
  - Sync up UAV related IE names in RAN3 related specifications.
R18 NCR
  - Introduce NCR-MT definition and change all “NCR” to Network Controlled Repeater in TS 38.401.
Other important info
N/A

## Slide 24: TEI Corrections
Progress in the last quarter
2RX for XR
- Introduce a new SPID value for 2RX XR UE.
- Add a new IE to indicate 2Rx XR devices in the UE RADIO CAPABILITY INFO INDICATION message.
- Continue discussion on XnAP/F1AP enhancements for Served Cell Info and F1 Paging to include 2 Rx indication.
R17 SON/MDT
  - Update the procedural description of MIMO PRB usage reporting.
  R18 RedCap UE MBS
- LS handling on RedCap UE MBS broadcast reception (i.e., separate FSA ID for RedCap UEs), and will provide RAN3 view based on RAN2 output.
IAB corrections:
  - IAB Authorization Status IE is introduced in X2APSGNB ADDITION/MODIFICATION REQUEST, XnAP HANDOVER REQUEST and XnAP S-NODE ADDITION/MODIFICATION REQUEST messages.
  - Add stage 2 clarification on the mapping between the IP addresses of the IAB-node and the BAP address(es) of the corresponding IAB-donor-DU(s) in 38.401 for OAM-based IP address allocation case.
  SDT release
- Align with RAN2 solution in stage2 specs in the next meeting.
- Agree with network based solution in the next meeting, unless the showstopper is found for network solution.

## Slide 25: TEI Corrections
Progress in the last quarter
NTN Mobility Restrictions
- For RAT restriction information, add 4 codepoints to S1AP and X2AP (NR-LEO, NR-MEO, NR-GEO, NR-OTHERSAT), and 4 codepoints to NGAP and XnAP (e-UTRA-LEO, e-UTRA-MEO, e-UTRA-GEO, e-UTRA-OTHERSAT)
  N3IWF
- Introduce Trace functionality in N3IWF for non-3GPP access scenarios in TS 29.413.
Positioning Corrections:
- Correct the ASN.1 according to the tabular, add the presence Optional for the NR PRS Azimuth fine IE, the NR PRS Elevation IE and the NR PRS Elevation fine IE.
- Support for NR UE Rx-Tx time difference for NR UL E-CID measurement reporting.

## Slide 26: My Heartfelt Thanks To:
Angelo Centonza, Gen Cao (RAN WG3 Vice-Chairs)
  For chairing the corresponding sessions and all the support during the meeting!
Seonggu (RAN WG3 Secretary)
  For impressive hard work and kind support!
Hongzhuo, Georg, Man, Mingzeng, Jiancheng...
  For their positive and hard work on moderating some tough email discussions and good support!
All Rapporteurs and moderators, especially Alex (XnAP), Henrik(F1AP), Sean(NGAP)...
  For their efforts to rapporteur updates and TEI corrections!
All RAN3 delegates
  For their positive, constructive and cooperative spirit and hard work!