## Slide 1: Proposals on Demodulation Topics for Rel-19
NTT DOCOMO, INC.
3GPP TSG RAN #103
Maastricht, Netherlands, March 18-21, 2024
Agenda Item: 9.1.4.5
Document for: Discussion
RP-240069

## Slide 2: Overview
During RAN#102, candidate Demodulation topics were discussed and several topics were recommended for further discussions and down-selection
Based on the summary, we propose Demodulation topics for Rel-19 RAN4 package as follows:
  Performance requirements of MMSE-IRC receiver for NR BS

## Slide 3: Performance requirements of MMSE-IRC receiver for NR BS
Motivation
  According to the changing of mobile communication and expansion of rich context services, e.g. video streaming, uplink traffic has been becoming more important factor for mobile service
  As same as LTE situation, the expansion of NR makes inter-cell interference more severe than when NR service was started
  Moreover, if existing network deployment is designed based on non-HPUE, inter-cell interference from HPUE may cause significant degradation on uplink
  In addition, for multi-vendor architecture, it is difficult to ensure the minimum performance as a whole network from operator point of view, and also it is difficult for new vendor to implement MMSE-IRC receiver with satisfied performance for these network
  Based on above analysis, demodulation performance requirements of MMSE-IRC receiver for NR BS is necessary even if in this later stage

## Slide 4: Performance requirements of MMSE-IRC receiver for NR BS
Possible objectives
  Identify target deployment scenarios and agree on relevant network parameters
    At least homogeneous deployment (macro cell only) should be considered
    Heterogeneous deployment (co-channel between macro cell and low power node) can be deprioritized
    FR2 is not necessary because of its high propagation loss characteristics
  Study applicability of inter-cell interference modelling methodology and other side conditions identified during LTE study, and link-level simulation to evaluate gain of MMSE-IRC over baseline receiver (MMSE receiver)
    Conduct system-level simulation if necessary to determine the inter-cell interference modelling methodology and other side conditions
  NR BS MMSE-IRC receiver shall be assumed as the reference receiver structure for specifying the requirements.
    Demodulation RS based MMSE-IRC receiver can be considered as baseline, and practical and realizable implementation should be taken into account.
  Specify the enhanced demodulation performance requirements for verification of BS receiver’s ability on inter-cell interference suppression.
    For PUSCH, specify enhanced demodulation performance requirements based on the reference receiver.
    For PUCCH, with lower priority, determine whether to specify enhanced demodulation performance requirements based on the reference receiver.
  Specify the enhanced conformance test requirements.