## Slide 1: Candidate RAN4 led spectrum related NTN topics for Release 19
Sources: Thales, Novamint, Iridium, Terrestar, Inmarsat, Intelsat, Airbus, Gilat, OQ technology, Magister solutions, Hispasat
3GPP TSG RAN #103
Mars 18 - 22, 2024, Maastricht/The Netherlands
Agenda: 9.1.5 Proposals led by RAN4 (spectrum related)
TDOC: RP-240089
For: discussion

## Slide 2: Spectrum related NTN topics
Ku band definition (global allocation) for NR-NTN
L band definition - unpaired spectrum (global allocation) for IoT-NTN
Potential S band definition (specific Region 2 allocation) for NR-NTN
Extended L band definition (aligned with b253) for NR-NTN
Potential Combined L band for NR NTN (aligned with combined n255 + (n)253 range). Consider whether “unpaired” DL and UL band parts can be specified.

## Slide 3: Band description
Band | Downlink | Uplink | UE type | Radio interface | Orbit | Mode | TX-RX Separation
Ku | 10.7 – 12.75 GHz | 12.75-13.25 GHz & 13.75-14.5 GHz | VSAT type (Fixed and mobile) | NR | NGSO & GSO | FDD | 
L | 1616 - 1626.5 MHz | 1616 - 1626.5 MHz | PC3 | NB-IoT | NGSO | TDD | 
Potential S | 2180-2200 MHz | 2000-2020 MHz | PC3 | NR & NB-IoT | GSO & NGSO | FDD | 
Ext L | 1518-1525 MHz | 1668-1675 MHz | PC3 | NR |  | FDD | Flexible
Potential Combined L | 1518-1559 MHz | 1626.5-1660.5 MHz & 1668-1675 MHz | PC3 | NR |  | FDD or Unpaired DL and UL | Flexible or unspecified

## Slide 4: Questions ?
Nicolas.chuberre@thalesaleniaspace.com