## Slide 1
0
Views on candidate RF topics for Rel-19
3GPP TSG RAN Meeting #103 RP-240152 Maastricht, Netherlands, March 18-21, 2024
Agenda Item: 9.1.4.1
Source: CMCC
Document for: Discussion

## Slide 2
High power UE for CA
Specify HPUE CA RF requirements for handheld and FWA with following:
  PC1.5 UE for intra-band contiguous CA with or without UL MIMO with 2Tx
  PC 1.5 UE for two band inter-band CA with 2Tx
    PC2 TDD/FDD band 1Tx+PC2 TDD band 1Tx
  3Tx for both handheld and FWA
    PC2 3Tx for inter-band CA for handheld (only FWA supported in Rel-18)
    PC1.5 3Tx for inter-band CA:
      TDD + TDD band, including PC2 + PC2, PC1.5 + PC2/PC3
      TDD + FDD band, including PC2+ PC2, PC1.5+PC2
  Enable increase UE high power limit feature for inter-band CA HPUE.
Potential objectives

## Slide 3
6Rx
6Rx support for smartphone:
  Example bands are n41, n77, n78 and n79 (other bands to be introduced in the release independent way later from Rel-18)
  Applicable frequency upper bound to support 6Rx.
  Requirements to support SRS antenna switching
  Support at least 4 MIMO layers, FFS for 6 MIMO layers
Potential objectives

## Slide 4
Extension of UL Tx switching scenarios
Latest status
In Rel-17, UL Tx Switching between one carrier in band A and two contiguous carriers in band B was specified.
In our network, both 2.6GHz (n41) and 4.9GHz (n79) has two contiguous UL carriers. In order to further improve the uplink throughput, UL 2Tx-2Tx switching between band A (2.6GHz) and band B (4.9GHz), each with two contiguous uplink carriers, should be supported.
Time mask requirements need to be specified for UL Tx switching between two contiguous carriers in band A and two contiguous carriers in band B. No RAN1 and RAN2 spec impacts are expected.
Motivations: UL Tx switching
We propose this in last RAN4 meeting, due to lack of time, companies need more time to check. It was agreed that RAN4 will continue discuss this topic under maintenance. Hence, there is no need to add this objective in Rel-19.

## Slide 5
NTN HPUE
Study the co-existence for NTN/IOT-NTN HPUE in NTN FR1 bands, including PC2/1.5 and PC1. If feasible, specify corresponding RF requirements for handheld and non-handheld UE.
Potential objectives

## Slide 6
THANK YOU！