## Slide 1: UIC enhancements for FRMCS This is an update of RP-233211
3GPP TSG RAN#103 - RP-240244
Maastricht, 18-21 March, 2024
Agenda item 9.1.4.6

## Slide 2: FRMCS enhancements: Uplink MIMO
Use case: Increase throughput and reliability in uplink for railways using FRMCS in band n100 and n101
Description:
  Support of Uplink 2x2 MIMO
  Support of Uplink Tx diversity for 2Tx
  In bands n100 and n101
  For PC1 and PC3 UEs
  For PC1 HPUE enabling +31dBm output power in n100 and n101
  For open-loop configuration to support high speeds (350 – 500km/hr)
UIC would like to request in Release 19 support of Uplink MIMO and Tx diversity in n100 and n101

## Slide 3: FRMCS enhancements: QoS in HST
Use case: Downlink and uplink connectivity on high-speed trains (350 – 500km/hr) for critical services
Description:
  In R15 HST in FR1 has been addressed for best effort services in 2.7GHz;
  Railways/ FRMCS using bands n100 and n101 need support of specific QoS profiles for critical services:
  Deployment conditions may differ from current HST assumptions: BS at approximately 10m instead of 100m from rail track, intersite distance 2000m instead of 1732m. Doppler shift 880Hz;
  Unclear if NR channel quality under HST conditions still meets the 5QI criteria for packet delay and error rate.
RAN is requested to study High Speed Mobility in FR1 for critical services and specify enhancements where necessary.