## Slide 1
Proposed objectives for the UE RF RAN4 Rel-19 package
Ericsson
Agenda item: 9.1.4.1
Document for: Discussion
3GPP TSG-RAN Meeting #103
Maastricht, NL, March 18 – 21, 2024
RP-240253

## Slide 2: UE RF Rel-19
Proposed objectives for the following candidate WI listed in RP-240019
UE RF: Power boosting and/or MPR reduction for FR1/FR2
  MPR reduction for UL contiguous CA in FR1/FR2
UE RF: 6RX
  Improved SRS reporting for antenna switching usage
UE RF: High power UE (HPUE) for CA in TN
  PC1.5 UE for intra-band contiguous CA with or without UL MIMO with 2Tx
  PC1.5 UE for two band inter-band CA with 2Tx and/or 3Tx for handheld and FWA
  Generic framework of support increasing UE power high limit for inter-band CA HPUE (only for TN) for different power classes
OTA: TRP/TRS Enhancement

## Slide 3: Power boosting and/or MPR reduction: CA MPR for fragmented (non-contiguous) spectrum
MPR reduction for UL contiguous CA in FR1/FR2
Add scenario for non-contiguous CA with 2DL/2UL within FDD/TDD bands relevant for operators with fragmented spectrum holdings
  single PA as baseline; non-contiguous carrier separation < 100 MHz supported by one Tx/Rx branch
Currently, for UL intra-band non-contigous CA configurations,
  the MPR larger than that for the non-CA case for UL transmissions confined within one of the two carriers, e.g. the Pcell in the FDD example below, for UEs not indicating dualPA-Architecture
  the MPR for concurrent transmissions on two UL carriers very large, and only evaluated for Band n41
  significant reduction of UL coverage for CA in non-contigous spectrum
UL PCell
UL Scell
DL PCell
DL Scell
DL band
UL band
Single PA

## Slide 4: Power boosting and/or MPR reduction: proposed objectives for additional FR1 scenario
Improve coverage and TP for UL intra-band non-contiguous (NC) CA
Introduce additional requirements for
  UL intra-band non-contiguous CA (1Tx or 2Tx)
    single UL cell scheduled/active: by reducing MPR to that of non-CA for UL transmissions confined within one of the two cells also for UEs not indicating dualPA-Architecture at least when one of the cells is deactivated
    dual NC UL cells scheduled: by reducing MPR for concurrent transmissions for FDD and TDD regardless of PA architecture with additional side-conditions (LO leakage etc) if needed
    up to 100 MHz carrier separation (intraBandFreqSeparationUL-AggBW-GapBW-r16 class I) as supported by a single TX/PA and RX chain
    enhancements can be subject to UE capability
  combine with UL-MIMO (2Tx) or UL inter-band CA configurations with an UL intra-band NC part (1Tx + 1Tx)
Non-collocated cells can be considered (based on n77 requirements)
Justification: enhance performance of deployments in fragmented intra-band spectrum
UL PCell
UL Scell
DL PCell
DL Scell
UL NC CA (single/dual PA)
UL NC CA + UL-MIMO (dual PA)
MPR for non-CA when Scell not scheduled/activated

## Slide 5: Power boosting and/or MPR reduction: MPR reduction for UE-specific BW within carrier
RAN4 requirements specified w r t the channel bandwidth (MHz)
  Unwanted emissions apply outside NR RF carrier, while less stringent in-band emission requirements apply within the carrier
Consider MPR reduction for UE-specific CHBW smaller than the carrier bandwidth, e.g. for RedCap (see R4-233297)
Unwanted emissions requirements corresponding to the carrier bandwidth apply at an offset from the UE-specific CHBW (one-sided – see below – or two-sided), MPR can be reduced in parts of the UE-specific CHBW
  The offset known by the UE from SIB1 and ServingCellConfig, the MPR reduction depends on the offset

## Slide 6: 6RX: SRS reporting
Further discussions on the following potential objective:
  Improved SRS reporting for antenna switching usage
Poor SRS accuracy and variability degrade reciprocity-based DL-MIMO performance due to poor DL-CSI estimates
For SRS antenna switching, the actual SRS output power per SRS port(s) unknown
  Non-reciprocal insertion losses in the signal path(s) unknown
Received SRS power/SNR highly variable also under static conditions notwithstanding different UE antenna gains
  SRS transmissions not conformance tested

## Slide 7: 6RX: proposed objectives (SRS reporting)
Improvement of SRS reporting and performance for CSI estimation part of study phase
Depending on the outcome of the study:
  Specification of a reporting scheme for SRS output power for all configured SRS resources of SRS resource sets (RAN4, RAN2) for 2/4/6/8Rx
    or non-reciprocal UE insertion loss per SRS port(s) if considered feasible
  Limited changes to RAN1 specifications, no change of SRS power control or Type 3 PH
  Improved testing of SRS output power
    essentially no testing of SRS in the UE conformance test specifications

## Slide 8: High power UE (HPUE) for CA in TN: inter-band
PC1.5 UE for two band inter-band CA with 2Tx and/or 3Tx for handheld and FWA
Generic framework of support increasing UE power high limit for inter-band CA HPUE (only for TN) for different power classes
  Merely a continuation of basket WIs and business as usual: MSD specified with higher power per band
  Verification of UE RFFE linearity and isolation – is this necessary for all possible higher power classes? MSD will of course increase with higher power, but suffices to verify for one power class per band for 2Tx/3Tx?
  HPUEs configured with CA reduce UL power for top-level or fallback combinations just because an MSD for a higher power is missing, impacts performance in the field; many other factors not reflected in the worst-case MSD test determine the actual degradation in the field
Per-BC PC2 with ≤ 23 dBm on both bands, MSD up to 32 dB
Per-BC PC1.5 with ≤ 27.8 dBm in one band and ≤ 23 dBm in the other, MSD increases, up to 35 dB…

## Slide 9: High power UE (HPUE) for CA in TN: intra-band
PC1.5 UE for intra-band contiguous CA with or without UL MIMO with 2Tx
  For DL-only intra-band CA or UL contiguous CA cases with CCs combined in baseband, business as usual
  For UL intra-band non-contiguous case or a contiguous case with dualPA architecture (2 LO) a more fundamental change:
    in the current framework, the MPR/A-MPR per CC (of per-band power class) is the same as the MPR/A-MPR for the total power of the BC (of per-BC power class = per-band power class); the UE prioritizing (scaling) power when the UE becomes power limited
  For the new case the UE would not be power limited, up to 26 dBm for each CC and PC1.5 (29 dBm) per-BC power class unless the UE reduces maximum power due to SAR
  UL intra-band non-contiguous CA with PC1.5 a common use case? MPR feasible?

## Slide 10: High power UE (HPUE) for CA in TN: proposed objectives
Q2 2024 study phase on requirements needed for 2Tx/3Tx
  Study and evaluate requirements needed for 3Tx architectures, the per-band and per band-combination (BC) power classes to be specified for a BC
    three Tx paths active simultaneously, additional isolation and linearity requirements?
  Study the requirements needed with a supported higherPowerLimit for a BC with 2Tx or 3Tx
  Study whether verification of cross-band isolation and RFFE front-end linearity are necessary for all possible per-band/per-BC power classes
  Study whether support of UL-MIMO in BCs for 3Tx cases require additional changes
Justification: HPUEs configured with CA reduce output power for top-level or fallback BC just because of missing MSD requirements; many other factors not reflected in the worst-case MSD conformance test determine the actual degradation in the field. Are conductive MSD conformance tests necessary for all possible higher power classes?
Revisit study outcome at RAN#104

## Slide 11: OTA: TRP/TRS Enhancement: proposed objectives
Requirements work
  TRP TRS requirements for operator demanded bands including UE with 1Tx and 2Tx (non-coherent UE)
TRP requirements for UE supporting non-coherent precoding (2Tx)
  Verify full-power UL-MIMO modes (with single layer) if supported by the UE
  2Tx requirements include mutual coupling that affects efficiency/correlation
For UEs supporting coherent precoders, e.g. with 4Tx, min (peak) EIRP requirements specified for precoders, possibly swept
  measurements without phantom