## Slide 1: Way Forward on Spatial Channel Modelling in Rel-19
RP-240254
3GPP TSG RAN Meeting #103
Maastricht, The Netherlands, 18th – 21st March, 2024
Agenda Item 9.1.4.5
Source: BT, Nokia, AT&T, Bell Mobility, Bouygues Telecom, Deutsche Telekom, Ericsson, Intel, Keysight, KT Corp., Orange, Rohde & Schwarz, SK Telecom, Telecom Italia, Telenor, Telia Company, Telstra, T-Mobile USA, Verizon, Vodafone

## Slide 2: Motivation
Demodulation performance requirements in RAN4 are currently limited to the spatially-agnostic TDL channel model.
  Per-layer variability is not observed, unlike in real deployment scenarios. Hence the receiver’s ability to take advantage of spatial diversity provided by the channel/network is not subject to any requirements.
  In 8Rx SU-MIMO, where the 2 codewords are mapped to different sets of layers, no performance differentiation between the codewords is visible.
  MU-MIMO performance can only be tested when the UEs’ channels are spatially separable, which is not possible with the TDL channel model. Hence full benefits of operator investment in MU-MIMO cannot be verified.
Spatially realistic performance requirements are motivated for both 5G-Advanced and 6G:
  Help to underpin good performance for MIMO features in today’s 5G-Advanced networks, and
  Ensure that 6G uses spatially realistic methodology for performance requirements from day 1.
TR38.827 can provide a simple, testable, repeatable framework for spatial channel modelling requirements
  Previous discussions of spatial channel modelling in RAN4 revolved around the 38.901 spatial channel model, which had challenges with complexity and repeatability when used for testing. Now, TR38.827 presents a tuned model that enables alignment between companies and straightforward repeatability.
Widespread support for addressing this topic in Rel-19 was expressed on the RAN reflector in RAN#102
  At RAN4#110 in February 2024, a multi-company proposal was submitted explaining the rationale [1], and extensive technical details were provided in [2].
Observation: RAN1 has developed advanced SU- and MU-MIMO features, and MNOs invest heavily in 5G NR MIMO systems, but performance requirements for MIMO features do not provide confidence in a minimum real-world performance.
Proposal: A spatial component is needed in the channel modelling used in RAN4 for MIMO performance requirements.
[1] R4-2402774, “Channel Models with Spatial Features”, BT, Nokia, Nokia Shanghai Bell, Bell Mobility, CMCC, Deutsche Telekom, Ericsson, Intel, Orange, Telecom Italia, Telenor, Verizon, Vodafone, T-Mobile USA
[2] R4-2402277, “Discussion on 8Rx general demodulation aspects and spatial channel models”, Nokia, Nokia Shanghai Bell, BT

## Slide 3: Scope
Study Item to identify and define practical spatial channel modelling methodology for RAN4 demodulation and CSI reporting requirements
  Use the tuned repeatable spatial channel model of TR38.827 as the basis and identify any necessary changes.
  Methodology shall be applicable to SU-MIMO as well as being extended to be applicable to MU-MIMO.
  Verify test methodology feasibility including test complexity and achievable results uncertainty. The test complexity shall not be significantly increased.
  The methodology shall include both FR1 and FR2
Timescale:
  Start Q3 2024
  Target completion Q1 2025
Notes:
When the study is complete, consider normative work to define performance requirements using the identified spatial channel modelling methodology for:
  8Rx (SU-MIMO) 2-codeword requirements for PDSCH demod, CQI and PMI.
  CQI and PMI (eTypeII) for 4Rx MU-MIMO
Existing performance requirements in previous releases shall not be modified. Enhanced requirements for existing or new cases could be introduced with a UE capability and/or applicability rule to not increase testing load.