## Slide 1: RRM topics for Rel-19
RP-240260
3GPP TSG RAN Meeting #103
Maastricht, The Netherlands, 18th – 21st March, 2024
Agenda Item 9.1.4.4
Source: Nokia

## Slide 2
RRM Enhancements
FR2 L3/L1 measurement delay reduction
One aim when defining the RAN4 Rel-19 package is to ensure a reasonable workload for the RAN4 group.
Workload is easier to manage if Objectives are clear, focused and concise.
RAN4 should be very clear what is included into a WI and Objectives and what is not included.
We suggest following:
  Define concise objectives
  Define focused objectives – better to have for example two focused Objectives than 1 less focused objective.
  Ensure that when ‘and’ and ‘or’ are used in objectives, they are well understood
We suggest following related to this WI:
  Focus on FR2-1
  Decide whether L1 measurements for LTM are included
  Initial focus on SSB-based L3 measurements
  FR2-1 intra-band contiguous and non-contiguous CA.
  FR2-1 SA DC with more than one serving cell in one or more CG.
  Consider scenarios with and without measurement gaps

## Slide 3
RRM Enhancements
FR2 L3/L1 measurement delay reduction
Following Objectives should at least be considered:
  Define FR2-1 L3 measurement delay reduction considering one of:
    Reduced Rx beam sweeping, or
    Enhanced CSSF for connected mode
  For single Rx capable UE, consider FR2-1 intra-frequency measurements for a UE configured with CA and/or DC with more than one serving cell in a CG.
  For Multi-Rx capable UE consider single FR2-1 carrier operation with one single serving cell.
  Following scenarios will be assumed for discussing FR2-1 L3 measurement delay reduction:
    FR2-1 intra-band contiguous and non-contiguous CA.
    FR2-1 SA DC with more than one serving cell in one or more CG.
    Consider scenarios where UE is configured with and without measurement gaps.
  Focus shall be on L3 SSB-based measurement delay reduction.

## Slide 4
RRM Enhancements
FR2 L3/L1 measurement delay reduction
Following Objectives should at least be considered:
  Define FR2-1 L1 measurement delay reduction considering one of:
    Reduced Rx beam sweeping, or
    Enhanced CSSF for connected mode
  For single Rx capable UE, consider FR2-1 intra-frequency measurements for a UE configured with CA and/or DC with more than one serving cell in a CG.
  For Multi-Rx capable UE consider FR2-1 single carrier operation one single serving cell.
Following scenarios will be assumed for discussing FR2-1 L1 measurement delay reduction:
  CSSF for LTM.
  Reduced beam sweeping for FR2-1 L1-RSRP measurements for a cell with different PCI from serving cell.
    L1/L3 sharing factor reduction using Multi-Rx
  Consider scenarios where UE is configured with and without measurement gaps.
  Consider both SSB-based and CSI-RS based measurement delay reduction.

## Slide 5
RRM Enhancements
Fast SCell activation with EMR
Faster SCell configuration and activation after UE enters connected mode leads to significant improvement in offered user throughput and SCell usage:
Rel-18 limitations
  UE measurements are limited by Msg-1.
  Measurement accuracy is unclear as accuracy applies at the measurement instance, which could be a long time before reporting. (MaxValidityTime=100seconds)
  Conditions can change significantly between when UE performs measurements and when UE reports the measurement results.
0-100ms delay is desirable

## Slide 6
RRM Enhancements
Fast SCell activation with EMR
Following Objectives should, at least, be considered:
  Fast SCell activation with EMR
    Ensure that the measurement results reflect the current conditions at reporting, by allowing continued measurements during and after RRC connection setup.
    UE reports the measurement results when these meet the defined measurement accuracies.
      Define related measurement delay requirements.
      Define enhanced measurement accuracy requirements.
  Define related SCell activation delay requirements based on the measurement delay and accuracy requirements.
Following UE measurement scenarios will be assumed:
  UE may use available measurement performed by the UE prior to the connection setup/resume.
  UE may continue performing measurements during the connection setup.
  UE may continue performing measurements after entering connected mode.
  Enhanced measurements are performed at least from connection setup and until reporting.
    Enhanced measurements may use already available and continued measurements.