## Slide 1: Title: Addition of new MSS band for NTN NB-IoT
TDOC#: RP-240264
Source: Iridium Satellite, LLC
Type: Discussion
Document for: Information
Agenda Item: 10.1.5
Release: Rel-19
3GPP TSG RAN Meeting #103
Maastricht, Netherlands, March 18-21, 2024

## Slide 2: Introduction
Iridium operates and 66 Satellites constellation in Low Earth Orbit
The 66 satellites are evenly distributed in six orbital planes with an 86.4 inclination.
100% Global Coverage
L-band to MSS using small form-factor terminals for M2M and personal communications applications
MSS L-band spectrum (1616-1626.5 MHz)
Supports small form-factor terminals for M2M and personal communications applications

## Slide 3: New E-UTRA NTN Band
The aim to create a RAN4 led Rel-19 work item for a new E-UTRA NTN band for Cat NB1, NB2 and M1 addressing class 3 UE and applicable to all ITU regions
This new band [1616-1626.5 MHz] is currently used by Iridium for both uplink and downlink as depicted in the table below:
Table 1 Proposed New Band for NTN NB-IoT
L band for Non GSO Space Segment | Downlink (Space to Earth) | 1616-1626.5 MHz
L band for Non GSO Space Segment | Uplink (Earth to Space) | 1616-1626.5 MHz

## Slide 4: Market Perspective
  Target Markets:
    Applications where traditional satellite is prohibitively expensive, making it impractical to use
    Markets with an existing terrestrial, cellular messaging-based solution that need satellite to increase their market penetration, or to provide failsafe fallback reliability
    Approximately 15% of global cellular IOT market addressable via satellite NB-IOT
    Range of Applications addressable

## Slide 5: 3GPP Benefits to New Band Addition
Near term deployment of NTN NB-IoT services with 100% global coverage
Expansion of the higher availability S/L frequency bands for NTN NB-IoT services
Lower cost/complexity of UE & satellites in future constellations to support NTN NB-IoT service
Harvesting fallow spectrum to increase the available capacity for NTN NB-IoT services
Lower cost of NTN NB-IoT services by reducing spectrum acquisition costs

## Slide 6: Regulatory Context and Co-existence Statement
Iridium is a global operator of the low-earth orbit satellite system providing voice and data services globally. The space segment of the system is authorized by the U.S. Federal Communications Commission (FCC), as the notifying Administration for the Iridium system at the International Telecommunication Union (ITU).
The satellite network was notified with ITU under the name HIBLEO-2 in the 1616-1626.5 MHz frequency band (MSS band). Iridium’s satellite system employs 66 low earth orbit satellites that support user-to-user, user‑to-gateway, and gateway-to-gateway communications.
The Iridium uplink and downlink service links operate in the same frequency band and have been coordinated under the relevant provisions of the Radio Regulations. The assignments were first notified and recorded in the ITU-R MIFR in October 1995.

## Slide 7: Bands with proximity to proposed new band
Frequency (MHz)
Downlink
Uplink
1616
1626.5
1660.5
255 UL
1525
1559
255 DL
1668
1675
253 UL
New Band
UL & DL
1610
254 UL
E‑UTRA Operating Band | Uplink (UL) operating band SAN receive UE transmit |  |  | Downlink (DL) operating band SAN transmit UE receive |  |  | Duplex Mode
 | FUL_low – FUL_high |  |  | FDL_low – FDL_high |  |  | 
256 | 1980 MHz | – | 2010 MHz | 2170 MHz | – | 2200 MHz | FDD
255 | 1626.5 MHz | – | 1660.5 MHz | 1525 MHz | – | 1559 MHz | FDD
254 | 1610 MHz | - | 1626.5 MHz | 2483.5 MHz | - | 2500 MHz | FDD
253 | 1668 MHz | - | 1675 MHz | 1518 MHz | - | 1525 MHz | FDD
NOTE: Satellite bands are numbered in descending order from 256. |  |  |  |  |  |  | 
Reference: 4G Spectrum in TS 36.101 V18.4.0 (2023-12) 5.2-1 E-UTRA operating bands for satellite access
1518
253 DL

## Slide 8: NB-IoT NTN TDD : Technical Issue and Potential Enhancements
Technical issue: NTN variation in latency is dictated by the constellation design and the orbital parameters – intention is to extend a TDD mode for NB-IOT support in NTN.
One-way latency variations, are on the order of 5 msec
This requires to provision a guard time between Tx and Rx transmission of the same scale as the current LTE radio frame (i.e. up to 10 ms)
For efficiency purpose, flexibility of the DL transmission time, guard time, UL transmission time should be enabled by the standard
Potential Enhancements:
Define a semi static TDD slot pattern with multiple of 10 ms, able to accommodate a necessary guard time between DL and UL (possibly > 10 ms)
Configure and signal (e.g. via SIB) transmission opportunities per direction within the TDD slot pattern
Angle | Distance | One-way Delay
90° (above) | 780 km | 2.60 msec
20° (ave) | 1730 km | 5.76 msec
8° (horizon) | 2450 km | 8.16 msec
780 km @ 90°
1730 km @ 20°
2450 km @ 8°

## Slide 9: Relevant applicable standards/regulatory documents for the band definition
ETSI (Europe)
  EN 301 441
  EN 301 481-1
  EN 301 489-20
RED
  EU directive 2014/53/EU
FCC (U.S.)
  47 CFR Part 25
  47 CFR Part 15B
ISED (Canada)
  RSS-170
  RSS-GEN
ETSI EN parameters that could be used to derive 3GPP UE RF parameters:
Transmit Power Levels;
Dynamic Power Control;
Transmitter Modulation Distortion (EVM);
Transmitter Adjacent Channel Power (ACP);
Transmitter In-band Emissions;
Transmitter Out-of-band Emissions;
Receiver Sensitivity;
Receiver Dynamic Range;

## Slide 10: Potential objectives for the L band definition
Assumptions:
UE: PC 3
SAN: Reference scenario Set-1@600 km (See 3GPP TR 36.763)
TDD mode
Potential Objectives:
Specify UE and SAN RF parameters considering requirements defined for bands 254 and 255 specific to TDD configuration (e.g. including transmit ON/OFF, in-band blocking..)
Specify RRM requirements (e.g. timing error..) specific to the support of TDD
Specify test configurations (e.g. FRC, PRACH test preambles..)
Note: Specifications developed for FDD mode of operation in NTN NB-IoT should be leveraged as much as possible.

## Slide 11: Conclusion
We propose the inclusion of a work item (possibly including a study phase) in the Release 19 work plan to:
Proposal 1: RAN to consider as part of its Rel-19 work plan, the definition of a new band for NTN NB-IoT, i.e. [1616 – 1626.5 MHz] which is allocated by ITU to Mobile Satellite Services for both earth-space and space-earth in all three regions.
Proposal 2: For the definition of this new band, Class 3 user equipment and NTN enabled NB-IoT radio interface with Cat NB1, NB2 and M1 should be considered.