## Slide 1: Views on NTN enhancements in Rel-19
3GPP TSG RAN Meeting #103 RP-240318 Maastricht, Netherlands, March 18-21, 2024
Agenda Item: | 9.3.2.3
Source: | Xiaomi
Document for: | Discussion

## Slide 2: Uplink Capacity Enhancement
The following objective was approved for NR-NTN uplink capacity enhancement in RAN#102 plenary meeting[1].
  Uplink Capacity/Throughput Enhancement for FR1-NTN [RAN1, RAN2, RAN4]
    Study then specify, if beneficial, DFT-s-OFDM PUSCH enhancements via Orthogonal Cover Codes (OCC)
      Determine the achievable capacity improvement to be targeted taking into account realistic impairments (e.g. Doppler, time variation, phase distortion, etc)
      Specify necessary signalling, if needed
      Update RF requirements accordingly, if needed
      Note: The study can consider orthogonal cover codes across OFDM symbols, across slots, and/or within an OFDM symbol.
      Note: the study phase is targeted to be completed by RAN#104
    Notes for this objective:
      The enhancement is not targeting improvements/impacts of MU-MIMO capability
      The enhancement is not targeted to PUSCH DMRS
      No enhancement for initial access
      Enhancements to PRACH are not in scope.
      This feature may be applicable for UEs operating in terrestrial networks based on a common design

## Slide 3: Uplink Capacity Enhancement
Motivation
  It has been demonstrated in the current WID that PUSCH during initial access is not included in the current scope of NR-NTN uplink capacity enhancement.
  However, there is still confusion regarding whether MsgA/3 PUSCH during RRC_CONNECTED states, as well as, MsgA/3 PUSCH and CG-SDT PUSCH during RRC_INACTIVE states, are in the current scope.
  Given the limited TU and the complexity of specification efforts, it is better to exclude Msg3 PUSCH and CG-SDT PUSCH from the scope of uplink capacity enhancement.
Proposal
  Clarify that MsgA/3 PUSCH and CG-SDT PUSCH are not included in the current scope of uplink capacity enhancements.

## Slide 4: Summary
According to the proposal in the contribution, we suggest to revise the objective of NR-NTN uplink capacity enhancements in Rel-19 as follows.
  Uplink Capacity/Throughput Enhancement for FR1-NTN [RAN1, RAN2, RAN4]
    Study then specify, if beneficial, DFT-s-OFDM PUSCH enhancements via Orthogonal Cover Codes (OCC)
      Determine the achievable capacity improvement to be targeted taking into account realistic impairments (e.g. Doppler, time variation, phase distortion, etc)
      Specify necessary signalling, if needed
      Update RF requirements accordingly, if needed
      Note: The study can consider orthogonal cover codes across OFDM symbols, across slots, and/or within an OFDM symbol.
      Note: the study phase is targeted to be completed by RAN#104
    Notes for this objective:
      The enhancement is not targeting improvements/impacts of MU-MIMO capability
      The enhancement is not targeted to PUSCH DMRS
      No enhancement for initial access
      Enhancements to MsgA/3 PUSCH and CG-SDT PUSCH are not in scope.
      Enhancements to PRACH are not in scope.
      This feature may be applicable for UEs operating in terrestrial networks based on a common design

## Slide 5: Reference
[1] RP-234078, “New WID: Non-Terrestrial Networks (NTN) for NR Phase 3”, Huawei (Moderator, RAN1 Vice-Chair), 3GPP TSG RAN Meeting #102, Edinburgh, Scotland, December 11-15, 2023
Notes: For PRACH, some companies argues that if only format 2 is used, CE is unnecessary. Is it okay to only use PF2, any disadvantages?

## Slide 6
Thank you