## Slide 1: Proposals on Rel-19 RAN4-led UE RF

## Slide 2: Topics on UE RF Enhancement
High power UE for CA/EN-DC in TN
  References: RP-233918
  Potential objectives:
    High power UE (HPUE) for CA (non-spectrum item for the combinations which need generic requirements)
      PC1.5 UE for intra-band contiguous CA with or without UL MIMO with 2Tx
      PC1.5 UE for two band inter-band CA with 2Tx and/or 3Tx for handheld and FWA
        3Tx specifics: Also PC2?; EN-DC?
      Generic framework of support increasing UE power high limit for inter-band CA HPUE (only for TN) for different power classes
        Do we need a study phase, e.g.. in 2Q’24 (1 quarter)?
    Further discussion on other type of HPUE CA band combinations.
    Further discussion on whether to introduction of HPUE for EN-DC
    Further discussion on whether to introduce PC1.5 for intra-band non-contiguous
Power boosting and/or MPR reduction
  References: RP-233918
  Potential objectives:
    (Ensure reasonable load) Power boosting or MPR reduction for PC2/PC3 with ACLR relaxation with BS indication (Study on whether and how much the requirement can be relaxed first and how often the power boosting can be done, and at least lower modulation order need be studied and FFS on higher modulation order) for FR1 and FR2
      A study phase is necessary
      Is there a need to consider RedCap?
    MPR reduction for UL contiguous CA in FR1/FR2
      How about a single active UL carrier case when CA is configured?

## Slide 3: High power UE for CA/EN-DC in TN
Motivation
  The followings are specified as of now.
  For intra-band contiguous CA in FR1
    Up to PC2 UE is specified with or without UL MIMO
  For intra-band non-contiguous CA in FR1
    Up to PC2 UE is specified without UL MIMO
  For inter-band CA in FR1
    Up to PC2 is specified without UL MIMO
    Up to PC1.5 is specified with UL MIMO targeting FWA
  For inter-band EN-DC in FR1
    Up to PC2 UE is specified without UL MIMO
    Up to PC2 is specified with UL MIMO targeting FWA
  UE power high limit for inter-band CA
  Further coverage enhancement requirement is needed with high power UE for CA/EN-DC in TN.
  Proposed Objectives
  PC 1.5 UE for intra-band contiguous CA with or without UL MIMO with 2Tx
  PC 1.5 UE for intra-band non-contiguous CA without UL MIMO with 2Tx
  PC 1.5 UE for inter-band CA with 3Tx
  PC 1.5 UE for inter-band EN-DC with 3Tx
  Targeting UE type
    Handheld, non-handheld
  Generic framework of support increasing UE power high limit for inter-band CA HPUE (only for TN) for different power classes

## Slide 4: Power boosting and/or MPR reduction
Motivation
  As of now, power boosting is defined for Pi/2 BPSK and QPSK for PC3 in FR1 single carrier considering FDSS
  To enhance UL coverage, power boosting and/or MPR reduction are needed in FR1 with ACLR relaxation for a single carrier and UL contiguous CA
  Propose to focus on FR1 only considering work load and commercial deployment
  Further coverage enhancement requirement is needed with Power boosting and/or MPR reduction
Proposed Objectives
  Study FR1 ACLR relaxation to be allowed for power boosting and/or MPR reduction
  Then, specify the power boosting and/or MPR reduction in FR1 with the ACLR relaxation
    PC3 and PC2 in a single carrier
    PC3 and PC2 in UL contiguous CA / a single active UL carrier
  FR2 requirement can be considered after FR1 requirement is completed,