## Slide 1: Candidate RRM topics for RAN4 Rel-19
China Telecom
2024.03
3GPP TSG RAN #103
Maastricht, Netherlands, March 18-21, 2024
Agenda: 9.1.4.4
RP-240350

## Slide 2: RRM topics
2
  RRM objectives in proposed RAN4-led Rel-19 package summary refer to RP-240019:
  FR2 L3/L1 measurement delay reduction with reduced Rx beam sweeping and enhanced CSSF for connected mode
    FFS on applied scenarios, justification and feasibility on reduced number of Rx beam sweeping
      For single Rx, focus on the case of CA/DC where it is currently specified that the delay is scaled with the number of CCs
      For multi-Rx, focus on the single carrier case
      Other scenarios (if so, clearly defined)?
  Fast Scell activation with EMR with both delay requirements for Scell activation and enhanced measurement accuracy requirements.
    To start from Q3’2024 and aim for completion in Dec’2024
      Workplan for this bullet can be discussed in May’2024
Introduction

## Slide 3: View on L3/L1 measurement delay reduction
  L3/L1 measurement delay reduction
  Justification:
    FR2 L3/L1 measurement delay is much longer than FR1 measurement delay because of UE Rx beam sweeping. In addition, simultaneous reception using Multi-Rx chains is beneficial for FR2 L3/L1 measurement delay reduction.
    The enhancements of Rx beam sweeping were specified in Rel-18, e.g., FR2 unknown SCell activation enhancement, FR2 L1 measurements with multi-Rx, FR2 HST enhancement.
    To further reduce L3/L1 measurement delay in more scenarios, it is beneficial to introduce reduced Rx beam sweeping and enhanced CSSF for L3/L1 measurement delay reduction.
  Objectives:
    Rx beam sweeping number reduction and enhanced CSSF for FR2 L3/L1 measurement delay enhancement [RAN4]
      The solution of enhanced CSSF can be reused for FR1 if applicable.
    Simultaneous reception using Multi-Rx chains for FR2 L3 measurement [RAN4]
    Potential UE capabilities and signaling enhancement to support L3/L1 measurement delay reduction [RAN4, RAN2]

## Slide 4: View on Fast SCell activation with EMR
  Fast SCell activation with EMR
  Justification:
    The delay of unknown SCell activation is much longer than the delay of known SCell activation.
    Measurement results can be used for unknown SCell activation if EMR report is valid when UE enters connected mode.
  Objectives:
    SCell activation delay requirements for Fast SCell activation with EMR [RAN4]
    Measurement accuracy requirements for Fast SCell activation with EMR [RAN4]
    Potential UE capabilities and signaling enhancement to support Fast SCell activation with EMR [RAN4, RAN2]

## Slide 5: Thanks!