## Slide 1
Views on the scope of Rel-19 UE RF topics
Agenda: 9.1.4.1
Source: Samsung
Document for : Discussion and decision
RP-240376

## Slide 2
Baseline Objectives from RAN Chair
  RAN Chair together with RAN4 Chair recently shared their summary for RAN4 Rel-19 Package (non-spectrum proposals) in RP-240019
  In the summary, UE RF enhancements for FR1 and FR2 list as one project with three topics: HPUE for CA in TN (including 3Tx), Power boosting and/or MPR reduction, and 6Rx.
  We observe there are several discussion points especially the yellow-highlighted parts.
    2/6

## Slide 3
HPUE for CA
  HPUE CA band combinations:
    We observed operators have demand to support PC 1.5 for intra-band non-contiguous CA in addition to contiguous CA e.g. band n77(2A).
    Based on the collection from operators for new HPUE scenarios as in appendix, example band combos are suggested as following.
  Proposals 1: Consider follow new HPUE scenarios with example band combos:
    PC1.5 UE for intra-band UL contiguous CA with or without UL MIMO with 2Tx
    Candidate example band combos: n41c, n77c
    PC1.5 UE for intra-band UL non-contiguous CA without UL MIMO with 2Tx
    Candidate example band combos: n77(2A)
  PC1.5 UE for two band inter-band CA with 2Tx and/or 3Tx for handheld and FWA
    Candidate example band combos: n41-n77 (TDD-TDD), n25-n77 (FDD-TDD), n25-n66 (FDD-FDD)
  Generic framework of supporting increasing UE power limit
    Existing RAN4/RAN2 specifications already support UE power class capability as per band, per band combination, and per band per band combination with different capability IEs.
    No strong demand foreseen to further optimize UE power limit reporting schemes given above IEs already covered all scenarios with latest clarifications in RAN4 and RAN2.
  Proposal 2: Study phase required for generic framework of supporting increasing UE power limit with check point at 3Q’24 (6 month study phase)
Observation and Proposals
HPUE for CA
  PC1.5 UE for intra-band UL contiguous CA with or without UL MIMO with 2Tx
    Candidate example band combos: n41c, n71c
    PC1.5 UE for intra-band UL non-contiguous CA without UL MIMO with 2Tx
    Candidate example band combos: n77(2A)
  PC1.5 UE for two band inter-band CA with 2Tx and/or 3Tx for handheld and FWA
    Candidate example band combos: n41-n77 (TDD-TDD), n25-n77 (FDD-TDD), n25-n66 (FDD-FDD)
  Generic framework of support increasing UE power high limit for inter-band CA HPUE (only for TN) for different power classes
    Study phase with check point at 3Q’24
Proposed objectives
    3/6

## Slide 4
Power boosting and/or MPR reduction
Observation and Proposals
  Power boosting or MPR reduction for PC2/PC3 with ACLR relaxation with BS indication (Study on whether and how much the requirement can be relaxed first and how often the power boosting can be done, and at least lower modulation order need be studied and FFS on higher modulation order) for FR1 and FR2
    Study Tx EVM relaxation for higher modulation orders including 64QAM and 256QAM (study only, w/o normative work in rel-19)
Proposed objectives
    4/6
Both ACLR/emission and Tx EVM requirements have impact on UE Tx power limitation.
Tx EVM is the major bottleneck for high modulation orders and large MPR required e.g. 64QAM, 256QAM.
Relaxed Tx EVM and reduced MPR can be applied in Tx side to leverage high modulation order usage and improve uplink performance.
  Proposal 3: Including Tx EVM relaxtion into MPR reduction for study only.

## Slide 5
6Rx
  MIMO layer:
    Rx impairment (Rx EVM) can be bottleneck for supporting combination of number of layers and modulation orders instead of baseband processing.
    It’s challenge to support 6 DL layers under high modulation orders considering the realistic Rx EVM for smartphone.
  Proposal 4: Limit to 4 layers in initial stage, and further study the feasibility of supporting 6 layers
  SRS reporting enhancement
    RAN4 has discussed IL (insertion loss) reporting scheme in previous release without any conclusion.
    IL belongs to UE implementation and it’s hard to harmonize and standardize the reporting scheme.
  Proposal 5: Not consider SRS reporting enhancement.
Observation and Proposals
  Investigate and enable 6Rx on higher frequency bands (>2.5GHz ) targeting at support of smartphone and FWA
  Specify the requirements to support SRS antenna switching
  FFS on the MIMO layer to be supported.
  Limit to 4 layers in initial stage and further study the feasibility of supporting 6 layers
  Further discussions on the following potential objective:
    Improved SRS reporting for antenna switching usage
Proposed objectives
    5/6

## Slide 6
Appendix: New HPUE scenarios
Note 1: For the scenarios marked in gray color FFS whether there is operators’ demand
Note 2: Example band combos collected based on operators’ feedback
Identified new HPUE scenarios for UL CA/DC for Rel-19 consideration