## Slide 1
Views on the scope of Rel-19 OTA topics
Agenda: 9.1.4.3
Source: Samsung
Document for : Discussion and decision
RP-240377

## Slide 2
Baseline Objectives from RAN Chair
  RAN Chair together with RAN4 Chair recently shared their summary for RAN4 Rel-19 Package (non-spectrum proposals) in RP-240019
  In the summary, one OTA testing enhancement WI and one OTA testing enhancement SI are included in the RAN4-led package.
    OTA testing enhancement WI with 2 topcis: TRP/TRS enhancement and MIMO OTA requirements and test enhancement
    OTA testing enhancement SI with 1 topic: FR2 OTA testing enhancement
  We observe still FFS for detailed objectives with candidates from the RAN#102 summary RP-233918
    2/4

## Slide 3
OTA testing enhancement WI
Observation and Proposals
    4/4
TRP/TRS enhancement:
  Rel-18 RAN-P and RAN4 have discussed the treatment on conductive REFSENS and OTA TRS requirements for 2-Rx non-Redcap XR devices on the bands where 4Rx is mandatory. It’s agreed OTA TRS requirements will be specified based on measurement campaign of commercial XR devices. It’s worth to study the test method for XR device types before deriving OTA requirements.
  It’s also worth to study suitable test method and test metric for NTN device type based on demand from the satellite industry.
Proposal 1: Test method for new device types including XR devices and or NR NTN and IoT NTN devices
    Study phase required with check point at 3Q’24
MIMO OTA objective:
  Among all candidate core part objectives, FR1 dynamic channel model is gather widely interesting from companies which also adopted by certification bodies i.e. CTIA.
  Hand phantom was included in Rel-18 WI as study objective which the conclusion that existing QZ size is not feasible.
  We didn’t observe urgent demand for Multi-TRP test scenarios.
Proposal 2: Focus on test method study for dynamic channel model (FR1 only) for MIMO OTA testing enhancement
Study phase required with check point at 3Q’24
Proposed objectives
MIMO OTA objective:
  Core part: MIMO OTA test method under dynamic channel model
    Study phase required with check point at 3Q’24
    Focus on FR1, no performance requirements in Rel-19
  Perf part: FR1 MIMO OTA requirements for operator demanded bands
FR1 TRP /TRS objective:
  Core part: Test method for new device types including XR devices and/or NR NTN and IoT NTN devices
    Study phase required with check point at 3Q’24
  Perf part: TRP TRS requirements for operator demanded bands

## Slide 4
OTA testing enhancement SI
Observation and Proposals
    4/4
Test method Multi-Rx UE was studied and specified in Rel-18 together with core/performance requirements in separate SI and WI. And some RF requirements were specified for STxMP scenario under Rel-18 MIMO WI.
It’s desirable to study and specify test method for STxMP scenario based on the study conclusion in Rel-18 FR2 test SI for multi-Rx scenario.
Proposal 3：Study and specify Test method for STxMP for non-handheld UE