## Slide 1
Views on the scope of Rel-19 RRM topics
Agenda: 9.1.4.4
Source: Samsung
Document for : Discussion and decision
RP-240378

## Slide 2
Baseline Objectives from RAN Chair
  RAN Chair together with RAN4 Chair recently shared their summary for RAN4 Rel-19 Package (non-spectrum proposals) in RP-240019
In the summary, RRM enhancements list as one project with 2 topics: FR2 L3/L1 measurement delay reduction and Fast Scell activation with EMR.
  We observe there are several discussion points especially the yellow-highlighted part for spatial channel model.
    2/3

## Slide 3
FR2 L3/L1 measurement delay reduction
Observation and Proposals
    3/3
In previous releases, optimization of RRM requirements with reduced beam scaling factor was specified under specific deployment scenario i.e. FR2 HST deployment.
It’s desirable to further study and enhance FR2 RRM delay requirements with identified specific scenarios and precondition.
Proposal 1: Consider follow additional scenarios on FR2 L3/L1 delay reduction
  Study suitable scenarios and conditions to decrease the measurement delay in FR2 with reduced beam scaling factor [RAN4]
    Example scenarios for study: Low mobility scenario, fixed indoor scenario and multi-TRP scenario with prediction on candidate beam directions
Phase I: Study phase
Study suitable scenarios and conditions to decrease the measurement delay in FR2 with reduced beam scaling factor [RAN4]
  Example scenarios for study: Low mobility scenario, fixed indoor scenario and multi-TRP scenario with prediction on candidate beam directions
Note: Check point at Q3’24 for phase I.
Phase II: Specify enhanced FR2 measurement requirements pending on phase I conclusion
Specify the measurement delay in FR2 with reduced beam scaling factor under the identified scenarios [RAN4]
Specify necessary NW assistant signaling and UE capability signaling [RAN4, RAN2]
Proposed objectives