## Slide 1
Views on the scope of Rel-19 demodulation topics
Agenda: 9.1.4.5
Source: Samsung
Document for : Discussion and decision
RP-240379

## Slide 2
Baseline Objectives from RAN Chair
  RAN Chair together with RAN4 Chair recently shared their summary for RAN4 Rel-19 Package (non-spectrum proposals) in RP-240019
  In the summary, Demodulation performance requirement enh. list as one project with 2 topics: UE performance requirements with MMSE-IRC for 8Rx，MMSE-IRC receiver for uplink.
  We observe there are several discussion points especially the yellow-highlighted part for spatial channel model.
    2/4

## Slide 3
MMSE-IRC receiver for uplink
Uplink inter-cell interference scenario is typical scenario for FR1 NR deployment. The interference is even severe compared to LTE due to HPUE widely deployed in NR network.
Similar as MMSE-IRC receiver test cases specified for downlink side in NR, we suggest to focus on data channel and slot aligned scenario in the initial stage.
LTE interference profile as captured in TR can be used as staring point with further evaluation on suitable interference profile for NR deployment.
Proposal 1: Focus on PUSCH demodulation requirements and slot aligned scenarios
Proposal 2: Using LTE interference profile from TR 36.884 as staring point and further evaluate applicable profile for NR deployment scenarios
Observation and Proposals
Specify advanced receiver for suppressing uplink inter-cell interference (FR1 only)
    Define PUSCH demodulation requirements
    Reference receiver: MMSE-IRC with DMRS based interference covariance estimation
        Note: use the DMRS for served target UE’s PUSCH.
    Reuse LTE interference profiles from TR 36. 884 as starting point
      Further evaluate applicable profiles for NR deployment scenario
    Focus on slot-based transmission and aligned SCS among cells
Proposed objectives
    3/4

## Slide 4
Channel model with spatial component
Observation and Proposals
    4/4
It’s unclear for the motivation of introducing channel model with spatial component for performance requirements.
LTE and NR performance requirements (both BS and UE side) are specified based on the methodology of TDL channel + MIMO correlation matrix starting from Rel-8.
No critical issues were identified from network deployment for above methodology.
It’s undesirable to conduct new test methodology and channel model i.e. CDL channel model for introducing new performance requirements in late stage of NR.
Proposal 3: Clarification is necessary regarding the need and timeline the channel model with spatial component
  If there is need, study feasibility to introduce spatial component based TDL channel model with extension in Rel-19
  Postpone CDL channel model study to future release