## Slide 1: Scope discussion on Enhancements of Network energy savings for NR
Sources: Panasonic
3GPP TSG RAN #103
Maastricht, Netherlands, March 18-21, 2024
Agenda: 9.3.1.5
TDOC: RP-240409
For: discussion

## Slide 2: Background
Objective of Enhancement of NES is following in RP-234065
Specify procedures and signaling method(s) to support on-demand SSB SCell operation for UEs in connected mode configured with CA, for both intra-/inter-band CA. [RAN1/2/3/4]
  Specify triggering method(s) (select from UE uplink wake-up-signal using an existing signal/channel, cell on/off indication via backhaul, Scell activation/deactivation signaling)
  Note1: On-demand SSB transmission can be used by UE for at least SCell time/frequency synchronization, L1/L3 measurements and SCell activation, and is supported for FR1 and FR2 in non-shared spectrum.
Study procedures and signaling method(s) to support on-demand SIB1 for UEs in idle/inactive mode, including: [RAN1/2/3]
  Triggering method by uplink wake-up-signal using an existing signal/channel.
  Wake-up-signal configuration provisioning to UE
    Note: No modification of SSB will be discussed under this objective
  Information exchange between gNBs at least for the configuration of wake-up signal, if necessary.
  Checkpoint for normative work in RAN#105
Specify adaptation of common signal/channel transmissions. [RAN1/2/3/4]
  Adaptation of SSB in time domain, e.g. adapting periodicity
  Adaptation of PRACH in time domain
  Study adaptation of PRACH in spatial domain, e.g. non-uniform PRACH resources per SSB, and specify if found beneficial
    This study is to be done in 2Q’2024 only
  Adaptation of paging occasions including confining the paging occasions in the time domain
    Note: there shall be no paging latency increase
  Note: there shall be no negative impact to legacy UEs, unless significant benefits are shown

## Slide 3: Discussion
Obj#2 deals with on-demand SIB1 for idle/inactive mode, while obj#3 deals with SSB, PO and PRACH.
  Joint discussion among SIB1, other SIBs, SSB, PO and PRACH would lead unified/simplified design with better NES gain.
Single cell deployment with SIB1, SSB, PO and PRACH modification would not be backward compatible for legacy UEs.
  Focus on multi-cell deployment i.e. cell A and NES Cell.
  Backward compatibility is covered by cell A.
NES Cell
Cell A

## Slide 4: Discussion
Resource of IDLE/INACTIVE UEs does not scale to the number of camped IDLE/INACTIVE UEs so much. Constant overhead is required even no camped UEs.
  IDLE/INACTIVE UEs should be accumulated to Cell A with backward compatible manner.
Resource of CONNECTED UEs changes dramatically based on the traffic situation and its situation is basically known by NW.
  NES Cell should focus CONNECTED UEs for maximizing NES gain.
 | Legacy UEs | New UEs
Cell A | IDLE/INACTIVE/CONNECTED | IDLE/INACTIVE/CONNECTED
NES Cell | Not supported | CONNECTED

## Slide 5: Discussion
In order to have cell densitification gain, NES cell coverage can be part of Cell A. i.e. multiple NES Cells in Cell A coverage.
  Which NES Cell should be “ON” needs to be known to network. i.e. periodic signal may be required for NES Cell. NES Cell should be detectable by UEs.
In order to maximize NES gain, no periodic signal from NES Cell case should be also supported.
  Cell A and NES Cell are same coverage, which is one of typical deployment of carrier aggregation.
For NES gain of quick adaptation, Cell A and NES Cell should share same MAC i.e similar condition with carrier aggregation. This can reduce TU load.
Cell A
NES Cell
NES Cell
Cell A

## Slide 6: Proposal
Joint discussion among SIB1, SSB, PO and PRACH i.e. joint discussion of obj#2 and obj#3.
Focus on multi-cell deployment
  IDLE/INACTIVE UEs should be accumulated to Cell A with backward compatible manner.
  NES Cell should focus CONNECTED UEs for maximize NES gain.
  NES Cell coverage can be same or part of Cell A coverage.
  For NES gain of quick adaptation, Cell A and NES Cell should share same MAC i.e similar condition with carrier aggregation. This can reduce TU load.