## Slide 1: RAN4 Rel-19 demodulation topics
Ericsson
RP-240484

## Slide 2: Summary
According to the proposed summary in RP-240019, 3 topics are under consideration for Rel-19 demodulation enhancements:
  UE performance requirements with inter cell and with intra-cell inter-use interference for 8Rx CPE/FWA/vehicle/industrial devices
  MMSE-IRC receiver for uplink taking LTE interference profile as starting point.
  Channel model with spatial component for performance requirements
This package is in general reasonable, in our view it is very important to start the study on the channel model.

## Slide 3: UE performance requirements with inter cell and with intra-cell inter-use interference
This follows on from the Rel-18 8RX requirements
  Target is CPE/FWA etc.
Re-use interference profiles used for Rel-17 requirements
Work is not expected to be large; 2 or 3 quarters

## Slide 4: BS MMSE IRC receiver
In our view, the requirement is not essential
  AAS BS have more than 8 receivers, which is the limit for conducted performance testing (or 2 receivers, which is the testing limit for OTA). Thus, the requirement will not bear any relation to AAS UL beamforming performance.
  IRC receivers are already widely deployed with good performance
A potential argument is that HPUE deployment may increase in low bands
The scope for the IRC receiver should be focused on inter-cell UE interference, considering also HPUE

## Slide 5: Spatial channel model
MIMO schemes are growing in dimension and complexity
The current TDL channel model does not test whether the receiver exploits spatial diversity well to optimize performance
The CDL channel model has been parameterized in TR 38.827 such that it is reproducible and testable
It is important to move towards better spatial channel models. At least a SI should be commenced to check the viability of the model in 38.827, and that testing of a spatial channel model can be achieved with reasonable complexity.
This is essential for maximizing performance benefits from advanced MIMO systems