## Slide 1: NTN non-spectrum for Rel-19 RAN4
RP-240485

## Slide 2: Overview
The recommendation in R4-240019 proposes the following areas for NTN:
  HPUE
  NGSO channel model and test framework
  Less than 5MHz channel bandwidth
  In-band co-existence with NR NTN

## Slide 3: HPUE
HPUE for PC2 is considered for both NR and NB-IoT.
  Note PC2 NB-IoT is not defined in TN specs
PC2 may be handheld or non-handheld.
In case other power classes (PC1.5, PC1) are included, non-handheld should be considered for those
Co-existence should be checked for PC2
PC1 and PC1.5 need co-existence studies.
  Based around similar parameters and scenarios to existing work.
  It is OK to include them, but there should be a clear motivation.

## Slide 4: Performance requirements for NGSO
Requirements need to consider Doppler and time-shift to enable better test coverage

## Slide 5: Less than 5MHz bandwidth
Re-use TN 3MHz design to the greatest extent possible.
It is not clear that a significant study phase is needed if the specifications are exactly the same as for 3MHz TN.
  One thing to clarify is whether the same sync raster design can be used in Satellite bands as currently defined
  If new raster points are needed then a RAN1 checking of k_ssb, Offset_RB applicable for the raster points may be needed.
  Another is whether the 12PRB is really needed

## Slide 6: In-band NB-IoT
- This can be incorporated into the NTN specs in a similar manner to TN