## Slide 1: Fragmented carriers in the DL A proposal for Rel-19 study item RAN #103
TELUS, Bell Mobility, Nokia, Nokia Shanghai Bell, Telstra, T-Mobile USA, US Cellular, Spark NZ Ltd, Southern Linc, AT&T

## Slide 2: Background
The maximum number of component carriers (CCs) in a Carrier Aggregation (CA) combo is limited by the number and capabilities of the analog Rx chains in the UEs
As a result, it is not expected that the number of CCs that chipsets support will go up significantly in the coming years (6 or 7 is likely the limit in the FR1 range)
Today, fragmented carriers in the same band consume multiple Rx chains, thus limiting the CA capabilities
We propose studying the use of fewer Rx chains than carrier fragments in a band which could result in freeing up Rx chains for additional component carriers
This restriction exists only in the RF domain as some chipset vendors have already demonstrated that fragmented blocks require the same number of baseband processing units as single non-fragmented blocks (e.g., 7A-7A requires single downlink processing unit, same as 7A)

## Slide 3: Example of fragmented blocks in FR1 mid-bands in Canada
PCS (n25) example of fragmented spectrum in Toronto*
BRS (n7) example of fragmented spectrum in Toronto*
AWS1/3/4 (n66) example of fragmented spectrum in Toronto*
*Same colour indicates spectrum access for the same operator; each block is 5 MHz wide

## Slide 4: Example of fragmented blocks in FR1 low-band in Australia
*Same colour indicates spectrum access for the same operator; each block is 5 MHz wide

## Slide 5
Study Item Proposal
Study Item to identify a solution for minimizing the number of UE Rx chains needed for intra-band non-contiguous CA
Objective:
  Study methods by which a UE can dynamically switch the number of Rx chains (one or two) needed for a single DL band of ≤ 100 MHz within a CA combination, considering
    ACLR implications
    The near-far problem
RAN4 led item with minimal RAN2 impact and no RAN1 impact is foreseen
Timescale:
  Start Q3 2024
  Target completion Q2 2025

## Slide 6: Proposed solution example
In the example below, currently 6 Rx chains are needed, thus precluding additional CCs to be added (assuming a 6 Rx limit)
Our proposal is to implement this dynamically using 3 to 6 Rx chains
This would enable 10+ CCs combo implementation for much higher speeds
PCS
AWS
BRS
2 Rx / 2 CCs
Current count:
2 Rx / 2 CCs
2 Rx / 2 CCs
Total: 6 Rx chains / 6 CCs
Rx / 2 CCs
Proposed count:
Total: Rx chains / 6 CCs
Rx / 2 CCs
Rx / 2 CCs