## Slide 1: Satellite Operator views on OTA requirements for NTN
Inmarsat, Viasat
3GPP TSG RAN #103
March 18 - 22, 2024, Maastricht/The Netherlands
Agenda: 9.1.4.3 - Proposals led by RAN4 (not spectrum related), Candidate OTA topics
TDOC: RP-240615
For: discussion

## Slide 2: OTA Radiated Requirements for FR1-NTN
  Background:
  Current 3GPP RF Requirements for FR1-NTN bands are conducted only
  As we see initial UE implementations come to the market, there is a big variability in the quality of antenna implementations and resulting performance
  Usage assumptions are often very different from TN (e.g. no indoor coverage, predominantly LoS operation)
  In many cases, UE is aware of user behavior and is capable of estimating satellite direction, which could be used for beamforming in handheld (or non-handheld) UE capable of tracking the satellite by beamforming with multiple antenna elements, in cooperation with the Network
  Antenna performance and coverage assumptions (e.g. spherical vs directed bias) are crucial for NTN!
  There is a need to study and identify OTA RF characteristics and performance requirements for NTN

## Slide 3: NTN Antenna Bias
Key factors:
UE elevation angles for NTN are typically >20°, in majority of cases.
TRP, TRS, EIS – do not consider directivity – single value is used – this may be insufficient for NTN especially when the link margin is very small – having a higher gain in the upper hemisphere of the antenna pattern is very beneficial.
Benefits:
For fixed UE (even without tracking antenna) – antenna can be quite directional, with bias given to the upper hemisphere with no system performance penalty.
For handheld/smartphone UE – UE may be upside-down when a call is initiated (e.g. in pocket):
  If we assume only synchronization and paging typically occur when UE is upside down, we can still sacrifice some antenna performance on the bottom hemisphere, due to lower SNR requirements for the physical channels associated with these procedures.
  When data transfer is occurring– e.g. PUSCH/PDSCH and the UE is pointing upwards, it is advantageous to have a higher antenna performance in the upper hemisphere to allow for a higher link margin.
  This would also reduce the antenna noise temperature, meaning the system noise is less significant, which increases G/T, increasing the DL link margin, while increasing the UL margin due to higher gain towards the satellite orbital arc.
Assessing the directivity of the antenna can be done with a similar effort level to obtaining the TRP, TRS and EIS values, and would allow for more detailed link level analysis.

## Slide 4: Proposals
Proposal 1: Study and identify applicability of OTA requirements for FR1-NTN use cases
  Consider a sufficiently open framework, allowing use cases / antenna classes for different UE to have different requirements and constraints which are optimized for NTN:
    From low-gain omni handheld UE to potential future high gain, highly directional FR1 VSAT-like terminal with multiple antenna elements.
  Transmitter Antenna requirements (TX):
    Antenna Gain Plot at Tx Frequencies (dBi)  for NTN, to include some directivity requirements for the antenna, allowing an optimized Tx antenna design for an NTN UE – Includes antenna efficiency, and TRP can be derived from antenna gain with a similar amount of effort to the TRP measurement.
  Receiver Antenna requirements (RX):
    Antenna-Gain-to-Noise-Temperature (G/T)  for NTN, to include some directivity requirements for the antenna, allowing an optimized Rx antenna design for an NTN UE, also incorporates system noise parameters.
    Antenna Gain Plot at Rx Frequencies (dBi)  same as above – can be used to derive G/T and TRS, so long as REFSENS is known.
  General Antenna Requirements
    Introduction of a singular ‘antenna bias’ parameter would allow a quick assessment of the weighting of the antenna beam pattern, with requirements derived from a trade-off between antenna gain requirements and system noise requirements.
Proposal 2: Consider UE capability to perform simple beamforming with multiple antenna elements based on knowledge of satellite location

## Slide 5: Thank You!