## Slide 1: Operator Proposal for 2Rx for XR REFSENS
T-Mobile USA, Telstra, Spark, Vodafone, Telecom Italia, Inmarsat, Viasat, Deutsche Telekom, Telia Company, Odido, Telenor, Telefonica, CMCC, AT&T, Orange, BT, Anterix, TELUS, Southern Linc, UScellular, CHTTL, SK Telecom, China Unicom, KPN, Rogers
3GPP TSG RAN Meeting #103 RP-240649
Maastricht, Netherlands, March 18-21, 2024

## Slide 2: Overview
Background
Summary of RP-230681
Current situation
Data supporting the operator position on 2Rx meeting the 4RX REFSENS requirement
XR form factor challenges
Proposals for 2Rx XR REFSENS

## Slide 3: Background
Higher frequency bands have 4Rx mandatory to improve performance and user experience
There is a proposal to relax the requirement from 4Rx to 2Rx for bands that mandate 4Rx for XR devices
Many operators from around the globe have vehemently opposed relaxing the requirement from 4Rx to 2Rx for the 6 GHz licensed band on the grounds that it would lower spectral efficiency and capacity, and the value of their spectrum
The XR WID includes “Specify the enhancements related to capacity” so changes that would reduce capacity would seem to run counter to the goals of the WID
It looks like 2Rx XR is inevitable, so now the questions are if barring is the default or not and what the REFSENS and OTA performance will be.

## Slide 4: Summary of RP-230681: There would be a large impact to network throughput for UEs with 2Rx instead of 4Rx
At RAN#99 in March of 2023, several operators co-sourced RP-230681 summarizing our concerns about 2Rx for XR in bands where 4Rx is currently mandatory.
RP-230681 showed that there would be a large impact to network throughput for UEs with 2Rx instead of 4Rx based on drive test results by Signals Research Group
RP-230681 asked if the smartphone might go the way of the pager. More recently, in a review in the Wall Street Journal on January 30th, a reviewer referred to a mixed-reality headset as the company’s “boldest bet yet on the post-smartphone future.”
RP-230681 pointed out that user experience isn’t only based on device form factor, but also on network capacity, throughput and reliability.

## Slide 5: Current 2Rx XR situation
RAN2 has endorsed two 2Rx XR CRs: One with 2Rx XR UEs barred by default, and another with 2Rx XR UEs are not barred by default.
RAN4 has endorsed a 2Rx XR CR with TBD for the conducted REFSENS
  Several operators proposed that 2Rx XR UEs meet the 4Rx conducted REFSENS, which is 2.2 or 2.7 dB improvement over the current 2 Rx requirement depending on the band
  Several vendors proposed a 0.5 dB improvement for 2Rx XR UEs compared to the current 2Rx conducted REFSENS.

## Slide 6: Why some operators feel that 4Rx REFSENS is reasonable for 2Rx XR UEs
The testing data presented in R4-2403676 showed that every device tested had at least one port that could meet the 4Rx REFSENS requirements with a single Rx chain for n41
The data also showed that every port of every device tested could meet the 2Rx REFSENS with a single Rx chain (-84.5 dBm @100MHz) for n41
While only two of the device models had n77, the data showed that every port of every device tested could meet the 4Rx REFSENS with a single Rx chain (-87.2 dBm @100MHz) for n77
While not a large sample size, the data suggests it would be reasonable to require 2Rx XR UEs to meet the 4Rx REFSENS requirement

## Slide 7: Further discussion
During the discussions at RAN4#110 in Athens, some vendors stated that it would be more difficult to achieve the same conducted REFSENS performance in XR devices than in smartphones because of the more challenging form factor.
The operators responded that this is another reason for concern, because we might not only lose the 2.2-2.7 dB performance for 2Rx REFSENS compared to 4Rx if the 2Rx XR REFSENS isn’t tightened, but we may end up losing 5 to 7 dB relative to smartphones in the same band if in addition the XR UEs are not exceeding the REFSENS requirements as much as smartphones do because of the more challenging form factor.

## Slide 8: Proposal
We propose that the conducted REFSENS for 2Rx XR UEs is equal to the 4Rx REFSENS requirement