## Slide 1
Views on Rel-20 Ambient IoT
RP-250073
3GPP TSG RAN #107
Incheon, Korea, March 12-14, 2025
Agenda: 15.2.3
Source: Samsung
Document for : Discussion and decision

## Slide 2
Background
RANP-106 outcome
Workplan for Rel-20: (RAN#106) Includes D2T2 Includes Device 2 A limited number of additional use cases, deployments, connectivity topologies, devices, traffic types in TR38.848 as a starting point Note: work on D2T2, device 2 shall follow the Rel-19 study conclusions, and further down-selection of architecture options for topology 2 may be needed. For indoor use cases, deviations from Rel-19 study conclusion shall be well justified and agreed. Details to be discussed at a later RAN plenary meeting, including the need for study phase.
Samsung’s view
  In general, we are supportive of the above RAN#106 outcome, i.e., inclusion of D2T2 and Device 2 in Rel-20 scope.
  Additional use cases, deployment and topology options should be limited considering Rel-20 workload.

## Slide 3
Discussion
Device types
  Our view is to support both device type 2a and 2b.
    Device type 2a has minimal specification impact (e.g., solutions for extending device operation time, which is also for 2b) from Rel-19 specification, as it is not much different from device type 1 as both are passive type devices.
    Device type 2b for extending coverage. Possibly also for outdoor scenario with T2 (intermediate UE reader).
  Our view is do NOT support device type 2c, aka Type C, with a few mW power consumption
    Device type 2c would require a fundamentally new design from Rel-19 and may not be an ambient power device, i.e., infeasible via energy harvesting.
    It will be better to be handled in 6G LPWA work.
Additional scenarios/topologies
  Our view is to support T2(intermediate UE reader) for D2(device indoor, BS outdoor), and D4(device outdoor, BS outdoor) for extending coverage and business use cases.
  We do not prefer T4 (standalone UE reader).

## Slide 4
Discussion
Extending device operation time
  Our view is to support device unavailability direction 2 and also energy status report.
  Solutions for extending device operation time would be necessary for device 2a/b.
Additional use cases and traffic types
  We are open to further discuss additional use cases, e.g., positioning, and DO-A traffic type.

## Slide 5
Proposal
Proposal: Consider the following scopes for Rel-20 A-IoT
  Support of device type 2a/2b
  Support of T2(intermediate UE reader) for D2(device indoor, BS outdoor) and D4(device outdoor, BS outdoor)
  Support of DO-A traffic
  Support of extending device operation time, i.e., unavailability direction 2
  Support of co-existence solutions for A-IoT and NR, including interference control/mitigation
  Support of energy status, message size indication
  Further discuss additional use cases