## Slide 1
Overview on Rel-20 RAN4-led 5G-Advanced Scope
RP-250104
3GPP TSG RAN #107
Incheon, Korea, March 12-14, 2025
Agenda: 15.3
Source: Samsung
Document for : Discussion and decision

## Slide 2
Samsung prioritized Rel-20 RAN4-led 5G-A scope
UE RF (incl. RAN4-centric NTN)
  FR1 UE RF enhancement:
    NR FR1 DL fragmented carriers or Low-Low Band CA via switching enhancement
  Irregular Channel Bandwidth: 6MHz
  RAN4-centric NTN: HPUE, CA, etc.
RRM-centric enhancement
  CA RRM enhancement
  FR2 Multi-TX and Multi-RX
Demodulation study
  Further study on Spatial Channel Model (SCM)
AI/ML-assisted receiver (cross-area)
  New use cases with AI/ML-assisted advanced receiver
    AI/ML for Non-linear Compensation
    AI/ML for Channel Estimation

## Slide 3
UE RF – FR1 UE RF enhancement
NR FR1 DL fragmented carriers
Rel-19 WI: to enable low band carrier aggregation via switching:
Rel-20 WI proposed objectives:
Low-Low band CA via switching enh.
  Switching between {case 1, case 2}
    - Case 1: Tx/Rx on FDD carrier 1 and no Rx on SDL carrier 2
    - Case 2: Rx on SDL carrier 2 and no Tx/Rx on FDD carrier 1
  Only a semi-static switching pattern based on RRC configuration
  For FDD + SDL low-band carrier aggregation CA_n5A-n29A.
  Constraints by: <1GHz; co-located/sync network; single TAG; 15kHz SCS
  Extend Rel-19 “switched single DL” to other FDD+SDL combo, if any.
  Specify RF/RRM requirement for “dual DL” case:
    - For FDD+SDL combination n12+n29 and/or n28+n67;
    - Reuse the existing Rel-19 semi-static switching pattern design.
  Minimize RAN1 impact by precluding dynamic switching (e.g., DCI-based)
Rel-19 SI status:
Rel-20 WI proposed objectives:
  Identified methods to reduce the number of UE Rx Chains
  Studied the impacted requirements (Limit to 2 CC intra-band NC CA)
  Studied the ability to semi-statically switch hardware resources
  Specify the RF requirements, based on Rel-19 concluded RF architecture:
    - RIBNC shall be specified base on the specific Wgap configuration.
  Specify trigger condition of “fragmented” and “legacy” mode switching
  Specify RRM requirement for in-gap interference measurement, interruption, and other impacted RRM requirements if any.
  Note: Band combination examples can be CA_n2(2A), CA_n66(2A).
General principle: UE RF topics shall be selected to “address real and critical commercial deployment needs* ”.
Identified demands from operators: (a) NR FR1 DL fragmented carriers and (b) low-low band CA via switching enhancement.
  Proposal: FFS prioritization between these 2 proposals, based on operator’s preference, implementation impact and benefits.
  *Quoted from RP-242438: “Release 20 for 5G-Advanced … to ensure all approved items address real and critical commercial deployment needs”

## Slide 4
UE RF - Irregular Channel Bandwidth: 6MHz
Background: Efficiently utilize spectrum is strongly requested given the large investment especially in low band spectrum.
Background for Irregular Channel BW
  The support of irregular channel bandwidth are studied in Rel-18 with identified solutions,
    - i.e., using larger channel BW than licensed BW, overlapping UE channel BWs, combined UE CBW and overlapping CA.
  3MHz was introduced in Rel-18: 8/13MHz can be achieved via CA.
  In RAN#116 a new WID [RP-243323] approved for 7MHz CBW for n5/n26, and guidance on future irregular CBW handling (including 6MHz per operators’ request) is endorsed in [RP-243322]:
6MHz irregular channel bandwidth:
  Identified demands from operators on 6MHz irregular channel BW;
  Expected minimum standardization effort by reusing conclusion from 7MHz irregular channel BW.
Rel-20 WI proposed objective:
6MHz Irregular Channel BW
  Generic core requirements to support 6MHz:
  - for bands: n29, n5, n12, n85, n28
  - only include 15kHz SCS
  - UE/BS RF requirements for UL and DL
  Band-specific requirements including REFSENS, A-MPR when needed
  Optional UE support of 6 MHz channel bandwidth from Rel-15 onwards in a release independent manner.
  Corresponding RAN2/3 specification impact.
Additional irregular channel bandwidth work, including 6 MHz channel bandwidth, will be deferred to Release 20 for possible consideration.
Other than 6 and 7 MHz, it is agreed that no other new irregular channel bandwidths will be created for FR1 in the future.
  For other “irregular” channel bandwidths, operators will use the overlapping carrier or next wider channel bandwidth approaches.
Band (s) | Channel Bandwidth(s)
n5 | 6, 11, 12 MHz
n12, n85 | 6, 12 MHz
n28 | 13 MHz
n29 | 6, 11 MHz

## Slide 5
UE RF - RAN4-centric NTN
NTN HPUE
Background:
Proposed objective for Rel-20 NTN CA:
Proposed objective for Rel-20 adv. VSAT:
NTN CA and Adv. VSAT
Rel-19 WI status:
Proposed objectives for Rel-20 NTN HPUE:
RAN4-centric NTN topics identified in Rel-20 5G-A:
  Potential remaining scope for NTN HPUE, and new scope for NTN CA and advanced VSAT requirements.
  Feasibility study and specify RF requirements for PC 1.5/PC 1 for hand-held NR-NTN and IoT-NTN devices;
  Feasibility study and specify RF requirements for higher power classes than PC1 for hand-held and non-handheld NR-NTN and IoT-NTN devices.
  Specify CA for NR-NTN for intra-SAN scenarios, where component carriers are co-located in same SAN;
  Support intra-band and inter-band CA, for UL and DL CA.
  NTN CA is demanded by satellite operators in both Ku-band and FR1-NTN bands, which is dropped in Rel-19 Ku-band WID.
  Advanced VSAT features are demanded by satellite industry, e.g., NGSO ESIM (mobile VSAT).
  Specify RF and RRM for NGSO mobile VSAT in Ku-band and Ka-band;
  Study and specify new VSAT antenna types, e.g., ‘Flat’ antenna, and VSAT with multiple antennas for FR2-NTN
  Progress achieved on Rel-19 RAN4-led WI for NR NTN and IoT NTN for non-handheld UE, while handheld HPUE is deprioritized;
  Expected study is desired on GSM PA possibly support 1Tx PC1 and IoT NTN [33] dBm handheld UE, based on operator's interests.

## Slide 6
RRM-centric enhancement
CA RRM Enhancement
FR2 Multi-TX and Multi-RX
RRM-centric enhancement topics are identified for Rel-20 5G-A:
  CA RRM enhancement: Even faster SCell activation, and RRM support for uplink only SCell;
  FR2 Multi-TX/RX: Remaining RRM requirement to enable UL STxMP and enhanced DL Multi-RX.
Even faster SCell activation
RRM support of Uplink Only SCell
  Justification:
    - CA deployment demands for UL only SCell, i.e, the necessity is identified to enhance the uplink spectrum efficiency and flexibility.
  Proposed objectives:
    - To specify RRM requirements including timing, SCell activation.
  Justification: SCell activation can be even faster than previous releases.
  Proposed objectives:
    Specify RRM requirement for faster SCell activation by:
      (1) enhanced meas. before SCell activation command reception;
      (2) improved known condition for SCell.
Justification for enhancement to support FR2-1 FWA:
FR2 Multi-TX:
FR2 Multi-RX:
  Proposed objective to enable UL STxMP*:
    - Necessary RRM requirement to support simultaneous multi-panel UL transmission to 2 TRPs, targeted for CPE/FWA devices.
  Proposed objective for supporting enh. simultaneous DL reception:
    - To specify necessary RRM requirements to support Rel-17/Rel-18 unified TCI state framework;
    - To specify necessary RRM requirements to support inter-cell multi-TRP scenario.
Source Cell
Cell with different PCI from serving cell
  FWA is identified as one of the most successful business use cases for mmWave deployment, especially in North America market.
*STxMP: Simultaneous transmission across multiple panels

## Slide 7
Rel-19 SI scope for study
Observations on Rel-19 SCM study (till RAN4#114):
Demodulation
Rel-19 SCM SI status
Rel-20 Scope for SCM further study
Further study on Spatial Channel Model (SCM):
  SCM channel shall be further studied for potentially not completed scope, AI/ML use case, etc.
  Scenarios identified to be studied, but not yet covered:
    SU-MIMO and MU-MIMO
    FR1 and FR2, TDD and FDD, DL and UL
  Methods identified to be studied, but not yet covered:
    CDL-based methodologies: TR38.827 based or TR38.901 based
    TDL based Methodologies: Introduce spatial component
  Rel-19 study is expected to only cover:
    FR1 TDD DL SU-MIMO UMa scenario based on TR38.827 CDL-C.
Rel-20 SI proposed study objectives:
  Further study on SCM impact on demodulation performance by considering testability and test repeatability.
  Study the scenarios, at least including MU-MIMO, FR2, UL, FDD.
  Study the performance impact on Rel-19 AI/ML use case with SCM, e.g. AI-CSI prediction test cases (expected to use TDL model in Rel-19).
  Study the performance impact by introducing possible extension for ISAC.
SNR working point for 70% maximum TP, 4Tx4Rx 4layer, 30kmh |  | 
 | CDL Option 1Y Antenna Configuration (8,2,2,8,1) | CDL Option3 Antenna Configuration (1,2,2,1,1)
Nokia | 20.0dB | N/A
BT | 14.3dB | N/A
Ericsson | 3.9dB | 18.3dB
Samsung | 18.4dB | 18.1dB
MediaTek | 17.8dB | 17.5dB
Huawei | 17.2dB | 15.1dB
ZTE | 11.2dB | 20.6dB
Apple | n/A | 19.9dB
  Misaligned simulation results among companies, even with same assumption.
  CDL-based SCM studied in RAN4 is hardly to be claimed as “calibrated”.

## Slide 8
AI/ML-assisted receiver (cross-area)
Case-1: AI/ML-assisted Non-linearity Compensation (AI-NC) at BS
  Rel-20 proposed objectives:
Justification: Non-linearity from RF front-end to hinder higher-order modulation performance
Solution | App. in 5G FR1 | App. in 5G FR2 | Drawbacks
PA power back off | Yes | Yes | Lower PA efficiency Reduced coverage
DPD at UE TX | Yes | Not yet | Additional H/W Cost with high complexity
Model-based non-linearity RX equalizer | Not yet | Not yet | Model deficit
AI-NC at BS RX | Efficiently compensate RF impairment with low complexity Enhance BLER performance for high-order modulations |  | 
AI/ML-assisted receiver, as RAN4-centric work item:
  Focus on identified use cases without or with limited collaboration (collaboration level x).
  RAN4-centric study/work in Rel-20 5G-Adv. is important to identify use cases for 6G day-1 features for AI-native design.
  New use cases to be selected by considering AI/ML feasibility and practical performance benefits: AI-NC at BS as Case-1.
Compared to other solutions, AI-NC greatly enhanced BLER performance with low complexity.
Required SNR for 10% BLER | Conv. receiver 3.5% EVM | AI-receiver 3.5% EVM | AI-receiver 6% EVM
4RX, 256QAM, TDL-A, 30ns | 24.2 dB | 22.8 dB | 22.8 dB
64RX, 256QAM, TDL-A, 30ns | 15.5 dB | 11.5 dB | 10.8 dB
Training sequence
AI model update
Post-processing
Receiver
Enable high-order modulation
  Study on the feasibility of AI/ML-assisted non-linearity compensation (AI-NC) under existing and relaxed UE TX EVM requirements;
  Specify reduced MPR with relax EVM requirements for high order modulations (64QAM, 256QAM).
Received signal
Processing in gNB (receiver side)

## Slide 9
AI/ML-assisted receiver (cross-area)
Case-2: AI/ML-Channel Estimation (AI-CE) at BS
AI/ML-assisted receiver, as RAN4-centric work item:
  New use cases to be selected by considering AI/ML feasibility and practical performance benefits: AI-CE at BS as Case-2.
DMRS compression ratio | Schemes | NMSE | FLOPs
1 | LMMSE | -11.39 dB | 4.9e7
1/8 | cdDNN-L | -11.04 dB | 0.17e7
1/17 | cdDNN-L | -11.55 dB | 0.25e7
Justification: AI-based channel estimation to reduce DMRS overhead for data channel can significantly improve coverage and link performance
  Rel-20 proposed objectives:
  Study on the feasibility of AI/ML-assisted channel estimation (AI-CE) with comparable and reduced DMRS overhead;
  Specify demodulation performance for receiver with AI-CE.
Processing in gNB (receiver side)
AI model for CE
Legacy CE and decoding process
UE signal with lower DMRS density
Performance Monitoring
Configuration
Scheduling
UE signal with high DMRS density