## Slide 1: LGE’s overall view on Rel-20

## Slide 2: Categorization in RP-243292 (RAN chair summary)
Three columns in RP-243292
  Left-side items reflect more attention compared to in the right-side items for Rel-20 normative work.
1st column item
2nd column item
3rd column item

## Slide 3: Preferred Rel-20 WI list
For WIs in the 1st column, required TU for RAN2 is estimated to be lower than that for RAN1
  a) AIML air-interface and MIMO enhancement are RAN1-centric item, both are expected to occupy non-trivial TUs
  b) AIML mobility and IoT-NTN are RAN2-centric item. Required TU for both is estimated to be smaller that that for AIML air-interface and MIMO enhancement
  c) For AIoT, required Tus for RAN1 and RAN2 are expected to be not much different.
  Considering the a), b) and c), addition of RAN2-centric item is necessary for balanced TUs between RAN1 and RAN2 for Rel-20 5G.
Observation1: addition of RAN2-centric item is necessary for balanced TUs between RAN1 and RAN2 for Rel-20 5G.
Proposal1: For balanced TUs between RAN1 and RAN2 for Rel-20 5G, one RAN2-centric WI is added into baseline Rel-20 package comprising 1st column items in RP-243292.
LGE’s preference
  Our 1st preference is to add Mobility Enhancement WI as RAN2-led item into the baseline Rel-20 package.

## Slide 4: LGE’ preferred Rel-20 WI list
Items | Preferred objectives | WG
AI/ML for air interface (RP-250399) | Positioning left-over CSI prediction with NW-sided model | RAN1-led
AI/ML for mobility (RP-250401) | RRM prediction Measurement event prediction | RAN2-led
AI/ML for NG-RAN (RP-250402) | Multi-hop UE trajectory across gNBs AI/ML-based QoE optimization | RAN3-led
Ambient IoT enhancements (RP-250160) | Support of Device 2a/2b (incl. large frequency shift), Topology 2, DO-A, and TDD Capacity enhancements and enhancements on paging/RA/R2D transmission for R2D FDMA Coverage extension and enhancements of proximity detection accuracy/coverage D2R scheduling enhancements considering device’s energy level Paging enhancements to support multiple reader scenario | RAN1-led
IoT-NTN enhancement | Support of IMS voice call over IoT-NTN No additional “enhancement type” of work | RAN2-led
MIMO enhancement (RP-250400) | STxMP enhancement UEI BM enhancement | RAN1-led
Mobility enhancement (RP-250161) | LTM overhead reduction (beam measurement overhead, L1 measurement reporting overhead, early UL synchronization overhead) Conditional LTM specific enhancements (minimization of network resource reservation for CFRA/RACH-less CLTM, support of DG based RACH-less cell switch Intra-CU CLTM for DC case if not supported in Rel-19 | RAN2-led

## Slide 5: Additional WIs for Rel-20
More addition of WIs into Rel-20 package
  As indicated in observation1, we believe that addition of RAN2-centric WI is necessary for balanced TUs between RAN1 and RAN2.
  On top of the added RAN2-centric WI, whether and how many extra Wis can be added into Rel-20 package depends on both a) TU allocated for 5G Rel-20 and b) scope of each of the WI in the 1st column and the mobility enhancement WI (if added).
  Our strong preference is still to minimize approved WI list for Rel-20 5G. However, just for the case many companies strongly prefer to add extra WIs into Rel-20 package, we show our preference.
LGE’s preference (just in case companies strongly prefer to add more than one WI into baseline Rel-20 package)
  For RAN1 centric-item,
    1st priority: Coverage enhancement WI
  For RAN2 centric-item
    1st priority: Mobility enhancement WI
    2nd priority: UAV/UAM enhancement WI (minimal scope), XR enhancement WI
      UAV/UAM enh. WI: Mobility enhancement for RRC_IDLE, CONNECTED, measurement report enhancement
      XR enh. WI: Traffic awareness enhancement, power saving enhancement

## Slide 6: Additional WIs for Rel-20
Proposal2: For ISAC, parallel study/work in both 5G-Advanced and 6G should be avoided. Priority should be given to 6G. Study item considering all 6 sensing modes in 6G is supported.
Proposal3: Further NR-NTN enhancement in 5G-Advanced is not desirable unless there is a feature with strong demand from the market, and priority is given to conducting studies targeting the integration of TN and NTN in 6G.

## Slide 7: Alternative LGE’ preferred Rel-20 WI list (with extra WIs)
Items | Preferred objectives | WG
AI/ML for air interface (RP-250399) | Positioning left-over CSI prediction with NW-sided model | RAN1-led
AI/ML for mobility (RP-250401) | RRM prediction Measurement event prediction | RAN2-led
AI/ML for NG-RAN (RP-250402) | Multi-hop UE trajectory across gNBs AI/ML-based QoE optimization | RAN3-led
Ambient IoT enhancements (RP-250160) | Support of Device 2a/2b (incl. large frequency shift), Topology 2, DO-A, and TDD Capacity enhancements and enhancements on paging/RA/R2D transmission for R2D FDMA Coverage extension and enhancements of proximity detection accuracy/coverage D2R scheduling enhancements considering device’s energy level Paging enhancements to support multiple reader scenario | RAN1-led
IoT-NTN enhancement | Support of IMS voice call over IoT-NTN No additional “enhancement type” of work | RAN2-led
MIMO enhancement (RP-250400) | STxMP enhancement UEI BM enhancement | RAN1-led
Mobility enhancement (RP-250161) | LTM overhead reduction (beam measurement overhead, L1 measurement reporting overhead, early UL synchronization overhead) Conditional LTM specific enhancements (minimization of network resource reservation for CFRA/RACH-less CLTM, support of DG based RACH-less cell switch Intra-CU CLTM for DC case if not supported in Rel-19 | RAN2-led
XR enhancement | Traffic awareness enhancement (reliability improvement for important PDU set, e.g. selective PDCP duplication, and prioritized scheduling for important PDU set, e.g. transmission via different RLC entities, Power savin enhancement (support for multiple flows, e.g. multiple DRX configurations, jitter efficient DRX operation, e.g. additional onDuration | RAN2-led
Coverage enhancement | Msg1 PRACH repetition with different Tx beams, UL beam indication for Msg3 Msg5 PUSCH repetition scheduled by DCI 0_0 with C-RNTI | RAN1-led
UAV/UAM enhancement (RP-242470) | Mobility enhancement, such as altitude dependent neighbor cell/measurement beam restriction for RRC_IDLE UE, and altitude dependent CHO candidate cell restriction for RRC_CONNECTED UE target cell Measurement reporting enhancement | RAN2-led
Extra
WIs