## Slide 1: Views on Rel-20 Ambient IoT
3GPP TSG RAN#107
Incheon, Korea, March 12 - 14, 2025
RP-250160

## Slide 2: Background
Standardization of Rel-20 NR will start from June 2025
  First package of Rel-20 WIs/SIs will be approved in RAN#108 in June 2025
  It is expected to start the 2nd phase of standardization of Ambient IoT for NR in Rel-20
In general, WI scope of Rel-19 Ambient IoT is focused on essential scenarios/features for the first step deployment based on the outcomes of Rel-19 study, as shown below;
  Target scenarios/topologies focus on indoor, topology 1, DO-DTT and DT, and FR1 licensed FDD spectrum
  Target device types focus on device type 1
  PHY layer design to support the target scenarios/topologies/device types
  L2 protocol structure and new A-IoT MAC PDU formats for data, control, and paging
  A-IoT paging (focusing on a single reader scenario) and random access
  RAN architecture and signaling and procedures for CN-RAN interface (NGAP enhancement)

## Slide 3: Discussion on Rel-20 Ambient IoT (1)
In our view, Rel-20 Ambient IoT should focus on
  Extended scenarios/topologies; and
  Enhanced functionalities
For extended scenarios/topologies, we propose to support the following:
  Topology 2
    To support Deployment scenario 2 (device indoors, BS outdoors) for all devices (1/2a/2b)
  FR1 licensed TDD and DO-A traffic scenarios
    These two may require study for the first few months in Rel-20
  Device 2a and 2b
    To support the use cases that require ~ 50 meters, or even larger coverage (if agreed)
    To support FR1 licensed FDD spectrum without any spectrum regulation issues
  Large frequency shift for device type 2a (if feasible)
    To expand the use case scenarios in FR1 licensed FDD spectrum (e.g., to support the case where CW2D is in DL and D2R is in UL in FR1 licensed FDD spectrum)
    To support the case where readers do NOT have (enough) in-band full-duplex (or SIC) capabilities

## Slide 4: Discussion on Rel-20 Ambient IoT (2)
For enhanced functionalities, we propose to support the following:
  Coverage extension
    To improve indoor coverage for Device 1/2a, or to improve indoor/outdoor coverage for Device 2b
    Techniques to enable this would include repetition, retransmission, CW node control/coordination, etc.
  Capacity enhancements
    To support the use cases that require larger connection density or shorter inventory latency compared to Rel-19
    Techniques to enable this would include R2D FDMA, enhancements of resolution of TDMA/FDMA (e.g., support of sub-slot for TDMA, 2-dimensional TDMA and FDMA, etc.), and inter-reader coordination
  Enhancements of proximity detection accuracy/coverage
    To support the proximity services that require higher accuracy/coverage compared to Rel-19
    E.g., dedicated signals and/or procedures for proximity determination can be considered for improved accuracy/coverage

## Slide 5: Discussion on Rel-20 Ambient IoT (3)
For enhanced functionalities of RAN2, we propose to support the following:
  D2R scheduling enhancements considering device’s remaining energy level
    A-IoT device may not have sufficient energy to perform the remaining D2R transmissions.
    D2R scheduling enhancements for Rel-20 A-IoT includes:
      Energy status indication
  RAN2 enhancements to support R2D FDMA
    If FDMA is applicable for R2D direction, RAN2 enhancements should be considered to exploit R2D FDMA. The following RAN2 functionalities can be considered for the enhancements.
      Paging mechanism
      Random access
      R2D data transmission

## Slide 6: Discussion on Rel-20 Ambient IoT (4)
For enhanced functionalities of RAN2 and RAN3, we propose to support the following:
  A-IoT paging enhancement to support multiple reader scenario
    Paging associated to the same service request may be sent from multiple readers in case of paging for wide area covered by multiple cells, overlapped cell scenarios, and localization/positioning. In some scenarios, particularly, localization/positioning, duplicated responses from a device need to be allowed.
    Paging from multiple readers and duplicated responses from a device are considered.
  Support of topology 2
    The radio resources used by A-IoT radio interface between A-IoT devices and UE reader is controlled by network and the resources are configured to the UE reader via dedicated signaling according to the Rel-19 SI results.
    For support of topology 2, study and specify the followings:
      Down-selection on solutions (i.e., RRC-based, UP-based) for conveying A-IoT upper layer information
      A-IoT radio resource request/assist information from IN UE to gNB
      A-IoT radio resource control/allocation
      A-IoT radio resource validity

## Slide 7: Recommended scope of Rel-20 Ambient IoT WI
Extended scenarios/topologies | Enhanced functionalities
Device type 2a and 2b Large frequency shift for device type 2a (if feasible) Support of topology 2 A-IoT radio resource request/assist information from IN UE to gNB A-IoT radio resource control/allocation A-IoT radio resource validity Down-selection on solutions (i.e., RRC-based, UP-based) for conveying A-IoT upper layer information Support of DO-A and TDD | Coverage extension by, e.g., Repetition, retransmission, CW node control/coordination, etc. Capacity enhancements by, e.g., R2D FDMA Enhancements of resolution of TDMA/FDMA Inter-reader coordination D2R scheduling enhancements considering device’s remaining energy level RAN2 enhancements for R2D FDMA including paging, RA, and R2D data transmission A-IoT paging enhancements to support multiple reader scenario Enhancements of proximity detection accuracy/coverage