## Slide 1: Views on RAN4-led topics in Rel-20
3GPP TSG RAN Meeting #107
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.3
RP-250240

## Slide 2: Views of RAN4-led topics for Rel-20 5G-Advanced
Limited number of WI to be selected considering market demand and TU splitting
TU splitting : TU > 50% for 5G-A and TU < 50% for 6G study
RRM
  FR2 Multi-Rx enhancement
Cross-Area
Ku band NTN
Low band CA via switching
ATG Evolution
RF
High Power UE (HPUE) enhancement
SL-U enhancement
  DL fragmented carriers
LGE’s views on RAN4-led Rel-20 scope

## Slide 3: High Power UE (HPUE) enhancement (RF)
Motivation
  In Rel-19,
    NR FR1 HPUE requirements for inter-band CA/EN-DC is under discussion. In WID [RP-240828], only LTE FDD PC3 is considered in EN-DC configuration of PC2/PC1.5 with 2Tx or 3Tx.
    FR1 PDE in a single carrier and intra-band C/NC CA is under discussion for PC3 and PC2 (1Tx, 2Tx).
  In Rel-20
    LTE FDD PC2 needs to be considered in EN-DC configuration of PC2/PC1.5 with 2Tx or 3Tx.
    3UL CC in two bands needs to be considered for CA/EN-DC
      PC2 / PC1.5 (2Tx) with 2CC in NR
    FR1 PDE for PC1.5(2Tx) needs to be specified in a single carrier and intra-band CA
Objective
  RF requirement for PC2/PC1.5 EN-DC with PC2 LTE band with 2Tx or 3Tx
  RF requirement for 3UL CC in two bands for CA/EN-DC
    PC2 / PC1.5 (2Tx) with 2CC in NR
  RF requirement for FR1 PDE for PC1.5(2Tx) in a single carrier and intra-band CA

## Slide 4: SL-U enhancement (RF)
Motivation
  Up to Rel-19,
    In SL-U
      Only power class 5 has been specified
    In NR-U
      Both power class 3 and power class 5 have been specified in single carrier
      Power class 5 has been specified in intra-band contiguous CA
  In Rel-20 SL-U, it needs to specify
    Power class 3 in single carrier
    Power class 5 in intra-band contiguous CA
Objective
  RF requirement in SL-U for
    Power class 3 in single carrier
    Power class 5 in intra-band contiguous CA

## Slide 5: DL fragmented carriers (RF)
Motivation
  In Rel-19,
    Related SI is expected to be complicated.
      Identify methods for reducing the number of UE Rx chains (e.g. from separate RF chains per CC to shared RF chains ) needed for single DL band with frequency span ≤ 100 MHz, containing two non-contiguous CCs within a CA combination for the inter-operator co-located scenario, considering
    Based on the output, WI should be proceeded in Rel-20
Objective
  RF requirements for DL fragmented carriers

## Slide 6: FR2 Multi-Rx enhancement (RRM)
Motivation
  In Rel-18, RAN4 has defined L1-RSRP measurement requirements for simultaneous reception using multi-Rx from intra-cell based mTRP in FR2
  In Rel-19, RAN4 is discussing L3 measurement delay reduction by optimizing Rx beam sweeping using multi-Rx in FR2.
  To reduce delay further in FR2 RRM, in Rel-20, other scenarios (e.g., SCell activation, PSCell addition, etc) that were precluded in Rel-19 need to be considered.
  Additionally, inter-cell based mTRP using multi-Rx operation needs to be considered.
Objective
  RRM requirements of simultaneous multi-Rx operation in FR2 for
    Scenarios that were precluded in Rel-19 such as SCell activation, PSCell addition, CSI-RS based L3, etc.
    Scenarios on Inter-cell based mTRP

## Slide 7: Ku band NTN (Cross-Area)
Motivation
  In Rel-19, Ku band NTN requirements is being specified for Mobile VSAT type 4 and 5 in a single carrier considering
    FR1-NTN supporting 10, 20, 25, 35, 50, 70 and 100 MHz CBW with 30 kHz SCS
    FR2-NTN supporting 50, 100, 200, 400 MHz CBW with 120 kHz SCS.
    Assuming 60cm antenna aperture. Other antenna aperture sizes are postponed to future release.
  It is not clear to complete priority 2 Ku band
  Supporting satellite services in 125 MHz (UL) and 250 MHz (DL) aggregated bandwidths is needed
Objective
  In single carrier, RF requirement in Ku band for
    Mobile VSAT that can only support LEO connection
    Mobile VSAT with other antenna aperture size e.g. 20x20cm
    Priority 2 band if not completed in Rel-19
  RF/RRM requirements in Ku band for intra-band CA including 125 MHz (UL) and 250 MHz (DL) aggregated bandwidth under intra-SAN scenario

## Slide 8: Low band CA via switching (Cross-Area)
Motivation
  In Rel-19,
    Low band CA is under discussion considering FDD + SDL with switching between {case1, case2}
      Case 1: Tx/Rx on FDD carrier 1 and no Rx on SDL carrier 2
      Case 2: no Tx/Rx on FDD carrier 1 and Rx on SDL carrier 2
    Semi-static switching pattern
  In Rel-20, extend the scenario considering
    Low band CA in FDD + FDD with switching between {case3, case 4}
      Case 3: Tx/Rx on FDD carrier 1 and no Tx/Rx on FDD carrier 2
      Case 4: no Tx/Rx on FDD carrier 1 and Tx/Rx on FDD carrier 2
    Dynamic switching
Objective
  RF/RRM requirements for low band CA FDD + FDD with switching between {case3, case 4}
    Case 3: Tx/Rx on FDD carrier 1 and no Tx/Rx on FDD carrier 2
    Case 4: no Tx/Rx on FDD carrier 1 and Tx/Rx on FDD carrier 2
  RF/RRM requirements for dynamic switching configuration

## Slide 9: ATG evolution (Cross-Area)
Motivation
  In Rel-19, ATG enhancement is under discussion for 1UL/2DL intra/inter-band CA and MIMO in single carrier in FR1.
  In Rel-20, CA configuration needs to be expanded considering
    FR1 intra/inter-band UL CA
    FR2 in single carrier
      From the perspective of increasing capacity and reducing interference of TN network (i.e., existing network), expansion to FR2 band is an important features for ATG operation.
Objective
  RF/RRM requirements of ATG for
    FR1 intra/inter-band UL CA
    FR2 in single carrier