## Slide 1: 3GPP TSG RAN Meeting #107 - Incheon, KR Mar 12-14, 2025 AIML technology for Rel-20 and beyond Tim O’Shea & Jim Lansford, DeepSig Inc

## Slide 2: Rel-18 and Rel-19 are a start
NR_AIML_air Study Items showed areas of potential performance gain
  CSI Prediction
  Beam Management
  Positioning Accuracy
  Additional Studies
    CSI Compression
    Model Identification/Training/Transfer
Some items are FFS, some will carry forward to normative Work Items in Rel-20
  Including complementary work in RAN4
Rel-20+ is an opportunity to study even more innovations in L1/L2

## Slide 3: Next generation radio technology: Objectives
Build interoperably upon existing 5G-NR PHY
Expand performance using key AI-RAN optimizations
Retain existing NR Slot & DMRS Structure
  Use existing CP-OFDM and DFT-s-OFDM basis
Focus on driving performance in
  Mobility, Edge Performance, Capacity
  Energy Efficiency, Hardware Efficiency
  Additional private, NTN, IoT use cases
  Multi-user Capacity enhancement
  Spectrum & Power Efficiency
  Co-existence and Resilience

## Slide 4: Next generation radio technology: Key Tech & PHY Structure
Build interoperably upon existing 5G-NR PHY
  Novel modulation like OTFS/DDAM are problematic
Support AI based modulation, equalization approach
  Pilot free and end-to-end autoencoder learning
  Allow zero-DMRS allocation in PUSCH/PDSCH
  Gradual transition to zero-DMRS broadcast/control
  Side by side transmission modes
Leverage RAN data for Digital Twin and online optimization of modes and scheduling
Autoencoder can be thought of as AI-assisted MU-MIMO

## Slide 5: Next generation radio technology: Pilot Free & AE Modes
Learned modulation and equalization approach is a critical AI-RAN technology for 6G
  Support two sided deployments but most practically (codebook-based sharing)
  Leverage Existing or new FEC/Rate matching and slot mapping/ [CP/DFT]-OFDM basis
  Neural Modulation mappings can be shared via codebook definitions
  Study Item required to refine Autoencoder Modulation aspect in detail
Neural Modulation
(Encoder)
Rate Matching & Encoding
CP/DFT-OFDM
Mapping
CP/DFT-OFDM
De-Mapping
Neural
Receiver
Neural
De-mapper
(Decoder)
Rate De-match & Decoding
Transmitter Terminal
Receiver Terminal

## Slide 6: Next generation radio technology: Pilot Free & AE Modes
Low MCS Impact (Preliminary)
  Pilot-Free Neural Autoencoder MCS
  Improve both throughput and link margin required for edge performance in UL and DL scenarios
  Reduction in Pilot Overhead
  Mitigate Pilot Contamination
  Expand edge performance
  Improved doppler/fading operation
  (Shown: Ray-traced urban channel)
16% Increased Throughput
1-2dB improved sensitivity
Pilot-Free NNAE vs MCS 3 (2-DMRS 1:1)

## Slide 7: Next generation radio technology: Pilot Free & AE Modes
High MCS Impact (Preliminary)
  Pilot-Free Neural Autoencoder
  Improve both throughput and link margin required for edge performance in UL and DL scenarios
  Improved channel estimation & capacity in harsh multipath, doppler, enhanced high SINR data rates & margin
  (Shown: UMi channel)
Pilot-Free NNAE vs 5G MCS-19 2-DMRS 1:2
16% Increased Throughput
~2dB Improved Sensitivity

## Slide 8: Next generation radio technology: RAN Digital Twin
Leverage more channel distribution information across network for better transmission
  Allow fine-tuning per sector
  Codebooks management can be per-sector, per-region, per-network, etc
  Enable Autoencoder training and sharing with network elements
  Allow improved MU- scheduling, interference mitigation, control
Study Items should include DT channel models (e.g. calibrated ray tracing)

## Slide 9: Next generation radio technology: Sensing Native RAN
Spectrum sensing key technology for enabling interoperability
  Rapidly identify adjacent network allocations and radio technologies
  Allow network to mitigate interference and adjust network parameters
  Streamline adoption of new bands in FR1, FR3 /w shared usage (e.g. 3.1-3.4G)
  Enable intelligent scheduling to avoid network degradation or failure
Additional study on Sensing Native RAN
OmniSIG Air-Interface Awareness Software

## Slide 10: Next generation radio technology: Summary
Key technologies to consider for study items:
  Two-sided AI-RAN Models for Autoencoder-Modulation and Equalization
  Data-driven digital twins and channels for accurate site-specific optimization
  Sensing-Native RAN for spectrum awareness and shared band optimization
AI-RAN Offers a path to more resilient, performant and efficient air interface
  Channel models must improve to consider site-specific performance
  Existing channel models still important performance considerations
  AE modes can be considered beyond PUSCH/PDSCH for RACH, BCH, CCH
  Key enablers for improved capacity, operator value, density, optimization

## Slide 11: Thank You! info@deepsig.ai