## Slide 1: Way Forward to support L3 measurement based LTM in Split-gNB Architecture NTT DOCOMO, Qualcomm Inc, Fujitsu, Apple Inc, AT&T, JIO Platforms, Mediatek, Rakuten

## Slide 2: Background
R18 Introduced L1 measurement based LTM with the goal of reduced HO interruption during cell switch procedure by performing “early DL/UL sync” for UE.
In later phase of R18, RAN4/RAN2 agreed to support L3 measurement based LTM for FR1 only due to the fact that some network and/or UE implementation may not support L1 measurement based LTM in early phase of product development cycle.
RAN4 LTM performance requirements are same for both L1 and L3 measurements.
Based on LS (R2-2407606, R2-2409373) received from RAN2 , for split gNB Architecture F1-AP enhancements between CU and DU, RAN3 discussed following solution options
  Option1: CU based solution
  Option2: DU based solution
  Option3: Hybrid Solution (i.e., support F1-AP signaling enhancements for both CU and DU based solutions and it is up to implementation to choose CU or DU based solution as way forward)
  Option4: No Solution (i.e., it is left upto implementation of F1-AP)
R3-250879 LS was sent to RAN2, CC: RAN4, RAN
  RAN WG3 has discussed the solutions, however does not reach a consensus to specify the support for L3 measurement based LTM for CU/DU distributed architecture. As a result, F1 support for L3 measurement based LTM will not be specified in Release 18.
The above RAN3 chair decision is not in the spirit of 3GPP F1-AP open interface specification (between CU and DU) and is not inter-vendor interoperable.

## Slide 3: How to support LTM in mixed deployment scenarios
For L1 measurement based LTM, DU makes all decisions for DL MAC TCI state activation/deactivation, UL TA pre-sync and MAC-CE based Cell Switch Command triggering.
It is possible that gNBs will be able to support both L3 and L1 measurement based LTM configuration for FR1 and FR2 respectively.
Different UEs based on capability are expected to support L1 and/or L3 measurement based LTM for FR1.
  Whether to support FR1 intra-frequency and FR1 inter-frequency L1 measurements by UE is based on its capability.
Both Intra-freq L1 measurement based LTM and Inter-freq L3 measurement based LTM decisions has to be made by single node (i.e., DU) to avoid conflict of decisions between CU and DU.
For both FR1 and FR2, DU shall be able to process either L3 or L1 based measurement reports for all LTM event decisions.
In such mixed deployment scenario, it is necessary to have one node in split gNB Architecture should control LTM HO triggering decisions for both L1 and L3 measurements based LTM.

## Slide 4: Way Forward Proposals
RAN3 discussed CU and DU based solutions and multiple concerns were raised against CU based solution and details are provided in Annex slides.
In order to make progress and avoid implementation based CU-DU interface (which is NOT inter-operable), TSG RAN directs RAN3 to specify necessary F1-AP signaling enhancements
Proposal :
As compromise way forward support Hybrid Solution (i.e., support F1-AP signaling enhancements for both CU and DU based solutions and it is up to implementation to choose CU or DU based solution)
For CU based multiple code point solution, CU is allowed to send separate triggers in F1-AP signalling message to DU with the following information.
  DL TCI state activation/deactivation per cell ID/beam ID (i.e., allow flexibility to signal DL TCI state activation/deactivation for multiple cells/beams)
  UL TA pre-sync trigger for each candidate cell/SSB
  Allow flexibility to send both DL TCI state activation/deactivation and UL TA pre-sync together for a given candidate cell/SSB ID.
  Cell Switch Command for one candidate cell/beam
In order to support intra freq L1 measurement based LTM and inter-freq L3 measurement based LTM via optional CU based solution, CU can optionally provide L3 measurements to DU. If L3 measurements are provided, DU must have freedom to select either L1 based intra-freq or L3 based inter-freq LTM decision. i.e., it is optional for DU to follow CU triggered L3 measurement based LTM and specify F1-AP signalling to indicate from DU to CU.

## Slide 5: Annex1 (DU based Solution)
R3-250568 : Way forward Signalling enhancements to support L3 measurement based R18 LTM
The difference between L1 vs L3 measurements is only about usage of L1 filter vs L3 filter by the UE. At receiving RAN node, there is no additional de-filtering needed and meaning of absolute value of L1-RSRP Vs L3-RSRP remains same. DU will understand radio measurement very well and DU will handle processing of L3 measurements based on implementation.
DU shall be responsible for PHY/MAC scheduling decisions and CU taking control of DU scheduling functions is violation of CU-DU functional split for split gNB.
Control plane part of DU can understand RRC IEs and in many existing F1-AP signalling messages RRC IEs are already exchanged by CU and DU. In fact DU gets MeasResultList2NR IE within CU to DU RRC Information IE -> Handover Preparation Information -> RRM-Config -> MeasResultList2NR.
CU forwarding L3 filtered measurements to DU simplifies F1 signalling design and DU scheduler can autonomously make decision about when to trigger DL/UL pre-synchronization and MAC-CE based cell switch command depending on either L3 or L1 measurements.
DU based solution is baseline and is common for both L1 and L3 measurement based LTM.

## Slide 6: Annex2 (Issues with CU based Solution)
R3-250568 : Way forward Signalling enhancements to support L3 measurement based R18 LTM
CU triggering F1-AP signalling messages towards DU for MAC-CE based TCI state activation, PDCCH order and MAC-CE Cell switch command adds additional complexity without adding any real LTM performance benefit.
CU triggering single F1-AP signalling message with single code point towards DU does not allow to activate/deactivate MAC-CE TCI state for multiple candidate cells and per cell level UL pre-sync cannot be performed in advance and thus defeats the purpose of early DL/UL sync.
CU does not have any timing information related to SMTC/SSB availability, RACH Occasion , TA information and whether DL/UL Sync is successful or not is not known to CU and only DU knows all this information.
CU triggering single F1-AP signalling message with single code point towards DU for triggering MAC-CE based TCI state activation, PDCCH order and MAC-CE Cell switch command causes additional delay for DU to trigger MAC-CE based cell switch command , causes long delay to execute CSC and adds all interruptions in a sequence manner and deteriorating serving cell conditions may cause UE declaring RLF on serving cell and defeats the purpose of early DL/UL synchronization for LTM UE.
CU sending separate F1-AP singling messages to DU for DL TCI state activation, UL TA pre-sync and cell switch command offers some flexibility even though it DOES NOT provide any additional LTM performance benefits compared to DU autonomously making decisions based on L3 measurements.
CU based solution for L3 measurement based LTM has multiple issues and is not aligned with R18 DU solution for L1 measurement based LTM.