## Slide 1
Scope for Rel-20 AI/ML Mobility WI
3GPP TSG RAN meeting #107
Incheon, South Korea, Mar 12th – 14th 2025
Ericsson
RP-250389

## Slide 2: Introduction
In Rel-19, the Study Item “Study on AI (Artificial Intelligence)/ML (Machine Learning) for mobility in NR” (RP-242393) is studying and evaluating the potential benefits and gains of the AI/ML aided mobility for network triggered L3-based handover.
The activity is studying the following:
  RRM measurement predictions [RAN2]
    Cell/beam-level measurement prediction including intra and inter-frequency
  Measurement events predictions [RAN2]
HO failure and RLF predictions has been scoped out from Rel-19 SI
Life Cycle Management (LCM) is also considered in the activity, based on the general framework defined in Rel19 AI/ML-air interface WID with some potential AI mobility specific additions.
RAN4 aspects are also considered, in particular the testability, interoperability, and impacts on RRM requirements and performances.
Simulation aspects take great part of the activity, since the focus is the evaluation of the prediction accuracy and the benefits on the network KPI.

## Slide 3: Motivation: Basic use cases
The Rel-19 activity for AI/ML for Mobility is ongoing and the results from simulations show that the usage of AI/ML is beneficial to L3-assisted mobility. This is an indication that the normative work can start in Rel-20, based on the outcome from the Rel-19 SI.
  Proposal 1: Approve a WI for AI/ML-assisted mobility for network-triggered L3 handover based on the outcome from the Rel-19 Study Item
However, the use cases which are most beneficial to the mobility should be prioritized during the normative phase, that is:
  RRM measurement predictions based on temporal/frequency/spatial predictions
  Measurement events predictions, based on indirect approach
  Proposal 2: During the normative phase, specify cell level and beam level RRM measurement predictions based on temporal/frequency/spatial domain predictions and the measurement events predictions.
  Proposal 3: During the normative phase, specify measurement event prediction for A1 to A6 events.

## Slide 4: Motivation: additional use cases
Although the current scope of Rel-19 study only mentions the L3 mobility, it is beneficial to consider the usage of AI/ML to other cases, such as SCell handling and SCG handling.
We don’t think that there would be any additional work of allowing the measurement predictions to be used for other use cases. It rather only means that RAN2 should skip adding unnecessary restrictions stating that the measurement prediction can only be used for handovers, or similar.
Proposal 4: During the normative work, RAN WGs should not add restrictions on what the measurement prediction can be used for, e.g. avoid specifying restriction such that they can only be used for handovers, in order to allow the gNB to use them for SCell/DC handling

## Slide 5: Motivation: Data collection for Network side model training and inference
During the study item, comprehensive simulation-based evaluation of AI/ML models is done regardless of whether they are deployed at the UE side or at the network side. In some simulations, some assistance information are used which are only available at the UE and, in order to enable network side models with high accuracy in prediction, reporting such information to the network is deemed necessary.
Therefore, we propose to consider specifying data collection for the network side model with the focus on collecting information (radio related and non-radio related assistance information) which are beneficial for the network side models.
  Proposal 5: During the normative phase, specify data collection from the UE that is beneficial for the network side model training and inference

## Slide 6: Motivation: performance monitoring/evaluation
UE side LCM:
  Signaling and protocol aspects of LCM mechanism shall be specified, based on the Rel-19 Study Item outcome, including enhancements specific to AI/ML for Mobility, if needed.
Proposal 6: Specify signaling and protocol aspects of Life Cycle Management (LCM) mechanism for UE-based AIML functionality.
Data collection for Network side model performance evaluation:
  Regarding network-side models, in the context of RAN2, we believe data collection from the UE is necessary to assess and validate the performance of these models running at the network side. We consider the rest of the LCM related functionality to be outside the scope of this item which is so far limited to RAN2 and RAN4. Therefore, we propose to consider the data collection for model performance evaluation for the network side model.
Proposal 7: Specify signaling and protocol aspects of data collection from the UE for the network side model evaluation.
RAN4 should continue identifying and specifying RRM measurement/prediction requirements and extend them to the new use cases included in Rel-20 WI (e.g., AI/ML for LTM)
Proposal 8: RAN4 to specify requirements for the objectives identified in Rel-20 WI, as necessary

## Slide 7: Proposals
To conclude, we have the following proposals for Rel-20 AI/ML for Mobility:
Proposal 1: Approve a WI for AI/ML assisted mobility for network-triggered L3 handover based on the outcome of the Rel-19 Study Item
Proposal 2: During the normative phase, specify cell level and beam level RRM measurement predictions based on temporal/frequency/spatial domain predictions and the measurement events predictions.
Proposal 3: During the normative phase, specify measurement event prediction for A1 to A6 events.
Proposal 4: During the normative work consider the potential use-cases that can be enabled using the RRM measurement prediction and the event prediction:
    Use cases such as CA/DC based on the RRM prediction and event prediction are investigated and enabled by RAN2 during the normative phase.
    Proposal 5: During the normative phase, specify the data collection from the UE beneficial for the network side model training and inference
Proposal 6: Specify signaling and protocol aspects of Life Cycle Management (LCM) mechanism.
Proposal 7: Specify signaling and protocol aspects of data collection from the UE for the network side model evaluation.
Proposal 8: RAN4 to specify requirements for the objectives identified in Rel-20 WI, as necessary.