## Slide 1: Discussion on Rel-20 MIMO

## Slide 2: MIMO evolution status
MIMO has been evolved in every release
  Rel-16
    BM enhancements: BM overhead reduction, SCell BFR, L1-SINR
    mTRP support: S-DCI and M-DCI mTRP
    CSI enhancement: FD compression codebook
    Full power UL Tx
    Low PAPR RS
  Rel-17
    BM enhancements: BM overhead reduction(u-TCI)
    mTRP enhancements: extended for PDCCH/PUCCH/PUSCH, mTRP SFN, mTRP BM
    CSI enhancements: NCJT CSI, FDD reciprocity
    SRS enhancement: >4Rx support, coverage/capacity enhancement
  Rel-18
    BM enhancements: u-TCI extension
    mTRP CJT enhancements: type-II codebook for CJT, SRS enhancement for TDD CJT
    MPUE support:STxMP, 2TA
    CSI enhancements: TD prediction/compression, TDCP report,
    8Tx UL MIMO
    DMRS for larger scale MU-MIMO
  Rel-19
    BM enhancements: UEI beam report
    mTRP CJT enhancements: inter-TRP frequency/phase offset
    CSI enhancements : up to 128 CSI-RS ports
    3Tx UL MIMO
    Asymmetric DL-UL: PC and TA

## Slide 3: Discussion on Rel-20 MIMO
High level principles
  Duplicated discussion between 5G-A and 6G should be avoided.
  Scope/TU of Rel-20 MIMO work item (if supported) should be reduced and maintained in a reasonable level(e.g. 0.5~1TU for RAN1) compared to MIMO WIs in previous releases considering that 6G SI is likely to take more than half of the overall TU budget.
  Focus on making the existing features more attractive and more useful in the real deployment scenarios, rather than supporting a new feature or supporting an increased dimension(e.g. ports/layers).
Discussion
  Further mTRP enhancements (e.g. supporting 4 TRPs) seem not urgent due to lack of practical scenarios in 5G NR
  Further BM enhancements seem not urgent but UEI BM enhancement may be considered to make R19 UEI BM feature more attractive and useful.
    Reducing beam application latency would be important to reduce overall BM latency.
  STxMP enhancement will be useful since R18 supports only part of UL channels/signals so that the practical usage of STxMP is limited in the field.
    Note that STxMP is related to RF/hardware design at UE side, so it is hard to implement STxMP only for a specific UL channel which belongs to baseband processing
  UL MIMO enhancements may be considered but introducing a new UL MIMO Tx scheme such as UL subband precoding and UL precoder cycling would require a large specification work. Since same/similar proposals are expected in 6G, it is better to discuss it in 6G SI.

## Slide 4: Proposals
Proposals for Rel-20 MIMO
  Rel-20 MIMO focus on making existing features more attractive/useful and avoid to introduce brand new features.
  Prioritized items
    STxMP support to other UL channels/signals: PUSCH+PUCCH for S-DCI/M-DCI based STxMP and PUCCH+PUCCH for M-DCI based STxMP
    UEI BM enhancement: beam application latency reduction
.