## Slide 1
Huawei, HiSilicon
Rel-20 MIMO Scope
3GPP TSG RAN#107 RP-250491
Incheon, South Korea, March 12-14, 2025
Agenda Item: 15.2.2

## Slide 2
MIMO enhancements in Rel-20
For TDD Massive MIMO, the MIMO performance is restricted by the accuracy of SRS based channel estimation, especially for cell edge UE. To enhance the accuracy of SRS channel estimation, we propose following enhancements:
  Enh.2: SRS hopping pattern within a frequency hop to enable channel interpolation, and cross-slot (S and U slot) SRS resource for repetition
Massive MIMO has been widely deployed in current networks, which provides high spectrum efficiency for 5G and 5G-A. However, for the two typical deployments, TDD Massive MIMO and multi-TRP coordination, the channel estimation for SRS and DMRS is the bottleneck for network performance with Massive MIMO. In Rel-20, we focus on addressing the key issues.
UE
SRS needs to be enhanced for accurate channel estimation in TDD Massive MIMO
The leftover issue from Rel-19 for UL enhancement, i.e., UL frequency selective precoding, also could be considered.
For large-scale multi-TRP coordination, inter-cell PDSCH interference is the key issue, so a large number TRPs is required in a coordination set to avoid the inter-cell interference. In the case, SRS measurement needs to be enhanced for accurate channel estimation, and DMRS also needs to be enhanced for supporting large number layers MU transmission. Thus, we propose following enhancements:
  Enh.1: Long term channel covariance assisted SRS channel estimation
Address strong inter-cell interference for SRS
Required SRS
Remote UE
Interference

## Slide 3
Large-Scale multi-TRP Coordination
  CJT/JR is commercially deployed by tens of operators globally.
  In commercial deployments, more than 10 TRPs are in a CRAN structure for CJT transmission. With large scale multi-TRP coordination (6 or 9 TRPs), significant gain can be observed especially for cell edge users, since inter-cell PDSCH interference are avoided in the multi-TRP coordination. In following preliminary evaluation results, 70%~110% performance gain for cell edge can be observed with 6TRPs and 9TRPs coordination compared to 3TRPs.
Signal S1
Residual interference S2'
  However, due to the limitation of SRS channel estimation, currently, CJT transmission is only with 2 or 3 TRPs. The key issue is that: the interference from other cells is much larger than the required SRS from remote UE in the large scale multi-TRP coordination network. As shown in the following preliminary evaluation, only enlarge the number of TRPs in the coordination group but without any SRS interference mitigation, the system performance even decrease.
Strong inter-cell interference for SRS measurement
Required SRS
Remote UE
Interference
Observation: SRS channel estimation accuracy is the bottleneck for enabling large scale mTRP coordination.
1X
Cell Average
0.9X
Cell Edge
1X
0.62X
R19 with 3 measured TRPs
R19 with 9 measured TRPs
2.1X
1X
9TRPs Coordination
6TRPs Coordination
3TRPs Coordination
1.7X
1.5X
1X
9TRPs Coordination
6TRPs Coordination
3TRPs coordination
1.36X
Large scale multi-TRP coordination
Cell Average Gain
Cell Edge Gain

## Slide 4
UE calculates the long term channel covariance RHH where channel covariance could be calculated per subband and average across subbands and time.
UE quantize the channel covariance: using DFT projection to matrix s, and select L largest coefficients to report
gNB Recover (implementation): In gNB side, channel covariance could be rebuild by , and use the covariance matrix to filter out interference and noise with MMSE/LMMSE channel estimation by implementation.
Overhead analysis: As an example, 64Tx, assuming L=128, and 4 bits for each coefficient (only amplitude), including bits for coefficients position indication in space and frequency domain. then the feedback overhead: 128*4+log2()+ log2()=556 bits for 320ms period or more for each report.
Enh. 1: Long-Term Channel Covariance Assisted SRS Channel Estimation
Proposal 1:
Specify CSI feedback with long term channel covariance to assist SRS channel estimation.
  To address the issue of strong interference on SRS from other TRPs, gNB can use long term channel covariance matrix （） to filter out interference and noise (e.g., using MMSE/LMMSE: ) outside the signal space to assist SRS channel estimation, while the channel covariance matrix is based on DL signal measurement and UE feedback to guarantee the accuracy.
Angle-Delay power
L largest coefficients
index
channel energy
Signal space
Interference + noise
Signal space
Filtered out part
is the DFT matrix for transforming the space-frequency channel to angular delay domain, such as kronecked from vertical, horizontal and frequency (only a subband length) DFT vectors.
Long term channel covariance acquisition:
½ number of Tx
RB number in a subband
UE report: (Spec impacts):
1X
1.26X
Cell Average
Cell Edge
1.55X
1X
R19 with 3 TRPs without RHH reporting
6 TRPs coordination with RHH reporting
Preliminary Simulation results
3.5 GHz
30kHz
7*3 Cell
200m
80% indoor 20% outdoor
20ms
64T,4R
FTP3, 50% RU
1.19X
1.45X
9 TRPs coordination with RHH reporting
The CSI overhead is 200~300bits/20ms for 6 or 9 TRPs, which is less than R18 CJT CSI feedback overhead (500~1000bits/20ms for 3TRPs).
R19 with Single-TRP without RHH reporting
Single-TRP with RHH reporting
1X
Cell Average
Cell Edge
1X
1.11X
1.32X

## Slide 5
For TDD massive MIMO
TDD massive MIMO is the main deployment in 5G/5G-A, where the performance is highly relied on the accuracy of SRS-based channel acquisition. However, in current spec, there are two main challenges for accurate CSI acquisition, especially for cell-edge UEs
  Coverage for SRS, i.e., low SRS SINR of cell edge UE
  Channel measurement accuracy only with extra-polation in SRS hopping
To improve UE experience in cell edge, there are SRS repetition and partial sounding (high power density) can be used in current spec. However, due to the restriction of SRS resource configuration, and extra-polation, the UE experience is still difficult to be improved.
50% Spectrum Efficiency loss
1x
1.1x
1.4x
About 50% SE loss is observed for cell edge user caused by low SINR of SRS
Performance of cell edge users can be improved by repetition of SRS
1x repetition
2x repetitions
8x repetitions
Observation: For TDD Massive MIMO, how to enhance SRS accuracy is the key issue, especially for cell edge UEs.
SRS pre-SINR is low than -10dB in high probability in some areas
Pre-SINR
Spectrum efficiency
The mentioned SRS issues will be more critical in high frequency band, such as 6GHz compared with the case of C-band.

## Slide 6
Only extrapolation for channel estimation could be used with current partial sounding. To enhance the SRS channel estimation accuracy, enabling interpolation for channel estimation in the SRS hopping for partial sounding is needed.
Enable channel interpolation in the Partial Sounding
  Spec impact: define Time continuity and frequency equal-spaced SRS repetition pattern to enable channel interpolation
Current Spec
Proposed Enhancement
For current hopping pattern, only extra-polation for partial SRS can used
Frequency equal-spaced SRS repetition pattern in a hop
Enh. 2-1: SRS Hopping Enhancement to Enable Channel Interpolation
Hopping period
Frequency
Time
SRS is only transmitted in partial bandwidth, e.g., 4 or 6RBs
Frequency
Hopping period
Time
Frequency hop
Proposal 2-1:
Specify SRS hopping pattern within a frequency hop for partial sounding, to enable channel interpolation for SRS
  - e.g., introduce a factor to change the frequency starting position of SRS within a frequency hop in partial sounding
Extra-polation only
1.28x
SRS contiguous sparse hopping
1x
64T4R
7*3 RCE 80ms
1.36x
SRS contiguous sparse hopping
1x
64T4R
7*3 RCE 80ms
Cell average
Cell edge
Time
Assumptions
3.5GHz
200m
80% in, 20% out
64Tx， 4Rx
D:U=4:1
5ms *16 hops
Full buffer

## Slide 7
Enh. 2-2: Cross-slot SRS resource for repetition
One key issue in current deployment is inaccurate channel estimation from SRS for cell edge UE. Generally, SRS is configured in the last two symbols in S slot for TDD system. More contiguous SRS symbols for repetition needs to be supported to improve the SRS channel estimation, i.e., enabling contiguous SRS resource repetition cross S and U slot.
Current Spec
Proposed Enhancement
In current spec, SRS configuration only in last symbols in U slot or occupy the whole U slot.
If SRS symbols for repetition are not contiguous, it will be difficult for SRS aggregation due to the phase/power changing between different slots.
SRS
…
SRS
DMRS
SRS
SRS
S slot
SRS
SRS
U slot
PUSCH (10 symbols)
SRS#0 (2 symbols)
SRS#1 (4 symbols)
//
Cross-slot resource for SRS repetition
SRS
…
SRS
SRS
SRS
SRS
SRS
DMRS
S slot
U slot
PUSCH (10 symbols)
//
Enabling cross-slot (S and U slots) SRS resource repetition configuration:
  Spec impacts: Cross slot SRS resource repetition configuration: enable SRS configuration in the tail of S slot and head of U slot, ensures efficient utilization of uplink resources and avoid phase/power shifting
1x
1.18x
1.3x
2x repetition
4x repetitions
8x repetitions
1.25x
6x repetitions
Assumptions
3.5GHz
ISD=200m
20ms
80% in, 20% out
64Tx， 4Rx
D:U=4:1
Full buffer
Proposal 2-2:
Specify cross-slot (S and U slot) SRS resource, to enable SRS repetition in contiguous symbols in S and U slot

## Slide 8
Views on Closed loop/Open loop Frequency Selective Precoding for PUSCH
12%
27%
8UE * rank=1/UE
SB precoder w/o
quantization loss
SB existing TPMI
UL sub-band precoding based on existing codebook can achieve 8~12% gain
Parameter | Value
Carrier Freq./SCS | 3.5 GHz / 30KHz
Ant. configuration @gNB | 64TRx
Ant. configuration @UE | 4Tx/UE
DMRS | Type 2 DMRS
Bandwidth/PRG size | 96RB / PRG=16RB
MCS | MCS adaptation
Channel model | CDL-B with DS=300ns
Overhead reduction for TPMI indication
Overhead reduction using frequency domain correlation
  Spec impacts: Indicates TPMIs for part of the sub-bands (e.g. only 3 sub-bands).
    PRG size is defined as 16 or 32 RBs
  UE implementation：The TPMIs of remaining sub-bands are recovered with FD interpolation.
sub-band 0
sub-band 1
sub-band 2
sub-band 3
sub-band 4
sub-band 5
TPMI 0
TPMI 2
TPMI 4
gNB: Indicate TPMIs for part of the SBs with equal freq. interval
UE: Calculate the precoders of remaining SBs with FD interpolation
max 13-bits overhead is required
Views:
Closed loop subband precoding is preferred for us since clear performance gain observed. For open loop, at least PRG size is required no less than 16/24 RBs, or restricted as non-coherent precoding.
Closed loop Subband precoding
Open loop Subband precoding
Precoder cycling for open loop subband precoding is proposed, but there are following main issues
Strong interference for NW: Since the precoders are out of NW control, so the precoders in some subbands will be directly pointed to neighboring gNB, which is strong interference for neighboring cells. Shown as UE2 precoders in the following figure.
Complexity of channel estimation: Since PRG is introduced for open loop precoder cycling, the strong interference
for neighboring cells will be per PRG. Small size of PRG means interference will be segmental for neighboring cells, it requires
always small size for channel estimation, otherwise the channel/interference estimation will be a incorrect (i.e., some subband is
no interference, some subband is strong interference in the same channel/interference estimation).
So, large enough PRG, such as 16/24PRG, is required before we agree to introduce the feature.
(Open loop)
(Closed loop)
(Serving cell)
(Strong interference)

## Slide 9
Conclusions
Based on the above discussion, we have the following proposals:
Proposal 1: Specify CSI feedback with long term channel covariance to assist SRS channel estimation
Proposal 2: To enhance SRS coverage and accuracy, specify
  SRS hopping pattern within a frequency hop for partial sounding, (to enable channel interpolation for SRS)
  Cross-slot (S and U slot) SRS resource, (to enable SRS repetition in contiguous symbols in S and U slot)
For Closed loop and Open loop frequency selective precoding for UL, we have following views,
Views: Closed loop subband precoding is preferred for us since clear performance gain observed. For open loop, at least PRG size is required no less than 16/24 RBs, or restricted as non-coherent precoding.