## Slide 1: Rel-20 UE energy savings
Huawei, HiSilicon
3GPP TSG RAN#107 RP-250496
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.10

## Slide 2
It becomes critically essential to expand the implement of Rel-15 UE power savings features in commercial fields, where the following issues are observed
    gNB is conservative to enable BWP switching and UL skipping, due to potential DCI miss detection
    Unnecessary UE power consumption due to inactivity timer extension when UL grant arrives, even though UE has no UL data to transmit
Motivation
UE power savings are critical to devices. For that, there have been many features specified for NR, including
  UE C-DRX (specified in R15): Devices go to sleep without monitoring PDCCH, controlled by an inactivity timer
  Configurable BWP (specified in R15): Devices work on a small BWP when lack of traffic, and can switch via DCI
  UL skipping (specified in R15): UE does not transmit padding PUSCH if no UL data available
  Other features specified in later release(s):
    PDCCH skipping
    dynamic max. MIMO layer adaptation
    etc.
Need for further enhancements
UE energy savings in NR
Notes: 288.8*1/3+288.8*2/3*0.7=231.04
321.48*1/3+321.48*2/3*0.7=257.184

## Slide 3
More opportunities for gNB to enable BWP switching, as well as UL skipping, which could be beneficial to both network and UE energy savings
Remarkable power saving gain could be expected due to power savings on the REs without padding bits
UL skipping enhancements
In order to provide simple confirmation of BWP switching without causing additional overhead and additional timer extension with no data,
    existing UL signal can be assisted information: for BWP switching confirmation and indication of data availability
    UL grant does not trigger Inactivity timer extension if UE has no data: for maintaining the power savings
Benefits
With Padding transmission
DMRS-only transmission
Padding
DMRS
DCI
ON
DCI
ON
OFF
Enhancements
Notes: 288.8*1/3+288.8*2/3*0.7=231.04
321.48*1/3+321.48*2/3*0.7=257.184

## Slide 4
UE has chance to use less antennas (e.g., 2RX) and smaller BW (e.g., same as the CORESET instead of the BWP) to save power, even the BWP is not changed.
Remarkable power saving gain could be expected since UE has more chances to use less antennas and smaller BW
  Based on TR38.840, for FR1 the scaling factor of UE power is
    0.7, for 2Rx compared with 4Rx
    0.4 + 0.6 * (X - 20) / 80, for XMHz compared with 100MHz
Adaptation of antenna/BW for PDCCH reception
In order to enable UE to efficiently use less antennas/smaller BW when there is no traffic, adaptation methods without changing the BWP can be considered
    UE switch between ‘less antennas/smaller BW’ and ‘more antennas/larger BW’ based on BS indication or timer within the same BWP
Benefits
Enhancements
power
power
PDCCH only
PDCCH +PDSCH
Notes: 288.8*1/3+288.8*2/3*0.7=231.04
321.48*1/3+321.48*2/3*0.7=257.184

## Slide 5
Summary
  Specify enhancements to reduce UE power consumption for PDCCH monitoring for UE energy saving in Rel-20
    UL skipping enhancements, including UE assisted information and Inactivity timer enhancements
    Adaptation of antenna/BW for PDCCH reception within active BW, including necessary signaling and timer enhancements
Notes: 288.8*1/3+288.8*2/3*0.7=231.04
321.48*1/3+321.48*2/3*0.7=257.184