## Slide 1
Huawei, HiSilicon, Lenovo
Multi-carrier enhancements for low UE DL complexity
3GPP TSG RAN#107 RP-250497
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.10

## Slide 2
Contents
UL Tx Switching with low DL complexity
Single band single control

## Slide 3
Multi-Carrier UL Tx switching with low DL complexity
Motivation
  Based on CA/SUL features, configuring UE to support Rel-18 UL Tx Switching across 3 or 4 bands mandates UE to support 3 or 4 DL CC
  According to third party statistics [1], under 600$ smartphone occupy around 70% market shares in China of 2024Q3, which mainly support up to 2 DL CC.
  In other words, large amount 2 DL CC UE cannot support Rel-18 UL Tx Switching across 3 or 4 bands.
  In addition to benefits of high UL data rate with low DL capabilities, for a UE supporting 3 or 4 DL CC, implementing MC with low DL complexity will bring additional power saving gain.
50%
[1] Resource from IDC China
  System-level simulation is performed for following cases, assuming UE has 2 DL CC capability. The simulation results show that cell edge users (10%) could reach beyond 50Mbps UPT based on 3CC/4CC UL Tx switching.
  Case1: No Tx Switching, 1CC@sub-3GHz
  Case 2: R17 Tx Switching, 2CC@sub-3GHz
  Case 3: R18 Tx Switching, 2CC@sub-3GHz + 1CC@sub-1GHz
  Case 4: R18 Tx Switching, 2CC@sub-3GHz + 1CC@sub-1GHz + 1CC@sub-6GHz
  * Calculation based on power consumption model in TR38.840
Proposal 1: Introduce enhancements in Rel-20 to enable a UE supporting two DL carriers with UL Tx Switching across 3 or 4 bands for band combination without SUL or with one SUL .

## Slide 4
Multi-Carrier UL Tx switching with low DL complexity
Elaborate on the issues
Inter-band Tx+Rx fast switching
Band A UL
TDD Band B CC#II UL
TDD
Band B CC#I UL
Band A DL
TDD Band B CC#I DL
DL CC#1
DL CC#2
UL CC#1
UL CC#3
UL CC#2
Cell #1
Cell #3
TDD Band B CC#II DL
Cell #2
DL CC#3
Band A UL
TDD Band B CC#II UL
TDD
Band B CC#I UL
Band A DL
TDD Band B CC#I DL
DL CC#1
DL CC#2
UL CC#1
UL CC#3
UL CC#2
Cell #1
Cell #3
TDD Band B CC#II DL
Cell #2
DL CC#3
Fast {Tx+Rx} switching between bands based on RRC pattern or dynamic DCI to implement MC UL Tx switching with low complexity
Sub-pattern 1
Sub-pattern 2
Sub-pattern 1
Sub-pattern 2
Cell #1
Cell #2
Cell #3
  Two DL carrier capability UE switch its DL along with UL Tx switching across 3 or 4 bands, i.e. cell-level switching
    R19 Low-Low band switching can be extended to FDD-TDD or TDD-TDD
    Based on RRC pattern or DCI
    Reuse R19 switching time 35, 140us
  New CA configuration to allow selecting 2 DL+UL pairs out of 3
  New UE capability
  No impact on HARQ timing
TDD Band B CC#II UL
TDD Band B CC#I UL
TDD
Band B CC#I DL
DL CC#2
UL CC#3
UL CC#2
Cell #3
Cell #2
TDD
Band B CC#II DL
DL CC#3
Band A UL
Band A DL
DL CC#1
UL CC#1
Cell #1
  The example band combination is shown above
  Issues:
    It is requires 3DL CCs, which is beyond the 2DL CCs capability, which is the typical capability for low/middle end UEs
No SUL band specified for TDD band B

## Slide 5
Motivation
  In the legacy CA feature, control resources including CORESET, SSB, TRS and CSI-RS are configured per cell, and according to specification, UE needs support self-scheduling, time-frequency synchronization and RRM in each carrier.
  Correspondingly, UE may independently process scheduling, synchronization and RRM in baseband per carrier, which limits the max CC numbers to be supported.
  In 5G-A, network can support 4~5 bands with 4~7 CC, while a typical UE may support 2 or 3 DL CC. The capability for processing PDSCH can be shared across CCs, while processing for control is limited by the maximum CC number for control.
  Thus UE could not fully support the operators’ spectra due to limited control capability, although UE can process total bandwidths of PDSCH on all CCs.
Single DCI
Not required to monitor PDCCH, but UE has to have capability to detect DCI on CC#2.
Single DCI
CC#1
CC#2
  Single DCI and SSB-less are introduced in standards. They can help to reduce the requirement of control signaling reception. However, the self-scheduling CA UE capability is the baseline.
SSB
CC#1
CC#2
TRS
TRS
Not required to receive SSB, but UE has to have capability to measure SSB and do timing synchronization on CC#2
SSB-less
  Single-band-single-control: considering intra-band CA, different carriers can share same BS RF chain in general, and BS can keep time-frequency synchronization between carriers accurately. This provides possibility to configure only one set of control including CORESET, SSB, TRS and CSI-RS for one band, e.g. configure them in one cell, and only requires UE has ability to receive control in one cell on one band
Single DCI
CC#1
CC#2
SSB
TRS
Not required UE has capabilities to monitor PDCCH and receive SSB/TRS/CSI-RS in this carrier.
Example: For a UE supporting 3DL CC + 300MHz, it can support more DL carriers if only one cell in a band is required to process control singling from capability perspective.
Single band single control
Proposal 2: Introduce enhancements in Rel-20 to support single band single control for intra-band CA.
n79
n41
n28
n78
n7
n1
Legacy
Legacy
Single Band Single Control
n79
n41
n28
n78
n7
n1
100MHz
100MHz
60MHz
30MHz
100MHz
100MHz
60MHz
30MHz
90MHz
20MHz
20MHz
30MHz
90MHz
20MHz
20MHz
30MHz
control
data
Single Band Single Control

## Slide 6
Single band single control
Band A CC#1 UL
Band A CC#1 DL
Band A CC#2 DL
Cell #1
Cell #2
Band A
Legacy intra-band CA
Intra-band MC Cell group = Reusing {SSB-less + Single DCI} + New R20 capability
Intra-band multi-carrier Cell group
Band A CC#1 UL
Band A CC#1 DL
Band A CC#2 DL
Cell #1
Cell #2
Band A
Cell group
Reference Cell
Control
Uplink
Downlink
CC# | PDCCH |  |  | PDSCH | Synchronization | 
CC数 | Channel estimation | MMSE-IRC | Blind detection |  | TRS proc | SSB proc
2CC | 2A | 2B | ≈2C | 2X | 2M | 2N
1CC | 1A | 1B | ≈1C | 1X | 1M | 1N
CC number | PDCCH | PDCCH+PDSCH
CC数 | According to TR38.840 | 
2CC | 170 | 510
1CC | 100 | 300
Complexity
Power consumption
  Single band Single control for intra-band CA
    Cell group, which contains multiple cells and always configures
      SSB on one reference cell
      All CORESETs, TRS and RRM measurement on the reference cell
      Note: Reuse the design of SSB-less and single DCI to minimize RAN1 specification impact as much as possible
  Conditional CA configuration/UE capability
    UE capability：UE indicates that support an intra-band CA: {Band A CC#1 + Band A CC#2}, on the condition that BS configures SSB-less and CORESETs confined within one reference cell/carrier
    Conditional CA configuration：Combined the existing SSB-less + single DCI from reference cell/CC + conditional CA UE capability into one feature package
  DCI based SCell/SCC activation/deactivation within the Cell group or single Cell

## Slide 7
Summary of proposals
Proposal 1: Introduce enhancements in Rel-20 to enable a UE supporting two DL carriers with UL Tx Switching across 3 or 4 bands for band combination without SUL or with one SUL .
Proposal 2: Introduce enhancements in Rel-20 to support single band single control for intra-band CA.