## Slide 1
AI/ML air interface for 5G-Advanced in Rel-20
3GPP TSG RAN Meeting #107
Incheon, Korea, March 12-14, 2025
RP-250548
Agenda Item: 15.2.1
Source: ZTE Corporation, Pengcheng Laboratory

## Slide 2: Background
Release 18
  AI Beam prediction and AI positioning enhancements were recommended for normative work
  There is no consensus on the recommendation of CSI prediction for normative work.
  There is no consensus on the recommendation of CSI compression for normative work due to
    1) Trade-off between performance and complexity/overhead;
    2) Issues related to inter-vendor training collaboration.
Release 19
  AI Beam prediction: Both spatial-domain beam prediction and time-domain beam prediction with either UE-side model or NW-side model are under normative work with moderate progress
  AI positioning enhancements: All the five sub cases are under normative work with moderate progress
    First priority: Case 1, Case 3a, Case 3b
    Secondary priority: Case 2a, Case 2b
    Note: It was confirmed that secondary priority cases (case 2a/2b) won’t be discussed in Rel-19 in RAN2
  AI CSI prediction: After the Sept. 2024 checkpoint, AI CSI prediction is escalated to normative work
  AI CSI compression
    In addition to Spatial/Frequency domain CSI compression, RAN1 further investigates the temporal domain use cases
    After the Sept. 2024 checkpoint, AI CSI compression is kept as study item until the end of Rel-19 focusing on the inter-vendor collaboration and specification impact
      Inter-vendor collaboration: Model transfer, dataset transfer, reference model
  AI framework: After the Sept. 2024 checkpoint, AI framework is kept as study item until the end of Rel-19
    Note: RAN1 confirmed that the work in agenda 9.1.4.2 “9.1.4.2 Other aspects of AI/ML model and data” is done and other framework discussion related to CSI compression can be discussed in 9.1.4.1

## Slide 3: General view on Rel-20 AI for air interface
Parallel progress of AI for air interface in Rel-20 5G-A and 6G
  The Rel-20 5G-A AI-PHY normative work will progress simultaneously with Rel-20 6G AI-PHY study
    Rel-20 5G-A AI-PHY normative work
      The study or normative work will focus on use cases that require less impact on 5G-A specification and less impact on existing implementation (targeted for commercialization in the 5G-A Rel-20 timeframe i.e. around 2027-2028).
        CSI feedback enhancements, e.g., CSI compression (Subjective to Rel-19 study outcome), downloadable codebook design
        Other mature AI-PHY use cases, e.g., AI Beam failure prediction, AI Pos prediction etc.
    Rel-20 6G AI-PHY study
      The study will focus on new AI-PHY use cases and enhancements of AI/ML framework
        The 5G-A AI-PHY use cases can be evolved to 6G with necessary updates accordingly
        Prioritize the AI-PHY use cases with promising commercialization prospects in 6G timeframe, e.g., use cases with clear performance gain and controllable complexity

## Slide 4: CSI feedback enhancements: AI CSI compression
Two-sided model: AI CSI compression (2 TU in RAN1) (if sufficient TU is allocated to 5G-A)
  The AI CSI compression may be converted to normative work for Rel-20 5G-A under the following preconditions
    Inter-vendor collaboration issue is well addressed
    Meaningful performance gain is observed
    Specification impact is thoroughly identified
    RAN4 testing framework is verified
  Potential scope of AI CSI compression in Rel-20 5G-A
    Use cases
      Case 0: Spatial/Frequency domain CSI compression
      Case 2: Spatial/Frequency/Time domain CSI compression
      Case 3: CSI prediction plus CSI compression
    Inter-vendor collaboration
      Reference model
      Model transfer
    Specification support
      Data collection, model pairing, performance monitoring, CSI report, etc
    RAN4 testing framework
  Overall progress of the above preconditions: moderate progress has been achieved, but there are still many pending issues
An example of model transfer

## Slide 5: CSI feedback enhancements: AI based codebook design 1/2
AI based codebook design: Reconfigurable/Downloadable codebook (0.5 ~ 1 TU in RAN1)
(an one sided model alternative to two sided model CSI compression)
  AI model is applied to derive one suitable codebook set for the existing cell/environment. Base station configures/downloads the suitable codebook set to the UE and tells UE to apply this codebook set later on.
    Motivation: Codebook download based on UE’s position, interference level, UE speed, computing capability, predicted position/beam (e.g., for UAV), etc.
    Overall procedure
      1st phase: NW generates codebook set that is suitable for the cell/UE based on the collected CSI.
      2nd phase: NW transfers the codebook set that is suitable for the cell and suitable for the UE to the UE. UE generates CSI report based on the received codebook set
    Generated codebook set
        Alt.1: unstructured codebook
        Alt.2: structured codebook subset based on eType II (e.g. via CBSR)
        Alt.3: structured codebook based on AI generated basis vectors (similar to eTypeII)
    Benefits
      Reduced CSI feedback overhead, more accurate CSI feedback, less specification/implementation impact, etc
An example of downloadable codebook

## Slide 6: CSI feedback enhancements: AI based codebook design 2/2
AI based codebook design (0.5~1 TU in RAN1)
  Simulation assumptions
    Single cell with single UE
    Rank1
    Channel model: CDL-C, UMI
  Simulation results
    AI based unstructured codebook provides 5.2% ~ 26.8% SGCS gain in case of CDL-C and UMI scenarios.
    AI based structured codebook provides 5.9% ~ 11.2% SGCS gain in case of CDL-C and UMI scenarios.
Scenario | Codebook size | Benchmark SGCS | AI SGCS | Gain
CDL-C | 1024 | 0.6454 | 0.8182 | 26.8%
 | 8 | 0.6454 | 0.6791 | 5.2%
UMI | 1024 | 0.6221 | 0.7056 | 13.4%
AI based unstructured codebook vs Type I codebook
Scenario | Beam number | Benchmark SGCS | AI SGCS | Gain
CDL-C | 4 | 0.8218 | 0.9144 | 11.2%
UMI | 4 | 0.7957 | 0.8431 | 5.9%
AI based structured codebook vs Type II codebook
Observation: AI based codebook design (including both structured codebook and unstructured codebook) provides comparable performance gain as AI based CSI compression with much smaller implementation/specification complexity.

## Slide 7: One-sided model AI-PHY use case
Consider a subset of the following AI use cases if sufficient TU is allocated (1~2 TU in RAN1)
  AI-based beam failure detection
    Motivation: The temporal beam prediction model can be used to assess the quality of failure detection resources for future time periods, enabling proactive triggering of beam failure event in advance to maintain consistent service quality.
  AI Positioning enhancements: 2nd priority use cases (Case 2a/2b) if they are not finalized in Rel-19
  AI based position prediction
    Motivation: The previous AI based positioning is based on the historic measurement and outputs the historic position. In case of high mobility scenario, the historic position may be outdated.
    Enhancement: The AI model can generate the predicted positioning for future time instances
  Overhead reduction of SRS: Exploit the correlation of different SRS ports or antennas
    For example, if UE has 4 Rx antennas and 1 Tx antenna, previously UE needs to perform 4 antenna switching. With AI prediction, maybe only 2 antenna switching are required
  AI-based traffic prediction
    UE-side prediction: Applying AI/ML technology to predict UL traffic, e.g., to reduce the UL scheduling delay
    NW-side prediction: Applying the AI/ML technology to predict DL traffic, e.g., to reduce the unnecessary PDCCH monitoring power consumption
Note: The use cases marked in grey can be considered in 5G-A if sufficient TU is allocated, otherwise they can be studied in 6G.

## Slide 8: Summary
Proposals
  Proposal 1: AI CSI compression may be converted to normative work for Rel-20 5G-A under the following preconditions (2 TU if sufficient TU is allocated to 5G-A)
    Inter-vendor collaboration issue is well addressed
    Meaningful performance gain is observed
    Specification impact is thoroughly identified
    RAN4 testing frame is verified
  Proposal 2: Consider AI based codebook design (i.e., Reconfigurable/Downloadable codebook) for Rel-20 5G-A (0.5 ~ 1 TU) – (an one-sided model alternative to CSI compression)
    AI based unstructured codebook provides 5.2% ~ 26.8% SGCS gain in case of CDL-C and UMI scenarios.
    AI based structured codebook provides 5.9% ~ 11.2% SGCS gain in case of CDL-C and UMI scenarios.
    AI based codebook design (including both structured codebook and unstructured codebook) provides comparable performance gain as AI based CSI compression with much smaller implementation/specification complexity.
  Proposal 3: Consider a subset of the following AI use cases for Rel-20 5G-A if sufficient TU is allocated (1~2 TU)
    AI-based beam failure detection
    AI Positioning enhancements: 2nd priority use cases (Case 2a/2b) if they are not finalized in Rel-19

## Slide 9: Thank You！