## Slide 1: Views on IoT-NTN in 5G-A Rel-20
RP-250552
3GPP TSG RAN Meeting #107
Incheon, Korea, March 12-14, 2025
Source: ZTE Corporation, Sanechips
Agenda: 15.2.5

## Slide 2: Motivation
  As endorsed in RP-243292, the evolution of IoT-NTN is supported by many companies with the following guidance:
  As an promising way to enable the direct connection between handheld device and satellite, the trial with operator to verify the feasibility and performance has been conducted as shown in: https://www1.10086.cn/aboutus/news/groupnews/index_detail_50179.html;
  Additionally, in Rel-19, for IoT-NTN, the following scope is endorsed in RP-242397 to boost the UL performance of IoT-NTN, which is essential for the deployment, especially in GEO cases.
  However, given the limited TU, it’s failed to align the views on the corresponding solutions, e.g., intra-symbol group, with the following conclusion made in RAN1#120:
Support of Capacity enhancements for uplink Study then specify, if beneficial, enhancements to enable multiplexing of multiple UEs (e.g. up to the min of 4 and the maximum allowed by the existing UL and DL signalling) in a single 3.75 kHz or 15 kHz subcarrier via orthogonal cover codes (OCC) for NPUSCH format 1 and NPRACH [RAN1, RAN2, RAN4]
Conclusion RAN1 did not reach consensus on whether OCC for NPRACH is beneficial or not. RAN1 will not specify support for OCC for NPRACH in Rel-19 IoT NTN.
In our views, the performance gain can be well justified via the simulation results. Given the needs for commercialization of IoT-NTN, the continual enhancement in Rel-20 is preferred.

## Slide 3: Conclusion & Objectives
  Based on the justification before, the following objective can be considered for Rel-20 IoT-NTN enhancement:
  Additionally, for other aspects, especially requiring the changes on the fundamental assumption for 5G-A IoT-NTN, it’s better to preclude it to avoid the market fragement along with complexity for implementation.
  Then, the following proposals are highlighted:
  Proposal 1: Considering the following objective for Rel-20 5G-A IoT-NTN:
  Proposal 2: The enhancement, which is not aligned with the fundamental assumption & framework of 5G-A IoT-NTN,
  should not be included.
Objectives:
  Support for IMS voice calls using GEO satellite access (e,g., ROHC overhead redcution) [RAN2, RAN1].
  Specify the application of intra-symbol group OCC to enhance the capacity of NPRACH [RAN1, RAN2, RAN4]
Objectives:
  Support for IMS voice calls using GEO satellite access (e,g., ROHC overhead redcution) [RAN2, RAN1].
  Specify the application of intra-symbol group OCC to enhance the capacity of NPRACH [RAN1, RAN2, RAN4]

## Slide 4: Thanks