## Slide 1: NR SBFD Phase II in Release-20
KT Corp., China Unicom, Turkcell, Vodafone, CEWiT, ETRI, Fraunhofer HHI, Fraunhofer IIS, Google, Huawei, Hisilicon, IIT Kanpur, NEC, Sharp, Tejas Networks, Wilus, Yonsei University
3GPP TSG RAN Meeting #108
Prague, Czech Republic, June 9-13, 2025
RP-250869
Agenda Item: 15.1.6

## Slide 2: Background and Motivation
Rel-18 SBFD (Study Item)
  Four different SBFD Deployment Cases were defined and studied as in TR 38.858
  Dynamic SBFD was studied and documented in TR 38.858
Rel-19 SBFD (Work Item)
  Deployment case 1 were prioritized
  Deployment case 2 and Deployment case 3 were not prioritized
  Dynamic SBFD was not included
  Intra-subband CLI handling was not optimized
D
D
D
U
U
U
U
D
D
D
D
D
U
D
D
D
U
U
U
U
D
D
D
D
D
U
Deployment case 1: Single operator with same SBFD subband configuration
D
D
D
U
U
U
U
D
U
D
D
D
U
U
U
U
D
D
D
D
D
U
Deployment case 2: Single operator with different SBFD subband configurations
D
D
D
U
D
D
D
D
U
U
U
U
D
D
D
D
D
U
Deployment case 4: Adjacent channel co-existence between TDD and SBFD
Operator A
Operator B
Deployment case 3: Single operator co-channel co-existence between TDD and SBFD
TDD Cell
D
D
D
U
U
U
U
D
D
D
D
D
U
D
D
D
U
D
SBFD Cell(s)
Motivation for Rel-20 SBFD Phase II
  Facilitate practical SBFD deployments (deployment case 3) and accommodate varying DL/UL traffic demands (dynamic SBFD and deployment case 2) via support of dynamic SBFD and intra-subband CLI enhancement

## Slide 3: Outcome of RAN#107
Decisions from the last RAN Plenary
  SBFD was endorsed with limited scope in slide #21 (RP-250040)
  Yet, no TU had been allocated for SBFD
Discussions on SBFD Phase 2 scope (RP-250797)
  DL power reduction(power back-off) seems to have no objection on as specification impact can be kept minimum
  Dynamic SBFD still has a lot of interest, however some concerns on specification impact considering workload
  Intra-subband CLI support also had a lot of interests, however some concerns on specification impact considering workload
Motivation for Rel-20 SBFD Phase II
  Specify subband-level DL power back off including corresponding enhancements in CSI measurement and report
  Specify signaling support of dynamic transition between SBFD symbols and non-SBFD symbols for small cell deployment

## Slide 4: Proposal
Proposal 1: to support a new Rel-20 work item for NR SBFD Phase II
Proposal 2: NR SBFD Phase II includes:
  Specify subband-level downlink power back off including corresponding enhancements in CSI measurement and report [RAN1, RAN4]
    Support frequency-dependent PDSCH EPRE to CSI-RS EPRE ratio for CSI derivation
    Extend gNB RE power control dynamic range as needed
  Specify signaling support of dynamic transition between SBFD symbols and non-SBFD symbols for small cell deployment [RAN1, RAN2]
    Note: the detailed schemes are to be down-selected from those in TR38.858
Proposal 3: Add 0.5 TU for the new Rel-20 NR SBFD Phase II work item