## Slide 1: Views on New RAN WG SI for 6G
3GPP TSG RAN #108
Prague, Czech Republic, June 9-13, 2025
Agenda: 16.2
Source: NVIDIA
RP-250883

## Slide 2: Background
In RAN #107 meeting, the RAN 6G SID “RP-250810” (Study on 6G Scenarios and Requirements) was approved.
The goal of the study item includes developing 3GPP requirements for 6G radio for improvement of existing services as well as enabling new services to ensure substantial gains across all relevant 6G bands.
To achieve significant performance and system gains (including spectral efficiency, energy efficiency, UE experience improvement and TCO reduction), RAN WG(s) should study various aspects of revolutionary 6G technologies that can unleash the true potential of the next generation wireless networks.
In the following slides, we express our views on RAN WG 6G Study Item (SI) during Rel-20.

## Slide 3: RAN WG 6G Study Item Proposal-1
Gigantic MIMO (gMIMO)
Justification
To meet the ever-increasing network capacity demand with 6G, two network dimensions need to scale beyond 5G - 1) Bandwidth and 2) Number of layers.
FR3 band (7.125 GHz – 24.25 GHz: Upper Midband) will be crucial for 6G, offering new spectrum to meet capacity as well as coverage requirements defined by ITU-R for IMT-2030 [1].
Gigantic MIMO (gMIMO) will be one of the most promising technologies for achieving full performance potential of 6G networks in FR3 band, supporting higher rank channels for UEs and promising target KPIs from ITU-R (for example, 200 Gbps peak throughput and 0.5 Gbps user experience throughput as research targets) [2].
There are several aspects of gMIMO operating in FR3 that require 3GPP standardization for its successful commercial deployment in 6G networks.
Objectives
The study on “Gigantic MIMO” for 6G should aim to –
Investigate typical deployment scenarios of gMIMO, including cell-free/distributed MIMO.
Develop near-field compliant channel models and algorithms for gMIMO operating in FR3, including ray-tracing based simulations and machine learning based refinements.
Determine simulation configurations (including attributes such as antenna placement strategy, e.g., distributed antenna sub-arrays and inter sub-array distance, and other relevant antenna form factors) and KPIs for performance evaluation.
Improve the reference signal design to minimize overheads for efficient channel estimation for gMIMO, given shorter coherence time in FR3.
Identify gMIMO beamforming and beam management requirements for achieving both capacity and coverage goals of 6G operating in FR3 as well as various 6G use cases, including-1) enablement of precise beam focusing for interference control, 2) 3D localization, and 3) sensing.
Proposal 1: RAN WG 6G SI should include a study on Gigantic MIMO (gMIMO), with the objectives stated above.

## Slide 4: RAN WG 6G Study Item Proposal- 2
Pilot and Signaling Overhead Reduction
Justification
As the connection density scales in 6G [1], signaling burden as well as pilot overhead will increase linearly (or worse). This would be unsustainable (in terms of spectrum usage and energy consumption) without pilot and/or signaling overhead reduction.
Supporting higher mobility in 6G would require more frequent handover and CSI updates. Similarly, higher frequency bands of operation in 6G (e.g., FR3 and sub-THz) would require more frequent pilot transmission (due to reduced coherence time) as well as more CSIs to estimate (due to potentially more antennas per device). Reducing pilot/CSI overhead is essential to achieve high throughput in these scenarios [3].
Promising 6G technologies such as cell-free/distributed MIMO would require more frequent channel estimates across many “access point (AP)-user (UE)” pairs and complex Tx/Rx coordination, increasing signaling overhead. Smarter signaling strategies will be necessary to reduce latency and fronthaul/backhaul congestion for cell-free/distributed MIMO [4].
Objectives
The study on “Pilot and Signaling Overhead Reduction” should aim to –
Investigate use cases and deployment scenarios, where signaling overhead could become a bottleneck for meeting 6G target capabilities (e.g., high mobility and connection density) or deploying 6G technologies (e.g., gMIMO in FR3).
Study more efficient pilot design for pilot overhead reduction.
Identify light-weight control signaling options (including implicit or opportunistic/event-driven feedback, AI-based signaling/ prediction) for scenarios requiring higher control signaling overhead (e.g., high mobility, FR3).
Develop more efficient beam management techniques (e.g., AI-based predictive beamforming) to reduce overhead from beam sweeping and tracking in high mobility scenarios.
Proposal 2: RAN WG 6G SI should include a study on Pilot and Signaling Overhead Reduction, with the objectives stated above.

## Slide 5: RAN WG 6G Study Item Proposal- 3
ISAC with Multi-modal Sensing
Justification
Integrated Sensing and Communication (ISAC) is one of the usage scenarios for 6G as per IMT 2030 [1].
Multi-modal sensing (i.e., diffusing data from multiple sources, e.g., radar, LiDAR, infrared, camera, RF signal/ sensor, acoustic sensor, Wi-Fi, GPS, thermal imaging) will be crucial for 6G in enabling critical applications like autonomous driving, smart cities, industrial automation, healthcare, military surveillance and security monitoring [5].
Data from various sensing modalities provide complimentary information. Fusing data from these various sources would provide redundancy across multi-modalities to improve [6]-
  Robustness (in adverse conditions like sensor failure/ spoofing),
  Reliability (with improved fault tolerance),
  Context-awareness (with real-time contextual data about the environment and obstacles therein, user activity etc.),
  Accuracy (in object detection/classification/ tracking),
  Security (with cross-validation of sensor data using multi-modality redundancy).
Objectives
The study on “ISAC with Multi-modal Sensing” should aim to –
Investigate use cases and deployment scenarios where multi-modal sensing will be crucial for ISAC in meeting 6G target KPIs as defined by IMT-2030.
Study design aspects for joint sensing and communication including waveforms (e.g., pulse, shape, duration), reference signals (used for both channel estimation and environment sensing), spectrum sharing aspects (including co-existence, spectrum efficiency and interference management), sensing algorithms (including AI/ML-based) and protocols supporting coordinated scheduling and flexible resource allocation (for both communication and sensing).
Determine target scenarios, simulation configurations and performance KPIs for comparing various design options.
Identify requirements for enabling multi-modal data fusion including cross-modal data formats, time stamping/ synchronization, fusion algorithms, methods for real-time sensor data fusion (e.g., using on-device/edge AI-inferencing) and interoperable interfaces for inter-sensor /inter-node data sharing.
Proposal 3: RAN WG 6G SI should include a study on ISAC with Multi-modal Sensing, with the objectives stated above.

## Slide 6: RAN WG 6G Study Item Proposal- 4
AI-native RAN
Justification
Harnessing the power of AI in communication (a.k.a. AI and Communication) is one of the usage scenarios of 6G IMT-2030 [1].
AI-native RAN algorithms for 6G have shown promising results in terms of improved performance (e.g., energy and spectral efficiency), enhanced adaptability (in highly varying and complex environment) and reduced computing complexity in solving highly-complicated (e.g., non-convex) optimization problems [7].
Neural transmitters/receivers/transceivers jointly optimizes Tx and/or Rx components using one-sided/end-to-end deep learning and have demonstrated enhanced robustness against channel impairments (e.g., fading and interference), improved reliability and efficiency in data transmission, better energy utilization and higher spectral efficiency through dynamic and optimized resource allocation and reduced computational complexity [7] [8].
Enabling AI-native RAN would require careful consideration of compute and communication integration in 6G networks.
Objectives
The study on “AI-native RAN” should aim to –
Investigate use cases and deployment scenarios where AI-native RAN will be beneficial (e.g., cell-free massive MIMO, FR3/mmWave/THz bands, highly dynamic environment) across all protocol layers (PHY, MAC, RRC, etc.).
Study additional use cases beyond Rel-19 work item on AI/ML for air interface, including neural constellation shaping, joint source and channel coding (JSCC) and end-to-end neural transceiver.
Identify requirements to enable hybrid and modular RAN (i.e., pluggable traditional and AI-based blocks together), related to interfaces between traditional and AI-based RAN Tx modules, Tx modules input/output and data collection for model training/validation.
Develop evaluation framework including test channel models and performance benchmarks to validate AI-native RAN and analyze trade-offs between AI-based vs non-AI-based RAN.
Determine model LCM requirements (including RRC signaling, fallback protocols and testing criteria for model robustness).
Proposal 4: RAN WG 6G SI should include a study on AI-native RAN, with the objectives stated above.

## Slide 7: RAN WG 6G Study Item Proposal- 5
Multi-RAT Spectrum Sharing (MRSS)
Justification
In ITU-R WRC 23, several mid-band frequency ranges (including 4.4-4.8, 7.125-8.4 and 14.8-15.35 GHz) have been identified for future IMT spectrum allocations, along with harmonization of existing 3GHz band and addition of new bands in upper 6GHz for wireless broadband [9].
6G will be eventually deployed across these bands as well as existing 5G bands and need to co-exist with other RATs (e.g., 4G(LTE), 5G, Wi-Fi). MRSS will be essential in ensuring fair co-existence between these radio access technologies (RATs) as well as flexible and sustainable network evolution from one RAT to another [10].
Integration of terrestrial/non-terrestrial networks (TN/NTN) is one of the key tenets of 6G towards enabling ubiquitous connectivity usage scenario of IMT-2030 [1]. MRSS will be crucial in ensuring efficient and coordinated spectrum usage by networks even when operated by different entities (e.g., mobile versus satellite operators) and dynamic sharing mechanisms aided by AI/ML-based methods to prevent destructive interference between different RATs operating in overlapping bands (e.g., Ka-band (27-40 GHz) and V-band (40-75 GHz)) [11].
Objectives
The study on “Multi-RAT Spectrum Sharing” should aim to –
Investigate MRSS use case scenarios, including coexistence of legacy and new RATs, co-existence of various unlicensed access technologies, sharing between public and private networks and spectrum leasing/sharing models.
Study advanced interference management and mitigation techniques crucial for MRSS, including interference detection and ML-based prediction models, inter-RAT interference coordination (e.g., using coordinated scheduling and nulling).
Develop common spectrum management framework to control/manage shared spectrum access across RATs, enforce policy and regulatory compliances and standardized formats for RATs to facilitate spectrum sensing.
Identify AI/ML integration scopes in MRSS, including cognitive spectrum sharing (i.e., predict/adapt to spectrum availability and interference conditions in real-time).
Establish MRSS KPIs (e.g., coexistence fairness, latency, energy/spectrum efficiency) and reference simulation models.
Proposal 5: RAN WG 6G SI should include a study on Multi-RAT Spectrum Sharing (MRSS), with the objectives stated above.

## Slide 8: RAN WG 6G Study Item Proposal- 6
RAN Digital Twin
Justification
With interactive mapping between the physical network and the virtual twin network, network digital twins can help efficiently and intelligently design, train, simulate, deploy, and manage a live network.
RAN digital twin can be developed as a brand-new autonomous network by digitalizing the physical network. It will have the ability to agilely perceive and adapt to the complex and dynamic environment and achieve network autonomy for its full life cycle in its planning, constructing, monitoring, optimizing, and healing phases [12].
Several aspects need to be considered to realize RAN digital twin.
  Data collection from terminals, BSs, core networks, and network management.
  Physically accurate, deterministic RF propagation channel modeling with 3D ray tracing.
  Interactive virtual-real mapping and control.
  Interfaces between twin layer and physical network layer/network application layer.
Objectives
The study on “RAN Digital Twin” should aim to –
Investigate key use cases and requirements of RAN digital twin, including digital twins of physical radio environment, access network components, and user equipment.
Study RAN digital twin architectural framework and interfaces for interactive virtual-real mapping and control, as well as synthetic data generated for physical AI.
Develop common data framework to serve the need of multiple use cases including RAN digital twin, and support data collection and data generation from various data sources and data exposure to data consumers.
Explore physically-accurate, deterministic, 3D ray tracing-based channel models for RAN digital twin and real-time feedback loop with physical radio access network.
Identify 3GPP specification impact for supporting digital twin RAN and develop interfaces to allow physical AI with digital twins for a real-time network management.
Proposal 6: RAN WG 6G SI should include a study on RAN Digital Twin, with the objectives stated above.

## Slide 9: RAN WG 6G Study Item Proposal- 7
New Coding and Decoding Schemes for 6G
Justification
5G introduced new technologies like millimeter wave and massive MIMO, but many original goals have been deferred to 6G due to the adoption of legacy concepts and architecture in 5G.
Current 5G is built upon an overlay of many quasi-sedimentary layers of successive legacies, from conventional suboptimal modulations, to interleaving over channels, to being limited to a small number of long-and low-rate physical layer codes such as LDPCs, to hybrid ARQ and ARQ repetition at the MAC and PHY layers.
The multiple layers in 5G are too complex, archaic, inefficient and they do not allow for real co-design and optimization necessary to achieve the true transformative 6G wireless network that will serve the world for decades to come.
The approach that allows revisiting these layers opens the door to creating new algorithms and a 6G RAN architecture that will dramatically improve performance. [13-16]
Objectives
The study on “New Coding and Decoding Schemes” should aim to –
Define/study a generalized medium access control layer (GMAC) that uses network coding (NC) to reduce retransmissions (ARQ and HARQ), generalized encoding and decoding/sensing unit (GEU/GDU), generalized interference management unit (GIMU), and generalized transceiver units (GTRxU) to implement optimum modulation with non-uniform constellations while maintaining low overhead, low latency, high reliability, efficient resource utilization, and sustainable processing cost.
Analyze the performance of these generalized units compared to current approaches in 5G.
Explore how the use of Guessing Random Additive Noise Decoding (GRAND) can leverage a converged decoder for control and bearer planes for 6G, as well as energy and spectral efficiencies of using the converged decoder that reduces retransmission and code interleaving currently in use in 5G.
Identify the ways to obtain soft output for a variety of decoders suitable for iterative decoding to open the possibility of codes of varied lengths and rates.
Proposal 7: RAN WG 6G SI should include a study on New Coding and Decoding Schemes, with the objectives stated above.

## Slide 10: RAN WG 6G Study Item Proposal- 8
Zak-Orthogonal Time Frequency Space (Zak-OTFS) Modulation
Justification
Estimating, measuring, tracking and equalizing channels with Doppler spreads/shifts (measured in KHz) can be challenging.
Zak-OTFS modulation provides the robustness in high Doppler and delay spread environments.
Zak-OTFS may support longer detection range, faster tracking rates and better Doppler estimation capability compared to OFDM for sensing applications especially relevant for ISAC.
The channel predictability of Zak-OTFS is the characteristics that improves the performance of ML-based resource allocation algorithms.
Since higher frequencies such as FR3 and FR2 will be used in 6G along with FR1, it is important to look at techniques such as Zak-OTFS in reduced coherence time scenarios.
Since Zak-OTFS offers the predictability of the channel, it is imperative to study the energy saving potential of reduced pilot overhead in 6G.
Objectives
The study on “Zak-OTFS” should aim to –
Define simulation scenarios to benchmark the benefits of Zak-OTFS [17-20].
Compare spectral efficiency of Zak-OTFS modulation with other modulation schemes for the same scenarios.
Study
  The effects of low PAPR with Zak-OTFS especially for RU design and energy consumption related efficiencies.
  The statistics of the channel in the Delay Doppler domain and accordingly define the coherence time and coherence bandwidth of the channel in the Delay Doppler domain.
  Over-the-air implementation and ray tracing of Zak-OTFS.
Conduct specific ISAC use case studies with Zak-OTFS and compare the results.
Proposal 8: RAN WG 6G SI should include a study on Zak-OTFS, with the objectives stated above.

## Slide 11: RAN WG 6G Study Item Proposal- 9
Orthogonal Sequence Division Multiplexing (OSDM)
Justification
The rationale of this study is to evolve a 6G air interface waveform by complementing OFDM with a new waveform to enhance the system performance in all envisaged 6G use cases.
While OFDM (as used in 4G and 5G) has many beneficial attributes, it also exhibits limitations in certain 6G use cases that experience large Delay Doppler (DD) spreads. For example, high-speed terrestrial transport (trains, vehicles), aerial platforms (UAVs), and non-terrestrial networks (satellites).
Orthogonal Sequence Division Multiplexing (OSDM) [21-23] enhances system performance over OFDM in high as well as low DD scenarios using the same resource footprint.
Therefore, the purpose of this study is to evolve a joint OFDM/OSDM waveform from OFDM that meets the requirements of the 6G air interface without increasing implementation complexity.
Objectives
The study on “Orthogonal Sequence Division Multiplexing” should aim to –
Define a joint OFDM/OSDM waveform for the 6G air interface.
Demonstrate the efficacy of the proposed waveform in representative 6G use cases and environments through system performance evaluation in software simulations as well as in hardware emulations.
Simulate BLER performance curves and compare OFDM versus OSDM for representative 6G uses cases and environments, including for ISAC applications.
Validate pilot designs for channel estimation in representative 6G beamforming scenarios.
Evaluate performance of ML-enabled OFDM/OSDM.
Quantify the implementation complexity of the joint OFDM/OSDM waveform.
Study the viability of OFDM/OSDM in the FR1/FR2/FR3 bands.
Proposal 9: RAN WG 6G SI should include a study on OSDM, with the objectives stated above.

## Slide 12: RAN WG 6G Study Item Proposal- 10
Agentic AI based RAN Architecture
Justification
Each generation of wireless networks has introduced increased complexity, resulting in higher operational expenses (OPEX) and total cost of ownership (TCO).
The vision for 6G emphasizes an AI-native design, aiming to embed intelligence directly into the RAN to enhance performance and reduce human intervention.
The advent of GenAI marks a transformative shift, enabling a new “Agentic” architecture where AI agents can plan, reason, and act across distributed RAN workflows.
This study introduces an Agentic AI architecture for RAN that integrates AI such as Large Language Model (LLM)-based agents into the RAN control loop to enhance decision-making, fault detection, and system adaptation [24-30].
The rationale is to enable modular, explainable, and scalable orchestration of AI and RAN workloads through agents that operate across control and orchestration layers.
Objectives
The study on “Agentic AI based RAN Architecture” should aim to –
Study the integration of generative AI and agentic architecture to enhance RAN capabilities. Explore the need for standardization in agentic implementation, focusing on function calling mechanisms, safety and security, architectural understanding, and the deployment of Agentic AI enabled RAN functions. Study the need for standardization of approaches for in-context learning and the use of knowledge graphs to improve reasoning capabilities and performance over time.
Define a reference GenAI-driven agentic architecture for RAN that embeds intelligent agents across control, orchestration, and edge layers.
Develop a multi-agent framework (i.e., a coordination framework for multiple agents) for RAN to operate across RAN layers, enabling distributed cognition, task decomposition, and workload orchestration.
Establish evaluation frameworks with standardized benchmarks and validation procedures to assess agent performance in RAN contexts, focusing on latency, reliability, and traceability.
Proposal 10: RAN WG 6G SI should include a study on Agentic AI based RAN Architecture, with the objectives stated above.

## Slide 13: Summary of Proposals
RAN WG 6G Study Item
Proposal 1:
RAN WG 6G SI should include a study on Gigantic MIMO (gMIMO), with the objectives stated in slide 3.
Proposal 2:
RAN WG 6G SI should include a study on Pilot and Signaling Overhead Reduction, with the objectives stated in slide 4.
Proposal 3:
RAN WG 6G SI should include a study on ISAC with Multi-modal Sensing, with the objectives stated in slide 5.
Proposal 4:
RAN WG 6G SI should include a study on AI-native RAN, with the objectives stated in slide 6.
Proposal 5:
RAN WG 6G SI should include a study on Multi-RAT Spectrum Sharing (MRSS), with the objectives stated in slide 7.
Proposal 6:
RAN WG 6G SI should include a study on RAN Digital Twin, with the objectives stated in slide 8.
Proposal 7:
RAN WG 6G SI should include a study on New Coding and Decoding Schemes for 6G, with the objectives stated in slide 9.
Proposal 8:
RAN WG 6G SI should include a study on Zak-Orthogonal Time Frequency Space (Zak-OTFS) Modulation, with the objectives stated in slide 10.
Proposal 9:
RAN WG 6G SI should include a study on Orthogonal Sequence Division Multiplexing (OSDM), with the objectives stated in slide 11.
Proposal 10:
RAN WG 6G SI should include a study on Agentic AI based RAN Architecture, with the objectives stated in slide 12.

## Slide 14: References (1/3)
[1] Recommendation ITU-R M.2160-0, “Framework and overall objectives of the future development of IMT for 2030 and Beyond”, [online]. Available: https://www.itu.int/dms_pubrec/itu-r/rec/m/R-REC-M.2160-0-202311-I!!PDF-E.pdf, accessed on June 2, 2025.
[2] E. Björnson et. al., “Enabling 6G Performance in the Upper Mid-Band by Transitioning From Massive to Gigantic MIMO”, [online]. Available: arXiv:2407.05630, accessed on June 2, 2025.
[3] J. Park et al., “End-to-End Deep Learning for TDD MIMO Systems in the 6G Upper Midbands”, IEEE Transactions on Wireless Communications, vol., 24, issue 3, pp. 2110-2125, Mar. 2025, DOI: 0.1109/TWC.2024.3516633.
[4] E. Björnson et. al., “Scalable Cell-Free Massive MIMO Systems”, IEEE Transactions on Communications, vol., 68, issue 7, pp. 4247-4261, Jul. 2020, DOI: 10.1109/TCOMM.2020.2987311.
[5] X. Cheng et al., “Intelligent Multi-Modal Sensing-Communication Integration: Synesthesia of Machines”, IEEE Communications and Surveys Tutorials, vol. 26, issue 1, pp. 258-301, Q1’ 24, DOI: 10.1109/COMST.2023.3336917.
[6] B. Lin et. al., “Environment Reconstruction Based on Multi-User Selection and Multi-Modal Fusion in ISAC”, IEEE Transactions on Wireless Communications, vol., 23, issue 10, pp. 15083-15095, Oct. 2024, DOI: 0.1109/TWC.2024.3424849.
[7] N. Ye et al., “Artificial Intelligence for Wireless Physical-Layer Technologies (AI4PHY): A Comprehensive Survey”, IEEE Transactions on Cognitive Communications and Networking, vol. 10, issue 3, pp. 729-755, Jun. 2024, DOI: 10.1109/TCCN.2024.3382973.
[8] S. Cammerer et al., “A Neural Receiver for 5G NR Multi-user MIMO”, IEEE Globecom Workshops 2023, [online]. Available: arXiv:2312.0261, accessed on June 2, 2025.
[9] ITU-R WRC 23, “Final Acts of the World Radiocommunications Conference (WRC-23)”, Dubai, [online]. Available: https://www.itu.int/dms_pub/itu-r/opb/act/R-ACT-WRC.16-2024-PDF-E.pdf, accessed on June 2, 2025.
[10] M. Parvini et al., “A Comprehensive Survey of Spectrum Sharing Schemes from a Standardization and Implementation Perspective”, [online]. Available: arXiv:2203.11125I, accessed on June 2, 2025.
[11] H.-W. Lee et al., “Feasibility and Opportunities of Terrestrial Network and Non-Terrestrial Network Spectrum Sharing”, IEEE Wireless Communications, vol. 30, issue 6, pp. 36-42, Dec. 2023, DOI:10.1109/MWC.001.2300209.
[12] X. Lin et al., “6G Digital Twin Networks: From Theory to Practice,” IEEE Communications Magazine, vol. 61, no. 11, pp. 72-78, Nov. 2023, DOI: 10.1109/MCOM.001.2200830.

## Slide 15: References (2/3)
[13] M. Medrad, “New Coding and Decoding for 6G”, [online]. Available: https://granddecoder.mit.edu/file-share/781531fa-a99d-42a2-bad9-9bac774b7416, accessed on June 2, 2025.
[14] P. Yuan et al., “Soft-Output Successive Cancellation List Decoding”, IEEE Transactions on Information Theory, vol. 71, no. 2, pp. 1007-1017, Feb. 2025, DOI: 10.1109/TIT.2024.3512412.
[15] K. R. Duffy et al., “Ordered Reliability Bits Guessing Random Additive Noise Decoding”, IEEE Transactions on Signal Processing, vol. 70, pp. 4528-4542, Aug. 31, 2022, DOI: 10.1109/TSP.2022.3203251.
[16] B. Ozaydin et al., “GRAND-Assisted Demodulation”, IEEE Journal on Selected Areas in Communications, vol. 43, issue 4, pp. 1200-1213, Apr. 2025, DOI: 10.1109/JSAC.2025.3531555.
[17] N. Mehrotra et al., “Zak-OTFS for Spread Spectrum Communication”, [online]. Available: arXiv:2505.08079, accessed on June 2, 2025.
[18] D. Nisar et al., “Zak-OTFS for Identification of Linear Time-Varying Systems”, [online]. Available: arXiv:2503.18900, accessed on June 2, 2025.
[19] I. A. Khan et al., “Waveform for Next Generation Communication Systems: Comparing Zak-OTFS with OFDM”, [online]. Available: arXiv:2505.13966, accessed on June 2, 2025.
[20] Claire et. al. “Over-the-Air Transmission of Zak-OTFS with Spread Pilots on Sub-THz Communications Testbed”, [online]. Available: arXiv:2504.15947, accessed on June 2, 2025.
[21] S. Henthorn et al., “Direct Antenna Modulation for High-Order Phase Shift Keying”, IEEE Transactions on Antennas and Propagation, vol. 68, issue 1, pp. 111-120, Jan. 2020, DOI: 10.1109/TAP.2019.2935136.
[22] B. A. Kenney et al., “Multi-user Capacity of Cyclic Prefix Direct Sequence Spread Spectrum with Linear Detection and Precoding”, in Proc. 2020 IEEE 92nd Vehicular Technology Conference (VTC2020-Fall), Nov. 18 – Dec. 16, 2020, Victoria, BC, Canada, DOI: 10.1109/VTC2020-Fall49728.2020.9348755.
[23] L. Gehre et al., “CP-DSSS for Radar-Centric Integrated Sensing and Communication”, in Proc. 2023 20th European Radar Conference (EuRAD), Sep. 20-22, 2023, Berlin, Germany, DOI: 10.23919/EuRAD58043.2023.10289259.

## Slide 16: References (3/3)
[24] Z. Nezami et al., “Towards Standardization of GenAI-Driven Agentic Architectures for Radio Access Networks”, [online]. Available: https://drive.google.com/file/d/14M8kxNIgQTgfLSUNL8dR3BZ_mOjxMgOI/view?usp=sharing, accessed on June 2, 2025.
[25] S. D. A. Shah et al., "The Interplay of AI-and-RAN: Dynamic Resource Allocation for Converged 6G Platform”, [online]. Available: arXiv:2503.07420, accessed on June 2, 2025.
[26] Z. Nezami et al., “From Connectivity to Autonomy: The Dawn of Self-Evolving Communication Systems”, [online]. Available: arXiv:2505.23710, accessed on June 2, 2025.
[27] Nokia, “Unlocking the full potential of AI-native 6G through standards”, [online]. Available: https://www.nokia.com/6g/unlocking-the-full-potential-of-ai-native-6g-through-standards/, accessed on June 2, 2025.
[28] Felipe A. Rodriguez Y., “Technical Language Processing for Telecommunications Specifications”, [online]. Available: arXiv:2406.02325, accessed on June 2, 2025.
[29] J. Kim et al., “Persona is a Double-edged Sword: Mitigating the Negative Impact of Role-playing Prompts in Zero-shot Reasoning Tasks”, [online]. Available: arXiv:2408.08631, accessed on June 2, 2025.
[30] T. R. Sumers et al., “Cognitive Architectures for Language Agents”, [online]. Available: arXiv:2309.02427, accessed on June 2, 2025.